## Slide 1: Reliable Dual Sub-Carrier Modulations (DCM) for HE-SIG-B and Data
Date: 2015-09-12
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun (Rossi) Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Andrew Blanksby |  |  |  | 
Matthias Korb |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 5
Authors (continued):
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Bo Yu |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 6: Authors (continued)
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Name | Affiliation | Address | Phone | Email
Hyeyoung Choi | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hy0117.choi@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Authors (continued)
Kazuyuki Sakoda | Sony Electronics |  |  | Kazuyuki.Sakoda@am.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Eisuke Sakai |  |  |  | Eisuke.Sakai@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Masahito Mori |  |  |  | Masahito.Mori@jp.sony.com

## Slide 9
HE-SIG-B and Data
HE-SIG-B
  Performance of HE-SIG-B is encoded using 1x symbol duration. So its performance is worse than data symbol with 4x symbol duration when used the same MCS.
  Under dense deployment, robustness with narrow-band interferences is also important to HE WLAN
HE-Data
  Enhance the PER performance of Data portion can extend range for outdoor scenarios
  Under dense deployment, robustness with narrow-band interferences is also important to HE WLAN

## Slide 10: Robustness to interferences
Jianhan Liu, Mediatek, et al
Narrow band interferences
  In 11ax, a STA can transmit one RU (about 2 MHz bandwidth) in Uplink OFDMA.
  Compared to its 20MHz preamble, the power density of its data portion is 9dB higher than its preamble.
  Therefore one STA can experience 9dB higher interferences on subcarriers in a particular narrow band than other subcarriers.
  DCM is a perfect solution to deal with such narrow band interferences.
    Note that narrow band interferences are intrinsic in 11ax.

## Slide 11: Introduce Dual Sub-carrier Modulation
Jianhan Liu, Mediatek, et al
Dual Sub-carrier Modulation (DCM) modulates the same information on a pair of sub-carrier n and sub-carrier m.
  Subcarrier n and sub-carrier m are typically separated far apart in frequency.
Pros
  Data rate can be kept same as modulations used in IEEE 802.11ac.
  Diversity gain can be obtained by using DCM.
  More robust when sub-band interferences are present.
  Significant improvement on PER for the same data rate
    Range extension
    Better user experiences

## Slide 12: Dual Sub-carrier Modulation
Jianhan Liu, Mediatek, et al
The encoding (TX side) and decoding (RX side) of DCM is really simple
  TX: just change the modulation with another mapping
  RX: just simple calculations to combine the LLR
    For example, for QPSK DCM:TX just mapping 2 bits with QPSK and Rotated QPSK; RX just add two LLRs
11n Bit interleaver
DCM
IFFT
Subcarrier K
Subcarrier K+N/2
Modulation Mapping 1
Modulation Mapping 2

## Slide 13: Dual Sub-carrier Modulation Mappings
Jianhan Liu, Mediatek, et al
For BPSK
  and can be obtained by mapping 1 encoded bit using BPSK and SBPSK respectively.
For QPSK
  and can be modulated by mapping 2 encoded bits using QPSK and SQPSK (or other rotated QPSK schemes) respectively.
For 16 QAM
Applying Sub-carrier Modulation to modulations higher than 16QAM should not be supported
  Dual Sub-carrier Modulation may reduce data rate for higher modulation to achieve higher performance.
where
and

## Slide 14: DCM Indication Schemes
In HE-SIGA, we introduce 1-bit DCM indication as follows.
The indication of DCM for payload in MU format is TBD.
DCM bit in HE-SIGA | HE-SIG-B MCS Indication in HE-SIG-A | HE-SIG-B Modulation Schemes
1 | x | MCS x with DCM
0 | x | MCS x
DCM bit in HE-SIGA | MCS of Payload Indication in HE-SIG-A | Modulation Schemes of Payload
1 | x | MCS x with DCM
0 | x | MCS x
For SU, DCM bit indicates the modulation of payload
For SU, DCM bit indicates the modulation of HE-SIGB

## Slide 15: Simulation Settings for Data
Channels: Channel type D and UMi channel
4x Symbol
1.6us CP
Packet length: 2048 bytes
Time domain simulation
  Real channel estimation
  With CPE tracking

## Slide 16: UMi NLOS Channel (4x symbol length, BCC)
Performance Gain:
  1.5dB gain for MCS0 and MCS2 at 1% PER
  Error floor is also reduced
It also says:
  Gain is also significant for 4x symbol.
  The payload in this simulation is just one 4x OFDM symbol.

## Slide 17: Simulations with Narrowband Interferences
  Setting: Narrowband interference that is 9dB higher than noise floor on one 26 tone RU.
Performance Gain:
  4dB gain for MCS0 at 1% PER
  2dB gain for MCS2 at 1% PER
  Even for MCS 1, there is about 0.6dB Gain
  Error floor is also reduced
It also says:
  When there is narrow band OBSS interferences, DCM provide a huge gain.

## Slide 18: Performance of DCM for LDPC
4x symbol length, 1.6us CP, 256 bytes packet, LDPC under UMi NLOS Channel model
For MCS 0 with DCM:
  Around 1.7dB gain at 1% PER;
  Around 1dB gain at 10% PER;
  Error floor reduced.
For MCS 1 with DCM:
  Around 0.7dB gain at 10% PER;
  Error floor is similar.
For MCS 2 with DCM:
  Around 1dB gain at 10% PER;
  Error floor is reduced.

## Slide 19: Simulations with Narrowband Interferences for LDPC
With interference 10 dB higher than noise on one 26 tone RU.
Performance Gain:
  4dB gain for MCS0 at 1% PER
  2dB gain for MCS2 at 1% PER
  Even for MCS 1, there is about 0.5dB Gain

## Slide 20: Simulation Settings for HE-SIG-B
1x symbol length
Assume 24-byte information bits for HE-SIG-B
Channels: UMi channel
0.8us CP
Time domain simulation
  With real channel estimation
  With CPE tracking

## Slide 21: UMi NLOS Channel (1x symbol length)
Performance Gain
  About 0.7dB gain over the same rate MCS
  Error floor is also reduced

## Slide 22: UMi NLOS Channel (1x symbol length) with perfect channel estimation
It also says:
  If we can improve the channel estimation, the gain can be much larger.
  Note that we indeed can improve the channel estimation by using RL-SIG.
Performance Gain
  1.7dB gain over BPSK, ½ rate code at 1% PER
  2dB gain and error floor significantly reduced for QPSK, ¾ rate code

## Slide 23: Advantages of using Dual sub-carrier modulation
No change for 11n/ac bit interleaver and other TX and RX blocks.
No latency added. (Modulation within one OFDM symbol)
Negligible complexity at modulator and demodulator
  For modulator, just modulate the subcarriers in the upper band and the subcarriers in lower band the similar way.
  For demodulator, LLR calculation just needs the combination of two subcarriers
  PER performance improved more than 2dB gain for MCS0 and MCS 2 in 4x symbol.
  The performance gain is significant. (Note LDPC just bring 1.5dB to 2dB gain over BCC.)
  Error floor is reduced for outdoor channels.
  More robustness to sub-band interferences.
  Provide a very good data rate vs. PER tradeoff between QPSK ½ rate code and 16QAM ½ rate code.

## Slide 24: Straw Poll #1
Do you agree to add dual sub-carrier modulations (DCM) as optional modulation schemes for HE-SIGB and Payload to 11ax SFD?
  Dual sub-carrier modulation (DCM) are only applied to BPSK, QPSK and 16QAM modulations.
  Y
  N
  A

## Slide 25: Straw Poll # 2
Do you agree to add one bit DCM indication in HE-SIGA to 11ax SFD?
  Y
  N
  A