## Slide 1: Further consideration on receive behavior based on the cascading structure and the BSS color scheme
Date: 2015-09-15
Authors:

## Slide 2: Abstract
The receive behavior of DSC/CCAC technique using BSS color is discussed and proved that termination of receive process improves the system throughput [1].
In this contribution, the further consideration on receive behavior based on the cascading structure [2] and the BSS color scheme is discussed.

## Slide 3: Background (1)
The receive behavior of the DSC/CCAC technique using the BSS color is discussed in [1]
STA/APs are suggested the following receive process when they detect
the preamble
  Step 1: Evaluate whether the BSS color contained in the preamble matches with the color of the BSS which the receiver is associated with.
  Step 2-1: If matched, continue decoding.
  Step 2-2: If not matched, the receiver stops the receiving process and wait for the next signal no matter what the channel status (BUSY/IDLE) is.

## Slide 4: Background (2)
Original BSS color scheme in 11ah[4]
  Place color bits and UL/DL indication in the PHY SIG field for assisting in identifying the BSS of frames.
    DOWN DIRECTION:
      1 UL/DL indication bit is used to determine definition of remaining 9 bits
      3 color bits selected by AP to avoid overlap with neighbor APs are used to identify BSS
      6 PAID bits
    UP DIRECTION:
      1 UL/DL indication bit, e.g. UP vs DOWN
      9 PBSSID bits
Bits:
1
9
DIR=down
Color
ID=PAID
Bits:
1
3
6
DIR=up
ID=PBSSID
We note that the UL/DL indication bit included in a frame implies the ongoing UL/DL transmission situation of its own BSS.

## Slide 5: Background (1)
The cascading structure is proposed [2] and has been approved in the SFD[3].
DL MU PPDU
UL MU PPDU
t
DL MU BA
DL MU PPDU
UL MU PPDU
…
TXOP
Cascading structures:
Considering the cascading structure, we suggest that UL/DL indication bit may help an AP to schedule its own traffic considering the neighboring BSS traffic. This has the benefit of mitigating the potential inter BSS collision in 11ax.

## Slide 6: Further consideration on receive behavior based on the cascading structure and the BSS color scheme
STAs terminate the receive process referring to BSS color as discussed in [1].
APs not only terminate the receive process referring to the BSS color but also properly schedule intra-BSS UL/DL traffic referring to the UL/DL indication bit of frames received from a neighboring BSS.
The compound process of terminating receiving and checking the UL/DL indication bit is hereafter denoted as neighboring UL/DL indication check.
Assuming that the cascading structure and the BSS color bit (already includes the UL/DL indication) are used

## Slide 7
Neighboring UL/DL indication check in an AP
Further consideration on receive behavior based on the cascading structure and the BSS color scheme

## Slide 8
Example case study
  Collision situation in OBSS scenario without AP’s neighboring UL/DL indication check
…
AP1
AP2
t
STA12
PHY header (color bits)
UL MU PSDU
Collision!
…
…
…
TXOP
…
STA22
…
PHY header (color bits)
UL MU PSDU
Further consideration on receive behavior based on the cascading structure and the BSS color scheme
AP2
AP1
STA 21
STA 11
STA 12
STA 22
…
PHY header (color bits)
Collision!
…

## Slide 9
Example case study
  Collision free & better spatial reuse situation in OBSS scenario with AP’s neighboring UL/DL indication check
…
AP1
AP2
t
STA12
PHY header (UL indication and color bits )
UL MU PSDU
…
…
…
TXOP
…
STA22
…
PHY header (DL indication and color bits )
DL MU PSDU
Further consideration on receive behavior based on the cascading structure and the BSS color scheme
…
PHY header (DL indication and color bits )
AP2
AP1
STA 21
STA 11
STA 12
STA 22
STA12 isn’t interfered by signals of AP2 since it is transmitting
Communications of these two neighboring BSSs could be conducted simultaneously without collisions

## Slide 10: Conclusions and future works
Further consideration on receive behavior based on the cascading structure and the BSS color was discussed.
  STAs terminate the receive process referring to BSS color as discussed in [1].
  APs not only terminate receive process by referring to BSS color but also schedule intra-BSS DL/UL transmission by referring to the UL/DL indication bit of the receiving frame transmitted from the neighboring BSS.
In future, further discussion and simulation performance of the receive behavior based on the cascading structure and the BSS color should be conducted.

## Slide 11: References
[1] Yasuhiko Inoue,”discussion-on-the-receiver-behavior-for-ccac-dsc-with-bss-color”, IEEE 802.11-15/0595r2.
[2] David Xun Yang, “cascading structure”, IEEE 802.11-15/0841r1
[3] “SPEC framework”, IEEE 802.11-15/0132r7
[4] Matthew Fischer, “CID 205 BSSID Color Bit,” doc.: IEEE 802.11-13/1207r1