## Slide 1: MU BFee Interference channel feedback
Date: 2015-09-14
Authors:

## Slide 2: Problem statement
MU-MIMO and TxBF precoding are based on channel information obtained during sounding
  Snapshot in time
The natural variability of the wireless channel causes the channel information and hence the precoding matrices to “age”
  Loss of BF gain over time in changing channel
  Loss of interference cancellation over time in changing channel
Channel information and precoding matrices need to be “refreshed” at an appropriate rate to keep up with the changes

## Slide 3: Sounding
Updating channel information implies overhead
  Protocol overhead from sounding and sounding feedback
Resources should be managed carefully
  Excessive sounding wastes channel capacity without benefit
  Too few soundings degrade performance, especially for MU-MIMO
MU-MIMO needs more frequent updates than BF
  Depends on environment and can change over time
How to find the right sounding frequency?
  Too frequent sounding increases overhead
  Too infrequent sounding increases interference

## Slide 4: Illustration: Effect of changing channel on SINR
A single-tone matrix model for changing channel
  Choose two independent channel matrix realizations
  Perform precoding based on the initial channel values
  “Morph” the channel from its initial value to the other realization
  E.g.: 1x4 channel (H1, H2, H3, H4)

## Slide 5: SINR calculation
For channels and precoding matrices :
  Evaluate SINR:
  With:
We compare to an “ideal” reference where precoding matrices are up to date with latest channel information
  Equivalent to sounding right before the transmission of the packet

## Slide 6: 1. No re-sounding
4x4 AP, three 1x1 users
Dramatic loss in SINR over time

## Slide 7: 2. Re-sounding with fixed interval
100 msec sounding interval
SINR restored after each sounding, gradually degrading between soundings

## Slide 8: 3. Re-sounding based on max SINR degradation
Sounding triggered by 3dB SINR degradation
Frequent resounding needed to limit SINR degradation within desired bounds

## Slide 9: How to optimize sounding overhead?
Sounding frequency is important to maintain MU interference cancellation
  Should be adaptive depending on channel behavior
  Rate adaptation alone can not distinguish between effects of interference and other effects
  The AP (or BFer in general) can implement adaptive behavior if it is provided with some information about effectiveness of its current precoding

## Slide 10: What information can the STA provide?
Using the MU preamble, the STA (MU BFee) can estimate the channel between its Rx antennas and every stream in the MU packet
  Including streams for other users (“interference channels”)
  With ZF precoding, interference channels are expected to be zero
  However, this will change as the precoding matrices age
  The value of the interference channels is a measure of the effective quality of the precoding used at the transmitter

## Slide 11: Illustration: MU channel estimation in changing channel
MU to two STAs
  NSTS,total = 4
  NSTS = (2,2)
Initially, channel for two streams is “just noise”
As channel changes, loss of precoding is seen on the interference channels
Channel from all four streams to first antenna

## Slide 12: What information can the STA provide?
The STA has direct information that can be used by the BFer to perform more optimal sounding
  But it’s not sharing …
The receiver directly sees :
Feeding back information about the interference channels gives the BFer a direct view of the effectiveness of it current MU precoding

## Slide 13: Proposal
Proposal: feed back some measure of (for ) from receiver to the MU BFer
Information can take many forms:
  Full information
  Magnitude
  Relative magnitude (signal to interference)
  “Threshold exceeded” indication
MU BFer can use that information to guide sounding decisions
  Precise algorithm outside the scope of the standard

## Slide 14: Keep overhead low
Information can be quantized in low # bits
  We expect small values
Information can be provided on a subset of tones or as an average
  We don’t expect huge tone-to-tone variations
Information can possibly be piggy-backed on the regular ACK frame
  Data frame will be followed by ACK anyway (mostly …)
  This avoids separate exchange

## Slide 15: Summary
MU needs frequent sounding to maintain precoding
  Optimal sounding frequency is function of environment
  Sounding implies overhead
STAs (MU BFees) have information of the effectiveness of precoding
  From observing the “interference channels”
Feedback from the MU BFee allows BFer to make more informed decision on sounding
  Reducing protocol sounding overhead
Let’s provide a mechanism to enable interference channel measurement from BFee to BFer

## Slide 16: Straw Poll
Do you agree to add the following to the IEEE 802.11 TGax Specification Framework?
  11ax shall define a mechanism to enable MU BFees to provide the MU BFer with feedback information on the interference channel estimates determined at the receiver
  Note: “interference channel estimate” means the channel estimate for a stream that is present in an MU transmission but that is not intended for the MU BFee itself.