## Slide 1: Recovery Procedures in Cascading Sequences
Date: 2015-09-14
Authors:
Name | Affiliations | Address | Phone | email
John (Ju-Hyung) Son | WILUS | 263-2 Yangjae-dong, Seocho-gu, Seoul, Korea | +82-2-552-0110 | john.son@wilusgroup.com
Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
Minseok Noh |  |  |  | minseok.noh@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com

## Slide 2: Introduction
In 11ax SFD [1], the cascading sequence is defined as follows
  A TXOP can include both DL MU and UL MU transmissions.
  The spec shall include the definition of a cascading TXOP structure, allowing alternating DL and UL MU PPDUs starting with a DL MU PPDU in the same TXOP
    The TXOP sequence has only one DL transmitter
    The TXOP sequence may have different UL transmitters within each UL MU PPDU
    The TXOP sequence may have a different set of transmitters in an UL MU PPDU as compared to the DL MU PPDU that follows the UL MU PPDU within the same TXOP
  DL/UL OFDMA (MU-MIMO) can multiplex different types of unicast frames in frequency (spatial) domain. Types of frames can be data frame/control frame/management frame.
  A unicast Trigger frame for a single user may be included in an AMPDU for that user in the DL MU PPDU that precedes the UL MU transmission by TBD IFS.
In this document, we analyze cases of control MPDU delivery failures in cascading sequences, and discuss possible recovery procedures. Also we propose several options for enhancing robustness of control MPDU in A-MPDU.
DL MU PPDU
Trigger
Example of Cascading Sequences
UL MU PPDU
DL Data to STA2
Trigger
DL Data to STA1
BA
UL Data from STA2
BA
UL Data from STA1
DL MU PPDU
Trigger
DL Data to STA2
Trigger
DL Data to STA1
BA
BA
. . .

## Slide 3: Robustness of Control MPDU
Within MU PPDU in cascading sequences, A-MPDU to a certain STA can be transmitted where Data MPDUs and Control MPDU(s) are aggregated
In A-MPDU, each MPDU’s MCS level should be the same
By using the same high MCS level chosen for data MPDUs, control MPDUs are more susceptible to interferences when receiving at STA
The delivery failure of control MPDU incurs resource wastes in the following sequence. Therefore we need to develop efficient recovery procedures that can minimize any further resource wastes in the cascading sequence.
High MCS
Unicast Trigger
DL Data MPDU
Trigger
M-STA
BA
DL Data MPDU
BA
High MCS
May utilize Robust MCS
Standalone UL MU Sequence
Cascading-based MU Sequence
UL Data MPDU
UL Data MPDU
UL Data MPDU
UL Data MPDU
Unicast Trigger
Data MPDU
DL Data MPDU
BA
UL Data MPDU
UL Data MPDU
BA
High MCS
UL Data MPDU
UL Data MPDU
BA
Cannot utilize Robust MCS

## Slide 4: Delivery failure of Unicast Trigger MPDU
DL MU PPDU
Trigger
UL MU PPDU
DL Data (STA2)
Trigger
DL Data (STA1)
UL Data (STA2)
BA
Recovery Sequence ?
DL Unicast Trigger MPDU was not correctly received at STA1
  STA1, without Trigger’s resource allocation,
    cannot send UL Data in the following PPDU
    cannot send UL BlockAck for the previous DL Data in the following PPDU.
  AP, without UL transmission from STA1 in the following PPDU,
    assume that either Trigger frame was not successfully delivered to STA1 or STA1’s UL transmission was totally failed to be received at AP
    is not clear whether the DL Data delivery was also failed
  Therefore, AP needs efficient recovery sequence in the following DL MU PPDU
corrupted
UL Data (STA1)
BA
UL MU PPDU

## Slide 5: Possible Recovery Procedures
(Opt-1) AP transmits BAR to check the status of the previous Data MPDUs
  When AP does not have queued DL data to the STA1 and STA2
  AP should set BAR’s SSN(Starting Sequence Number) to the SN of the previous data MPDUs
(Opt-2) AP retransmits the previous MPDUs to the STA
  When AP does not have queued DL data to the STA1, but have queued DL data to the STA2
(Opt-3) AP transmits additional Data MPDUs along with BAR
  When AP have queued DL data to the STA1 and STA2
  AP should set BAR’s SSN(Starting Sequence Number) to the SN of the previous data MPDUs
DL MU
Trigger
UL MU
DL Data (STA2)
Trigger
Data 1
(STA1)
UL Data (STA2)
BA
DL MU
Trigger
UL MU
DL Data (STA2)
Trigger
UL Data (STA2)
BA
DL MU
UL MU
UL Data (STA2)
UL Data (STA1)
(Option 2)
Data MPDU Retransmission
(Option 3)
New Data MPDU +BAR
Data 2
(STA1)
Data 3
(STA1)
BA
BA
(SSN=1)
BA
DL Data (STA2)
Data 1
(STA1)
Data 2
(STA1)
Data 3
(STA1)
Data 4
(STA1)
Data 5
(STA1)
BAR
(SSN=1)
DL MU
UL MU
UL Data (STA2)
UL Data (STA1)
BA
BA
(SSN=1)
BA
DL Data (STA2)
Data 1
(STA1)
Data 2
(STA1)
Data 3
(STA1)
Trigger
Trigger
Trigger
DL MU
Trigger
UL MU
DL Data (STA2)
Trigger
Data 1
(STA1)
UL Data (STA2)
BA
(Option 1)
BAR
Data 2
(STA1)
Data 3
(STA1)
DL MU
UL MU
UL Data (STA2)
UL Data (STA1)
BA
(SSN=1)
Trigger
BAR
(SSN=1)
Trigger
BA
Trigger
UL Data (STA1)
BA
UL Data (STA1)
BA
UL Data (STA1)
BA
BA

## Slide 6: MPDU contents and positions in A-MPDU
Current A-MPDU Contents definitions in IEEE 802.11-2012 [6].
  HT-immediate BlockAck
    If the preceding PPDU contains an implicit or explicit block ack request for a TID for which an HT-immediate block ack agreement exists, at most one BlockAck frame for this TID, in which case it occurs at the start of the A-MPDU.
  Data MPDUs sent under an HT-immediate Block Ack agreement
    QoS Data MPDUs with the same TID, which corresponds to an HT-immediate Block Ack agreement.
    These MPDUs all have the Ack Policy field equal to the same value, which is either Implicit Block Ack Request or Block Ack.
  Immediate BlockAck Req
    At most one BlockAckReq frame with a TID that corresponds to an HT- immediate block ack agreement. This is the last MPDU in the A-MPDU.
    It is not present if any QoS Data frames for that TID are present.
For the newly defined cascading sequences, 11ax needs to revise the current A-MPDU contents definitions such as
  Addition of Trigger MPDU content
  Assigning positions of control MPDUs in A-MPDU
  Allow transmission of BAR along with QoS Data frames

## Slide 7: Enhancing Robustness of Control MPDU
Even with the previous recovery procedures, the delivery failure of control MPDU already have incurred resource wastes and additional message exchanges.
Therefore, we also should develop proactive methods which can enhance robustness of control MPDUs in A-MPDU.
Assigning relatively robust positions to Control MPDUs in A-MPDU
  In 802.11-2012, the positions of BA and BAR MPDUs within A-MPDU are defined to be the first and the last MPDU [6]
  In 11ax, the position of Trigger MPDU within A-MPDU should also be newly defined
  In our measurement study [5], it seems that the latter MPDUs have higher error ratio
  Placing control MPDUs in the front part of A-MPDU, closer to PHY preamble, may improve control MPDU delivery ratio
Repetition of Control MPDU in A-MPDU
  Replicating a control MPDU into multiple positions within A-MPDU for robustness
  There is tradeoff between robustness and efficiency, but control MPDUs are usually small in sizes
Applying Robust MCS to Control MPDU in A-MPDU
  Currently, applying different MCS level for each user within MU PPDU is possible
  We should develop possible methods to apply robust MCS on a control MPDUs

## Slide 8: Summary
Under cascading sequence allowing aggregation of Control MPDUs with Data MPDUs, the high MCS level selected for Data MPDUs may incur delivery failure of Control MPDUs.
Based on data queue status of AP, it can choose one of the recovery procedures such as:
  Transmitting a BAR
  Retransmitting unacknowledged Data MPDUs
  Transmitting one or more new Data MPDUs along with a BAR
Also, in order to maximize advantage of cascading sequences, 11ax also should provide proactive methods that can enhance robustness of control MPDU in A-MPDU such as:
  Assigning relatively robust positions to Control MPDUs in A-MPDU
  Repetition of Control MPDU in A-MPDU
  Applying robust MCS to Control MPDU in A-MPDU

## Slide 9: References
[1] 11-15-0132r7, “Specification Framework for TGax”
[2] 11-15-0831r2, “Broadcast and Unicast in DL MU”
[3] 11-15-0841r1, “Cascading structure”
[4] 11-15-0829r2, “Uplink Ack and BA multiplexing”
[5] 11-14-1181r1, “Measurements on A-MPDU performances under various channel conditions”
[6] Table 8-284 –A-MPDU contents in the data enabled immediate response contexts, IEEE 802.11-2012.

## Slide 10: Straw poll - 1
  Do you agree to add the following text into 11ax SFD ?
  4.1 In cascading sequence, when AP does not receive acknowledgements from a STA after sending DL Data MPDUs, AP may recover using one of the following procedures:
    Transmitting a BAR with SSN value set to the SN of the unacknowledged Data MPDUs
    Retransmitting unacknowledged Data MPDUs
    Transmitting additional Data MPDUs along with a BAR with SSN value set to the SN of the unacknowledged Data MPDUs
  Y
  N
  A

## Slide 11: Straw poll - 2
  For robustness enhancements of control MPDUs in A-MPDU, which options do you prefer ?
  Assigning relatively robust positions to Control MPDUs in A-MPDU
  Repetition of Control MPDU in A-MPDU
  Applying robust MCS to Control MPDU in A-MPDU