## Slide 1: Reducing Channel Sounding Protocol Overhead for 11ax
Date: 2015-09-14
Authors:

## Slide 2: Background
802.11ax is envisaged to improve efficiency by introducing innovative technologies
  Multiplexing of BA/ACK responses from STAs to data transmission.
The TGax Spec Framework Document (SFD)[1] includes BA/ACK multiplexing;
  The amendment shall include a mechanism to multiplex BA/ACK responses to DL MU transmission. [MU Motion #4, March 2015]
The TGax SFD also includes MU modes for both UL and DL;
  MU features include UL and DL OFDMA and UL and DL MU-MIMO.
Multiplexing of responses from multiple STAs, to data transmission from AP, improves efficiency and reduces overhead
  More overhead reduction as the number of STAs increase
11ac Sounding protocol can be improved by applying similar techniques

## Slide 3: 11ac Sounding Protocol
DL-MU-MIMO relies on channel state information (CSI) obtained during sounding for pre-coding
Protocol overhead from sounding and CSI feedback
  MU-MIMO needs frequent updates of CSI
  Overhead increase with number of STAs
How to reduce the overhead incurred in sounding protocol for 11ax?
  Compressed beamforming frames (response to NDPA/NDP) from the STAs can be multiplexed using UL MU-MIMO/UL OFDMA
VHT NDPA
NDP
VHT Compressed Beamforming
Beamforming Report Poll
VHT Compressed Beamforming
Beamforming Report Poll
VHT Compressed Beamforming
AP
STA 1
STA 2
STA 3
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
DIFS & Backoff

## Slide 4: HE Sounding protocol
VHT NDPA
NDP
VHT Compressed Beamforming
Beamforming Report Poll
VHT Compressed Beamforming
Beamforming Report Poll
VHT Compressed Beamforming
Beamforming Report Poll
AP
STA 1
STA 2
STA 3
SIFS
SIFS
SIFS
SIFS
SIFS
DIFS & Backoff
SIFS
SIFS
SIFS
VHT Compressed Beamforming
STA 4
HE NDPA
NDP
HE Compressed Beamforming
HE Compressed Beamforming
HE Compressed Beamforming
HE Compressed Beamforming
AP
STA 1
STA 2
STA 3
SIFS
SIFS
DIFS & Backoff
STA 4
HE compressed beamforming frame can simultaneously be sent by the STAs [2]
  Reduces overhead associated with obtaining CSI feedback
To enable UL multiplexing for HE compressed beamforming, HE NDPA is sent
What is HE NDPA?

## Slide 5: How to enable UL multiplexing for Compressed Beamforming frames?
Aggregated NDPA and Trigger frame
Explicit Trigger frame after NDP frame
Enhanced NDPA frame
HE NDPA
NDPA
Trigger
Frame
NDPA
NDP
Trigger
SIFS
SIFS
HE NDPA
NDP
SIFS
HE NDPA
Enhanced NDPA

## Slide 6: Options for HE sounding protocol Aggregated NDPA and Trigger frame
NDPA and Trigger frames can be aggregated
Pros:
  Reduces overhead involved in sounding protocol
Cons:
  UL MU data does not arrive immediately after TBD IFS of trigger frame
    Exception to the rule (In this case TBD IFS= NDP+2*SIFS)
  Trigger frame and VHT NDPA frame may have redundant information
VHT NDPA
NDP
HE Compressed Beamforming
HE Compressed Beamforming
HE Compressed Beamforming
Trigger
Frame
AP
STA 1
STA 2
STA 3
SIFS
SIFS
DIFS & Backoff
HE Compressed Beamforming
STA 4

## Slide 7: Options for HE sounding protocol Explicit Trigger frame after NDP frame
AP sends a Trigger frame after the NDPA/NDP frames, explicitly
Pros
  Original NDPA frame format can be used for sounding
  The original Trigger frame sequence can be reused
    Compressed beamforming is sent immediately after Trigger
Cons
  Trigger frame and VHT NDPA frame may have redundant information
  Channel sounding frame exchange sequence is changed.
NDPA
NDP
HE Compressed Beamforming
HE Compressed Beamforming
HE Compressed Beamforming
Trigger
AP
STA 1
STA 2
STA 3
SIFS
SIFS
SIFS
TBD IFS
DIFS & Backoff
HE Compressed Beamforming
STA 4
Notes: to facilitate multiplexing of Compressed beamforming frames from STAs

## Slide 8: Options for HE sounding protocol Enhanced NDPA frame format
Include trigger info in NDPA to obtain an enhanced NDPA frame format
  NDPA and Trigger frame format are similar, they can be integrated.
  The trigger information can be included as a separate sub-field in NDPA
    A special type of Trigger format that enables multiplexing of Compressed beamforming reports
  Exclusive for channel sounding procedure
HE NDP
HE Compressed Beamforming
HE Compressed Beamforming
HE Compressed Beamforming
AP
STA 1
STA 2
STA 3
SIFS
SIFS
SIFS
DIFS & Backoff
HE Compressed Beamforming
STA 4
Enhanced NDPA

## Slide 9: Options for HE sounding protocol Enhanced NDPA frame format
  STA Info consists of the important trigger information in addition to the NDPA STA info format

## Slide 10: Options for HE sounding protocol Enhanced NDPA frame format
Pros
  Channel sounding frame sequence is the same as 11ac
  Enhanced NDPA contains the trigger info that enables UL MU mode of Compressed beamforming frames
  Efficient as Trigger and NDPA are integrated into one frame
    Robust, no redundant information
Cons
  A special type of Trigger mechanism
    UL data does not sent immediately after the Trigger frame

## Slide 11: Comparison of the HE Sounding Protocol Options
Aggregated NDPA and Trigger frame
  UL MU data (Compressed beamforming reports) does not arrive immediately after TBD IFS of trigger frame
Explicit Trigger frame after NDP frame
  No new frame format for NDPA
  Channel sounding frame exchange sequence is changed from the 11ac case
Enhanced NDPA frame
  Trigger info incorporated in the enhanced NDPA frames
  Robust and reduces overhead considerably
  A new trigger mechanism as UL MU data doesn’t arrive after TBD IFS of trigger frame

## Slide 12: Summary
Multiplexing of responses from multiple STAs, to data transmission from AP, improves efficiency and reduces overhead
Protocol overhead from sounding and CSI feedback
  MU-MIMO needs frequent updates of CSI
  Number of stations
Need for efficient mechanism for sounding
  Compressed beamforming frames from multiple STAs can be multiplexed.
A few plausible options for HE sounding protocol presented

## Slide 13: References
[1] 11-15-0132r7 Spec Framework
[2] 802.11-15/ 597r1 “Beamformed HE PPDU”

## Slide 14: Straw Poll 1
Do you agree to add to the TG Specification Framework:
x.y.z. :
  The amendment shall define a mechanism to enable multiplexing of the Compressed Beamforming Action frame (CSI feedback) from multiple stations using UL MU(MIMO or OFDMA) mode

## Slide 15: Straw Poll 2
Do you agree to add to the TG Specification Framework:
x.y.z. :
  The amendment shall define a new channel sounding sequence that includes trigger information in order to facilitate UL MU mode of Compressed Beamforming Action frame from multiple STAs.

## Slide 16: Straw Poll 3
Which option do you prefer for enabling UL MU mode in the channel sounding sequence in order to obtain CSI feedback from multiple stations simultaneously ?
1. Aggregated NDPA and Trigger frame
2. Explicit Trigger frame after NDP frame
3. Enhanced NDPA frame
4. Abstain
HE NDPA
NDPA
Trigger
Frame
NDPA
NDP
Trigger
SIFS
SIFS
HE NDPA
NDP
SIFS
HE NDPA
Enhanced NDPA