## Slide 1
Power Save with Random Access
Date: 2015-09-14
Authors:
Name | Affiliation | Address | Phone | Email
Chittabrata Ghosh | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-415-244-8904 | chittabrata.ghosh@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Avi Mansour |  |  |  | avi.mansour@intel.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea | +82-1023566164 | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi’an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Joonsuk Kim | Apple | Cupertino, CA | +1-408-974-5967 | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 9: Abstract
In this contribution, we propose a signaling mechanism that allows the Beacon frame to indicate the target transmission time(s) of one or more Trigger frame(s) that allocates resources for random access
We propose a signaling mechanism to indicate to STAs about a cascaded sequence of Trigger frames for random access

## Slide 10: UL MU features in 11ax PAR and SFD
In the 11ax PAR [1],
  This project may include the capability to handle multiple simultaneous communications in both the spatial and frequency domains, in both the UL and DL.
We have introduced the random access mechanism with Trigger frames using OFDMA [2]
  The spec shall define a Trigger frame that allocates resources for random access. [3]
In this contribution, we introduce the power saving features for the random access mechanism

## Slide 11: Illustration of Random Access with TF-R with Existing UL MU Procedure
RU 1 AID 0
RU 2 AID 0
RU 3 AID 0
Trigger Frame (TF-R)
(random access)
ACK
UL MU PPDU
(STA 1)
UL MU PPDU
(STA 2)
RU 4 AID 0
RU 5 AID 0
STA 2 selects RU 1
STA 1 selects RU 3

## Slide 12: Target Transmission Time for Scheduled TF-Rs
We propose to define a TF-R Start Time, a target transmission time of a TF-R with RUs allocated for random access
AP includes TF-R Start Time(s) of one or more scheduled TF-Rs in Beacon frame
PS STAs receive Beacon frame upon wake up and decode the value in the TF-R Start Time
PS STAs doze till the expiration of TF-R Start Time indicated in Beacon
  Scheduling information in Beacon assists STAs to optimize power consumption with reduced time in Listen state
  Value of TF-R Start Time assists PS STAs not to decode Trigger frame(s) that do not allow random access

## Slide 13: Illustration of Signaling Single Scheduled TF-R
TF
AP
Beacon
TF-R Start Time
TF-R
TF-R Start Time
STA 1
(Power Save)
STA 2
(Power Save)
Random Sub-channel Selection
Random Sub-channel Selection
UL Data
Doze time
Doze time
UL Data
(no random access)
(random access)
Chittabrata Ghosh, et al. (Intel)

## Slide 14: Illustration of Signaling Multiple Scheduled TF-Rs
TF
AP
Beacon
TF-R Start Time 1
TF-R Start Time 1
Random Sub-channel Selection
Doze time
Doze time
UL Data
(no random access)
(random access)
TF-R
TF-R
Doze time
UL Data
Random Sub-channel Selection
TF-R Start Time 2
TF-R Start Time 2
STA 1
STA 2
STA 3
Chittabrata Ghosh, et al. (Intel)
UL Data
Random Sub-channel Selection

## Slide 15: Discussion about Scheduled TF-Rs
The AP may transmit multiple scheduled TFs within a beacon interval
Signaling every scheduled TF-R in a Beacon frame may result in significantly increased overhead
We define a cascaded sequence of TF-Rs
  Following random access using UL OFDMA RUs indicated in current TF-R, the AP transmits another TF-R
  Transmission time of the cascaded TF-R is TBD
We propose a signaling mechanism to indicate whether a scheduled TF-R is cascaded or non-cascaded
Chittabrata Ghosh, et al. (Intel)

## Slide 16: Signaling Cascaded TF-Rs using Frame Control Field in MAC Header
Protocol Version | Type | Sub type | To DS | From DS | More Fragments | Retry | Power Management | More Data | Protected Frame | Order
Bits 2 2 4 1 1 1 1 1 1 1 1
Cascade Indication
For example, we could define a field “Cascade Indication” replacing More Data subfield in Frame Control field of MAC header in TF-R
  The value in this field set to 1 indicates cascaded sequence of TF-Rs
  The value in tis field set to 0 indicates non-cascaded sequence of TF-Rs
Chittabrata Ghosh, et al. (Intel)

## Slide 17: Illustration of Scheduled TF-Rs with Signaling for Cascaded TF-Rs
TF
AP
Beacon
TF-R Start Time
TF-R
TF-R Start Time
STA 1
STA 2
Random Sub-channel Selection
Random Sub-channel Selection
UL Data
Doze time
Doze time
UL Data
(no random access)
(random access)
TF-R
TF-R
Cascade Ind = 1
Cascade Ind = 1
Cascade Ind = 0
STA 3
Doze time
Doze time
UL Data
UL Data
Random Sub-channel Selection
Random Sub-channel Selection
STA 4
Collision
Collision
Chittabrata Ghosh, et al. (Intel)
MU-BA

## Slide 18: Summary
In this presentation, we proposed a signaling mechanism for scheduled TF-Rs
  A cascading sequence of scheduled TF-Rs have been discussed
We have also proposed a signaling mechanism to indicate whether a scheduled TF-R is cascaded or not

## Slide 19: References
[1] IEEE 802.11-14/0165r1 “802.11 HEW SG Proposed PAR”
[2] IEEE 802.11-15/0875r1 “Random Access with Trigger frames using OFDMA”
[3] IEEE 802.11-15/0132r2 “Specification Framework for Tax”

## Slide 20: Straw-poll 1
Do you agree to add to the spec framework?
The spec shall indicate cascaded sequence of Trigger frames for random access by using a bit in the Trigger frame.
Yes:
No:
Abstain

## Slide 21: Straw-poll 2
Do you agree to add to the spec framework?
The spec shall include a mechanism that allows the Beacon frame to indicate the target transmission time(s) of one or more Trigger frame(s) that allocates resources for random access.
Yes:
No:
Abstain