## Slide 1: Regarding UL MU protection
Date: 2015-09-14
Authors:

## Slide 2: Abstract
Addressing necessity of UL MU protection
Discussing possible ways of UL MU protection

## Slide 3: Protection for MU transmission
DL MU[1]
  DL MU protection mechanism was proposed in July meeting
  MU-RTS -> simultaneous CTS
    In order to avoid serial RTS/CTS transmission
  MU-RTS solicits multiple STAs’ simultaneous transmission
    MU-RTS format may not be the same as existing RTS frame
Protection for UL MU hasn’t been considered very well

## Slide 4: Necessity of UL MU protection
Potential problems due to lack of UL MU protection
  EIFS operation of L-STA might not protect M-BA transmission[2]
    EIFS duration can be shorter than M-BA
      Depending on datarate, number of UL-STAs
    ACK is equally important as data
    L-STA fairness problem
  OBSS STAs(hidden from AP) might interrupt UL STAs’ trigger frame reception
It is necessary to consider protection for UL MU as well

## Slide 5: Conditions for UL MU protection
The whole duration of UL MU session must be determined prior to the protection
Each UL STA might have different hidden STAs
  Depending on the location of UL STAs
  Every UL STAs must transmit CTS
AP will initiate protection process
  UL STAs cannot reach each other
  It is preferable that AP triggers multiple STAs protection operation
  RTS(AP: rx), CTS (UL-STAs: tx)
MU-RTS/Sim. CTS(from DL MU protection) can be reused for UL MU protection

## Slide 6: Possible options for UL-MU protection(1)
MU-RTS(AP) – Sim. CTS(UL-STAs) – TF(AP) – UL Data(UL-STAs) – M-BA(AP)
  The simplest form of UL-MU protection
  No further modification is required
  AP might choose whether it triggers Sim. CTS or not
Relatively high overhead
  MU-RTS and Trigger Frame are too much in common in terms of their functionalities

## Slide 7: MU-RTS and Trigger Frame
Both MU-RTS and Trigger Frame solicit UL STAs simultaneous transmission
  Targeting exactly the same UL STAs
  The only difference is that TF indicates RU allocation
MU-RTS doesn’t have to follow RTS format
  MU-RTS will contain multiple per STA info. (different from existing RTS)
  As long as it follows L-format, L-STAs are still able to read its duration field
    MU-RTS might not have NAV cancellation feature in case of CTS failure
    Probability of CTS failure will be much lower than SU case
It is highly likely for MU-RTS to have per STA information at MAC payload as well as TF
  Considering protection including L-STA, MU-RTS cannot contain HE preamble
  It is expected for MU-RTS to have similar frame structure to TF
TF could include the functionality of MU-RTS

## Slide 8: Possible solutions for UL-MU protection(2)
MU-RTS might be integrated into Trigger frame
  Trigger frame solicits both simultaneous CTS and UL-Data
    Reduced overhead (only 1 additional frame transmission is required)
  Format and protocol for implicit MU-RTS need to be further determined
  Issues:
    (1) should every UL MU PPDU follow right after TF? (regarding MAC motion #3[3])
      UL Data will be sent after Sim. CTS
    (2)IFS between Sim. CTS and UL-Data might be shorter than SIFS
      No tx/rx transition between Sim. CTS and UL data

## Slide 9: Conclusion
UL MU protection is necessary as well as DL MU case
To avoid excessive overhead MU-RTS and Sim. CTS, from DL MU protection, can be reused for UL MU
To further reduce the overhead, Trigger Frame might function as MU-RTS in case of UL MU transmission

## Slide 10: Strawpoll 1
Do you agree to add to the TG Specification Frame work document?
  x.y.z. The spec shall define a function that Trigger frame solicits simultaneous CTS responses from multiple STAs to protect UL MU transmission. In case of UL MU protection with simultaneous CTS, UL MU Data transmission follows the simultaneous CTS after xIFS (IFS is TBD).
Y/N/A

## Slide 11: Reference
[1] 11-15-0867-01-00ax-mu-rts-cts-for-dl-mu
[2] 11-15-0611-01-00ax-multi-sta-block-ack-protection
[3] 11-15-0365-00-00ax-ul-mu-procedure