## Slide 1: Discussions on HE SIG-A Structure
Date: 2015-09-16
Authors:
Name | Affiliations | Address | Phone | email
John (Ju-Hyung) Son | WILUS | 263-2 Yangjae-dong, Seocho-gu, Seoul, Korea | +82-2-552-0110 | john.son@wilusgroup.com
Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
Minseok Noh |  |  |  | minseok.noh@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com

## Slide 2: Introduction
TGax adopted HE-SIG-A structure as follows [1]
  HE-SIG-A (using a DFT period of 3.2 µs and subcarrier spacing of 312.5 kHz) is duplicated on each 20 MHz after the legacy preamble to indicate common control information.
  HE-SIG-A is present in all 11ax packets and is two OFDM symbols long when it uses MCS0
    Information bits in HE-SIG-A are jointly encoded as in VHT-SIG-A (using 48 tones or 52 tones is TBD).
    SU packets and UL Trigger based packets do not contain HE-SIG-B symbols.
In this submission, we discuss further about HE-SIG-A’s information and HE-SIG-A’s utilization of 52 data tones.

## Slide 3: HE-SIG-A Structure
64 FFT
256 FFT
(A-)MPDU
HE-
LTF
1
HE-
STF
HE-
SIG-A
HE-
LTF
n
...
For SU PPDU or UL MU PPDU,
  HE-SIG-A includes common control information and single-user specific information
For MU PPDU,
  HE-SIG-A includes common control information
  HE-SIG-B includes resource allocation information and multi-user specific information
Both HE-SIG-A and B should be decoded based on L-STF/L-LTF
  Out of the total 64 tones/20MHz, L-STF/L-LTF utilizes 52 tones (excluding 12 tones for guard/DC)
  Then out of the 52 tones, L-SIG/HT-SIG/VHT-SIG-A utilizes 48 tones for Data (excluding 4 tones for pilot)
  From 11n, 4 additional tones in guard bands are utilized increasing available Data tones to 52 in PSDU.
L-STF
L-LTF
L-
SIG
64 FFT
256 FFT
(A-)MPDU
HE-
LTF
1
HE-
STF
HE-
SIG-A
HE-
LTF
n
...
HE-
SIG-B
variable
L-STF
L-LTF
L-
SIG
SU
/UL MU
PPDU
DL MU PPDU
*RL-
SIG/
SS
*RL-
SIG/
SS
*RL-SIG/SS refers a symbol for auto-detection (details are under discussions in TGax)

## Slide 4: Possible Signaling Information of HE-SIG-A/B
Common Info (HE-SIG-A)
  BW (2b for 20/40/80/160MHz)
  GI (2b for 0.8/1.6/3.2us)
  Power Save (1b, TBD)
  LTF (1b for 6.4/12.8us)
  SU/MU indicator (1b, TBD)
  BSS color (TBD)
  HE-SIG-B Length (TBD)
  HE-SIG-B MCS (TBD)
  others (TBD)
Single User Info (HE-SIG-A)
  PAID (9b), NSTS (3b), MCS (4b), STBC (1b), Coding (1~2b)
  Beamformed (1b)
  others (TBD)
Resource Allocation Info (HE-SIG-A)
  Resource Allocation (TBD)
  others (TBD)
Based on VHT-SIG, 11ax SFD [1], and previous discussions in TGax, possible signaling information for HE Preamble can be classified as follows.
Multi User Info (HE-SIG-B)
  PAID (9b) (or GID), NSTS (3b), MCS (4b), Coding (1~2b)
  Length (TBD)
  others (TBD)
SU
Info
HE-SIG-A
HE-SIG-B
Resource
Alloc.
Info
variable
...
MU
Info
[n]
MU
Info
[0]
SU/
UL MU
DL MU
Common
Control
Info
Common
Control
Info
CRC
/Tail
CRC
/Tail
CRC
/Tail
Additional
Resource
Alloc.
Info

## Slide 5: Utilizing 52 Data tones for HE-SIG-A/B
In order to accommodate the previous signaling information in HE-SIG-A/B, it would be beneficial to utilize unused subcarriers in HE-SIG-A/B making available Data tones upto 52.
Then, we need channel estimation of additional subcarriers of {±27, ±28} before HE-SIG-A.
L-SIG (and/or RL-SIG/SS) can deliver pilot sequences on its {±27, ±28} subcarriers for channel estimation.
If channel estimation on those unused subcarriers are done by added pilots in L-SIG only, RL-SIG/SS symbol can deliver additional information on those subcarriers.
L-STF
L-LTF
L-
SIG
HE-
SIG-A
HE-
SIG-B
11ax PPDU
64 FFT part
L-SIG (and/or RL-SIG/SS)
L-SIG (and/or RL-SIG/SS)
D
C
-26
-1
Guard
Guard
1
26
-32
31
Pilot ?
Pilot ?
frequency
-29
29
HE-SIG-A/B
D
C
-28
-1
Guard
Guard
1
28
-32
31
HE-SIG-A/B
frequency
...
RL-
SIG
/SS

## Slide 6: Conclusions
We discussed possible design options for HE-SIG-A
  Information splitting between HE-SIG-A and B
    HE-SIG-A to have Common Control Info and SU specific Info for HE SU PPDU
  HE-SIG-A’s utilization of 52 data tones
    We propose HE-SIG-A to utilize 52 data tones after additional channel estimation of unused subcarriers {±27, ±28} from pilots in L-SIG (and/or RL-SIG/SS).
    We need to study further on the aspects of legacy impacts, optimal pilot sequences, and required number of symbols for channel estimation, etc.

## Slide 7: Straw poll
  Do you agree the following ?
  Information bits in HE-SIG-A are jointly encoded as in VHT-SIG-A (using 52 tones) with additional pilots on subcarriers of {±27, ±28} before HE-SIG-A symbols.
  Y
  N
  A

## Slide 8: References
[1] 11-15/0132r7 Spec framework