## Slide 1: Buffer Status Report
Date: 2015-09-12
Authors:

## Slide 2
Authors (continued):

## Slide 3
Authors (continued)

## Slide 4
Authors (continued)

## Slide 5
Authors (continued)
Alfred Asterjadhi, et. al.

## Slide 6
Authors (continued)
Alfred Asterjadhi, et. al.

## Slide 7
Authors (continued)

## Slide 8: Introduction
One of the main features introduced in 11ax is UL MU operation
  AP allocates UL resources used by multiple STAs to transmit their data
For an efficient allocation the AP needs to know UL buffer status (BS) of its STAs. The BS knowledge allows the AP to:
  Allocate resources to those STAs that have something to transmit in UL
  Calculate correctly the UL resources needed by the STAs
We propose to specify a BS report mechanism that:
  Relies on QoS Control field and its enhancements for improving BS report
  Allows solicited or unsolicited delivery of the buffer status reports
    Delivery is performed using commonly expected 11ax frame exchanges

## Slide 9: Summary of Proposal
AP elicits for BS reports via the Trigger frame
  The AP can indicate whether it is soliciting BS information for:
    E.g., a particular TID (per-TID), for all TIDs (all-TID), with different granularity, …
STA delivers BS report in QoS Control of QoS Data/Null frames
  Per-TID BS info. is contained in Queue Size/TXOP Duration Requested subfield
    Note: This is the same signaling that is used for HCCA
Note: Delivering BS information with different granularity, for the solicited and unsolicited case, is beneficial as well (see Appendix). The signaling for this case is currently TBD

## Slide 10: “BS report” frames: Details
STA reports BS info. in the QoS Control field of frames it transmits:
  Queue Size is reported when AP is in control of UL TX parameters (e.g., MU)
  TXOP Duration Requested when non-AP STA is in control of them (e.g., SU)
“BS Report”

## Slide 11: BS Report mechanism: Overview
STAs implicitly report their BS information in “BS report” frames
  A “BS report” frame is any frame that contains QoS Control field
AP can explicitly solicit particular BS info. in “BS polling” frames
  The frame carrying the Trigger is proposed to act as a “BS polling” frame
    It can explicitly contain the type of BS information requested
      E.g., Per-TID versus all-TID “BS report” (eventually the TID for which the per-TID polling refers to)
      Requested granularity for the BS info (i.e., units different from default)
QoS Data
QoS Data
Trigger
QoS Data
Ack
DL Data 3
DL Data 5
BA/QoS Data
BA/QoS Data
Beacon
BA
Buffer Status Report
Trigger
QoS Data/Null
Ack
SU
MU

## Slide 12: Summary
We propose to re-use the QoS Control field for reporting BS
  When carried in QoS Data/Null frame it allows per-TID “BS report”
We also propose a simple BS signaling mechanism that enables:
  AP to solicit BS information from STAs with different granularity
Future extensions are possible to enable BS reports with different granularity

## Slide 13: Straw Poll 1
Do you support using the QoS Control field in QoS Data and QoS Null frames to report per-TID Buffer Status information?

## Slide 14: Straw Poll 2
Do you support that an AP can poll STAs for buffer status reports using the frame carrying the trigger info?
  The poll can request for specific buffer status information with TBD granularity.

## Slide 15: appendix
Alfred Asterjadhi, et. al.

## Slide 16: QoS Control field: Overview
Current format of QoS Control field carries per-TID queue size/duration:
  Queue Size ranges from 0 to 64 768 Octets, with a unit of 256 Octets
  TXOP Duration Requested ranges from 0 to 8160 us, with a unit of 32 us
However, HE transmit rates are expected to be highly flexible:
  Covering a wider range (from ~416Kbps (@2.5MHz) to up to ~10?Gbps (@160MHz))
  Hence, these limitations in BS info. signaling will lead to inefficient allocations
E.g. 1: AP allocates low rate RU to STA that signaled 256 Bytes of UL Data
  But STA actually has less (e.g., 128 Bytes) UL to be delivered in the 256 Octet RU
    An RU of ~5ms for UL TX@416Kbps requires that all UL MU STAs transmit for 5ms!
      When time needed by the STA is actually half of that (50% of MU resource is wasted)
E.g., 2: AP allocates high rate RU to STA that signaled >64 KB of UL Data
  But STA actually has more (e.g., 640 KB) UL to be delivered in the 64KB Octet RU
    An RU of ~1 ms for UL TX@500Mbps is enough to transmit only 10% of its UL
      When the STA could actually support transmitting at higher rates to deliver its UL (resource was underused)
Similar observations apply to the TXOP Duration Requested subfield as well