## Slide 1: HE A-Control field
Date: 2015-09-12
Authors:

## Slide 2
Authors (continued):

## Slide 3
Authors (continued)

## Slide 4
Authors (continued)

## Slide 5
Authors (continued)
Alfred Asterjadhi, et. al.

## Slide 6
Authors (continued)
Alfred Asterjadhi, et. al.

## Slide 7
Authors (continued)

## Slide 8: Introduction
Many features that are candidates for 11ax require a wide range of control information to be exchanged between HE STAs and AP
  Examples include: Buffer status feedback, channel quality information feedback, resource allocation, power save feedback, power control, rx. operation mode change, etc.
All this control information needs to be signaled somewhere within exchanged frames between STAs
We propose to define an HE Aggregated (A-) Control field that:
  Is a universal carrier of all control information needed for different 11ax features,
  Is flexible and can be dynamically added to any PPDU with minimal overhead

## Slide 9: HE A-Control field
We propose to define an HE A-Control field that:
  Carries one or more HE Control fields
    Each HE Control carries control info. for different HE features [1, 2, 3]
HE A-Control field can be carried in PPDUs as part of:
  QoS Data/MGMT frames in the HT Control field
    HE A-Control field is compatible with HE variant of HT Control field
      See next slide
    It will be 4 Octets in length, i.e., no change in MAC header size
      Keeps backward compatibility
HE Control 1 | HE Control 2 | … | HE Control N
HE A-Control field
Padding
If 4 Octet boundary
is preferred
0-3 Bytes

## Slide 10: HE A-Control field as HT Control variant
HE A-Control field added to QoS Data/Mgmt frames (variant of HT Control field)
  Currently the type of the HT Control field is determined by values of B0 and B1
    B0 of HT Control field differentiates the VHT variant from the basic HT Control field (11n/11ac)
  If B0 and B1 are 1 then the HT Control field contains an HE A-Control field variant (11ax)
    Control ID field identifies the control information (usable for future amendments as well)
    End of HE Control (EOH) subfield in an HE Control indicates if another HE Control follows
Contents of HT Control field across multiple MPDUs of an A-MPDU
  Currently it is the same for all HT Control fields generated by pre-11ax STAs (11n/11ac)
  Within HE PPDUs we may want to consider relaxing this restriction:
    A large variety of control information can be carried within the A-MPDU
    Increases robustness of info. by aggregating it in different parts of A-MPDU with minimal overhead
Control ID
VHT (1)
HE (1)
Ctrl. Info.
EOH (0)
B2 B6
B7
B0
B1
variable
2 | 2 | 6 | 6 | 6 | 2 | 0/6 | 0/2 | 0/4 | 0/8 | variable | 0/8 | 4
FC | Duration /ID | A1 | A2 | A3 | SC | A4 | QoS Ctrl | HT Ctrl | CCMP Header | Frame Body | MIC | FCS
Reserved value indicates
HE A-Control variant of HT Control field
…
HE A-Control field

## Slide 11: HE Control field: Preview
See Appendix for a couple of examples
Octets: |  | 1 |  | 0 or more
 | Reserved | Control ID | EOH | Control Information
Bits: | 2 | 5 | 1 | 
Control ID | Control Information | Description
0 | Ack | Indicates an Ack (successful RX of immediately preceding MPDU)
1 | BAR | Indicates a Block Ack Request (request for a block ack)
2 | BA | Indicates a Block Ack (receive status of previously received MPDUs)
3 | QoS Control | Indicates buffer status request/report (enhanced version of QoS Control)
4 | CQI Control | Indicates channel quality info./MCS feedback (enhanced version of HT)
5 | Unicast Trigger | Indicates a Trigger (resource allocation and other parameters for UL)
6 | ROMI | Indicates a receive operating mode change [2]
7-30 | … | TBD
31 | Extension | Reserved for future extension

## Slide 12: Summary
We propose defining an HE A-Control field that:
  Is a universal carrier of control information needed for new 11ax features,
  Is flexible and can be dynamically added to any PPDU with minimal overhead
  Is extensible for future amendments

## Slide 13: Straw Poll 1
Do you agree defining an HE variant (of the VHT variant) of the HT Control field that carries one or more control fields for HE control information?
  B0 and B1 of the HT Control field in this case are set to 1
  The control fields can be called HE Control field

## Slide 14: References
[1] L. Chu (Marvell), et. al., 11-15-xxxx-00-00ax-acknowledgement to DL MU
[2] E. Wong (Apple), et. al., 11-15-0xxx-00-00ax-receive-operating-mode-indication-for-power-save
[3] A. Asterjadhi et. al., 11-15-xxxx-00-00ax-buffer status report

## Slide 15: appendix
Alfred Asterjadhi, et. al.

## Slide 16: HE Control: E.g., request/response for ack
STA adds HE Control to request/respond for/with acknowledgements
  HE Control is part of the HE A-Control field
The STA can carry control information in an HE A-Control field instead of adding Ack, BlockAck, or BAR frames whenever possible
  Reduces MAC overhead and simplifies design as it eliminates the need of aggregating multiple CTRL frames
Octets: |  | 1 |  | 0 or more
 | Reserved | Control ID | EOH | Control Information
Bits: | 2 | 5 | 1 | 
Ack (Control ID 0)
Octets: | 2 | 4
 | BAR Control | BAR Information
BAR (Control ID 1)
Octets: | 2 | variable
 | BA Control | BA Information
BA (Control ID 2)
 | HE Control 1 | … | HE Control n
HE A-Control field
Same contents as Ack/BAR/BA frames

## Slide 17: HE Control: E.g., buffer status poll/report
The AP polls the STAs for their buffer status in an efficient way [3]
  It sends “BS polling” frames that contain an enhanced QoS Control field
    Specifying whether polling is “per-TID”, “all-TID” and other related BS polling parameters
Non-AP STAs deliver buffer status reports in the QoS Control field
  Per-TID BS information is carried in QoS Data and QoS Null frames
  All-TID, per-TID BS information is carried in the enhanced QoS Control field
The enhanced QoS Control can be aggregated with other info. in HE A-Control
  Reduces the incurred MAC overhead and has other benefits as specified in [3]
Octets: |  | 1 |  | 2
 | Reserved | Control ID | EOH | Control Information
Bits: | 2 | 5 | 1 | 
2
QoS Control
 | HE Control 1 | … | HE Control n
TXOP Duration Requested
Queue Size
TID/SF
TID/SF
Reserved
“BS report”
“BS polling”
QoS Control (Control ID 3)

## Slide 18: HE Control: E.g., unicast Trigger
AP can add an HE Control field to indicate unicast trigger information
  Subchannel allocation for a STA, compressed/uncompressed UL MAC format, etc.
    Reduces overhead of a standalone MAC frame etc. [1]
By being part of an HE A-Control carried in a DL MU PPDU
  This way additional control information for the STA can be carried in the DL MU PPDU with minimal overhead
Octets: |  | 1 |  | 0 or more
 | Reserved | Control ID | EOH | Control Information
Bits: | 2 | 5 | 1 | 
Octets: | Variable (TBD)
 | Trigger Information
Unicast Trigger (Control ID 5)
 | HE Control 1 | … | HE Control n
HE A-Control field
Same contents as per-STA Info field of Trigger frame