## Slide 1: Identifiers in HE PPDUs for power saving
Date: 2015-09-12
Authors:

## Slide 2
Authors (continued):

## Slide 3
Authors (continued)

## Slide 4
Authors (continued)

## Slide 5
Authors (continued)
Alfred Asterjadhi, et. al.

## Slide 6
Authors (continued)
Alfred Asterjadhi, et. al.

## Slide 7
Authors (continued)

## Slide 8: Introduction
Currently, PHY is discussing populating SIG-A and SIG-B
  An identifier of the BSS (e.g., BSS COLOR) is proposed in SIG-A that is
    Beneficial for spatial reuse as discussed in [1]
    Beneficial for power save as discussed in this presentation
  Other identifiers, such as the (set) receiver(s) is likely to be present in the SIG-B field of HE DL MU PPDUs
    However, it is not clear whether it will be present in the other cases
In addition to the BSS COLOR field, we propose SIG-A to contain an UL/DL Flag field to:
  Enable intra-PPDU power saving

## Slide 9: Proposed Identifiers in PHY header
BSS COLOR field is proposed for the SIG-A field of an HE PPDU
  The BSS COLOR contains a non-unique value that identifies the BSS
    All HE PPDUs generated by BSS’s members have same value
      A STA that receives an HE PPDU with a BSS COLOR equal to its BSS classifies it as a member PPDU
      Otherwise, it classifies it as a nonmember PPDU
UL/DL Flag field is proposed for the SIG-A field of an HE PPDU:
  The UL/DL Flag indicates whether the frame is Uplink or Downlink
Legacy Preamble
(L-SIG)
HE Preamble
(RL-SIG, SIG-A, SIG-B, …)
PSDU
((A-)MPDU)
Identifiers: COLOR, RA, TA, …

## Slide 10: Considerations on power save
A non-AP STA that has declared to its AP to be in Awake state
  Can go to sleep for a duration of time only if:
    The AP is not going to transmit a frame to that STA during that duration of time
    E.g., the AP is busy communicating exclusively with other devices
For the purpose of this proposal we focus on intra-PPDU power save
  After decoding the PHY header of a PPDU, the STA can sleep for the PSDU duration only if
    The PPDU is a member PPDU and is not intended for the STA
Hence, the non-AP STA is not allowed to sleep for the duration of a PSDU that:
  Is contained in a non-member PPDU
  Is contained in a member PPDU intended for the STA
UL PPDU STA 2
PS state as known at AP (Awake)
STA 1 state
DL PPDU STA 2
UL PPDU
DL PPDU STA 1
DL PPDU
DL PPDU STA 4
OBSS Activity
BSS Activity
Doze
Awake
UL PPDU STA 7

## Slide 11: Can BSS COLOR alone enable intra-PPDU PS?
Assuming that only the BSS COLOR field is available in the PHY header:
  The STA could go to sleep only if the received frame is a non-member PPDU
    But by doing so it could end up sleeping while the AP happens to transmit to it, missing the frame!
      In general, it is not a good idea to do so as it increases transmission failures
In addition, BSS COLOR does not differentiate if the PPDU is intended to the STA
  Hence, the STA cannot go to sleep during the PSDUs that are:
    Transmitted by the AP and intended to other associated STAs (basically all BSS DL traffic minus 1)
    Transmitted by other associated STAs intended to the AP (basically all BSS UL traffic)
  Activating intra-PPDU PS for these PSDUs is very beneficial
    A STA is expected to receive frames generated within the BSS very frequently
Hence, BSS COLOR alone does not provide information to enable intra-PPDU PS
  Because the STA at least needs to know that the PPDU is not intended for it
  Additional identifiers can help (see next slide)
Legacy Preamble
(L-SIG)
HE Preamble
(RL-SIG, SIG-A, SIG-B, …)
PSDU
((A-)MPDU)
Identifiers: COLOR, RA, TA, …
Sleep if member-PPDU…
PPDU intended to non-AP STA

## Slide 12: Intra-PPDU PS enhancements
When both BSS COLOR field and UL/DL Flag are available:
  Non-AP STA determines if the member PPDU is uplink or downlink
    The STA can go to sleep for all member PPDUs that are uplink (only UL)
Hence, the addition of UL/DL Flag is beneficial for intra-PPDU PS
  Non-AP STAs can sleep during all UL member PSDUs not intended to it
Note: A STA still has to receive DL member PPDUs not intended to it
  I.e., no intra-PPDU PS is possible for these frames
  An identifier of the intended receiver helps in this case,
    Pros and cons of this case are currently under investigation

## Slide 13: Summary
We propose adding a BSS COLOR field and an UL/DL Flag field in the common portion of the HE PHY header to enable intra PPDU power saving for HE STAs

## Slide 14: Straw Poll 1
Do you support to add to the SFD:
  The spec shall support adding a BSS COLOR field in the SIG-A field
    The BSS COLOR field is an identifier of the BSS (size TBD)

## Slide 15: Straw Poll 2
Do you support adding the following rules to the SFD:
  An HE non-AP STA may enter the Doze state until the end of an HE DL MU PPDU if:
    the value of the PPDU’s BSS COLOR field is equal to the BSS COLOR of its BSS, and
    the value derived from any of the STA Identifiers in the SIG-B field does not match its own identifier or that of a broadcast/multicast identifier
  An HE non-AP STA may enter the Doze state until the end of an HE UL MU PPDU if:
    the value of the PPDU’s BSS COLOR field is equal to the BSS COLOR of its BSS

## Slide 16: Straw Poll 3
Do you support adding an UL/DL Flag field in the SIG-A of an HE SU PPDU?
  The UL/DL Flag indicates whether the frame is Uplink or Downlink
    The value of this field for TDLS is TBD

## Slide 17: Straw Poll 4
Do you support to add the following rules to the SFD:
  An HE STA may enter the Doze state until the end of an HE SU PPDU if:
    the value of the PPDU’s BSS COLOR field is equal to the BSS COLOR of its BSS, and
    the value of the UL/DL Flag field indicates that the frame is uplink

## Slide 18: References
[1] R. Porat (Broadcom), et, al, 11-14-0082-00-0hew-Improved-Spatial-Reuse-Feasibility-Part-I
[2] 11-15/0314r2 Sleep States in IEEE 802.11ax Simulation Scenarios