## Slide 1: Discussion on AP Coordinated Concurrent STA-to-STA Transmissions in 11ax
Date: 2015-09-14
Authors:

## Slide 2: Background
STA-to-STA (S2S) transmissions may provide significant benefits
  Higher spectrum (reuse) efficiency, higher order MCS, power saving, etc.
To boost spectrum (reuse) efficiency, concurrent S2S transmissions are particularly desirable
S2S transmissions may be operated with or without AP
More capabilities of transmission coordination such as scheduling based MU transmission using OFDMA are considered to be supported by AP in 11ax
In the case of S2S concurrent transmissions with AP, AP may provide transmission coordination to further enhance the performance
  Which also fully utilize the feature (AP centric) in 11ax

## Slide 3: Interference in S2S Concurrent Transmissions
There are multiple receivers in S2S concurrent transmissions
  For UL TX from STA_1 to AP, receiver is AP
  For S2S TX from STA_3 to STA_2, receiver is STA_3
AP may suffer interference from STA_3
STA_2 may suffer interference from STA_1
Concurrent are allowable if
  Interference level at two receivers are both acceptable
  Practically, SINR at two receivers are both acceptable (Concurrent TX opportunity)
To find a concurrent TX opportunity, intuitive and possible method is adjustable CCA and TPC

## Slide 4: Adjustable CCA and TPC
Adjustable CCA and TPC could support concurrent TX even when interference levels at receiver sides are high
  Concurrent TX are allowable when SINRs at all receivers are acceptable
To find a concurrent TX opportunity, STA_3 needs to know
  SINR at AP when power level PWRsta_3 is used
    Specific power level adopted by STA1, PWRsta_1
    Path loss from STA_1 to AP
    Path loss from STA_3 to AP
  SINR at STA2 when PWRsta_3 is used
    Specific power level adopted by STA1, PWRsta_1
    Path loss from STA_1 to STA_2
    Path loss from STA_3 to STA_2

## Slide 5: AP Coordinated Medium Access Flow for Concurrent TX
An adjustable CCA/TPC-only solution may invoke considerable information exchanges
An AP coordinated medium access may alleviate information exchanges while successfully finding our a transmission opportunity
When a S2S transmitter attempts to transmit, it determines a transmission power, PS2S, according to the QoS requirement. And then a S2S transmitter sends a buffer_report to both AP and S2S receiver.
  The buffer_report is transmitted using the maximum allowable TX power Pmax
  The buffer_report carries the value of Δ, by which PS2S can be derived by Pmax-Δ

## Slide 6: AP Coordinated Medium Access Flow for Concurrent TX
If the AP successfully receives a buffer_report from a S2S transmitter, it stores this message and waits for a period of time
  If an UL_buffer_report is received, the AP estimates its SINR
    If this SINR is acceptable, the AP replies a trigger_frame (this trigger_frame is valid for S2S transmitter, S2S receiver, and UL STA)
    If this SINR is not acceptable, the AP replies a trigger_frame (this trigger_frame is only valid for UL STA)
  If an UL_buffer_report is not received, then the AP replies a trigger_frame (this trigger_frame is valid for S2S transmitter and S2S receiver)

## Slide 7: AP Coordinated Medium Access Flow for Concurrent TX
Upon receiving a trigger_frame valid for UL and S2S, then the UL STA transmits uplink data to the AP.
  When UL transmission begins, a S2S receiver estimates its SINR according to UL interference and PS2S
    If SINR is acceptable, S2S receiver replies a S2S_clear_frame to a S2S transmitter. The S2S_clear_frame may contain recommended MCS, number of space-time stream, etc. which derived from the local SINR.
    Otherwise, no S2S_clear_frame is replied
  When a S2S transmitter receives both a S2S_clear_frame from a S2S receiver and a trigger_frame from an AP, it begins the S2S concurrent transmissions using parameters suggested by the S2S receiver.

## Slide 8: AP Coordinated Medium Access Flow for Concurrent TX

## Slide 9: Summary
In this contribution, an AP coordinated MAC flow is discussed for concurrent S2S transmissions
  Find the opportunity that SINRs at both receivers are acceptable
  Performance of concurrent transmissions is guaranteed
  Fully reuse the buffer_report/trigger_frame exchange framework
When a buffer_report is transmitted by a STA attempting to initiate S2S transmissions as a transmitter, the buffer report carries
  Δ: a power level deviation from the maximum allowable TX power (facilitate both receivers to estimate the received power level)
S2S concurrent TX are performed if a S2S transmitter receives both a S2S_clear_frame from a S2S receiver and a trigger_frame from an AP