## Slide 1: Notes on current status of 802.11ax Spatial Reuse ad hoc group
Date: 2015-09-14
Authors:

## Slide 2: Abstract
Intense debates in Study Group (SG) High Efficiency WLAN (HEW) and in the following Task Group AX (TGax) reveal a substantial interest in the optimization of conditions that affect spatial frequency reuse in 802.11. Around seventy submissions discuss varies aspects of improvements for spatial frequency reuse and several ideas for enhancements have been provided. Until today however, TGax failed to agree on an addition to the current Specification Framework Document (SFD). With the SFD approaching an advanced status, the 802.11ax Spatial Reuse (SR) ad hoc group needs to decide how to progress.
The present chairmen’s note intends to stipulate discussion in the SR ad hoc group to develop a compromise SFD text that will be acceptable to the majority of delegates in the ad hoc group and TGax.

## Slide 3: The Past

## Slide 4: CSMA/CA retrospect
802.11 was formed after amendments to 802.4 (Token Bus) and 802.3 (Ethernet) failed [78]
802.11 builds on Carrier Sensing Multiple Access with Collision Avoidance (CSMA/CA)
  Carrier Sensing implements Listen-before-Talk (LBT)
  802.11 initial PHYs are Infrared (IR), Frequency Hopping Spread Spectrum (FHSS), and Direct Sequence Spread Spectrum (DSSS)
802.11-1997 defines “Physical and virtual carrier sense functions” for all PHYs
  Clear Channel Assessment (CCA) implements Physical carrier sensing and Network Allocation Vector (NAV) implements virtual carrier sensing

## Slide 5: CCA from DSSS in 802.11-1997 to OFDM in 802.11a-1999
802.11’s first commercial success based on DSSS PHY
  802.11-2012 marks FHSS and IR PHYs as obsolete
DSSS defines three conditions for CCA to turn busy
  Energy above threshold (down to −80 dBm)
  Carrier sense only (unconditional)
  Carrier sense with signal strength above threshold
802.11a OFDM extends DSSS CCA principles
  Introduction of Energy Detection (ED) and Preamble (resp. PHY Protocol Data Unit, PPDU) Detection thresholds
  Forms basis for amendments 802.11g, 802.11n, 802.11y, 802.11ac, and 802.11af

## Slide 6: Energy Detection (ED) in 802.11
ED concept introduced with 802.11a
  A letter ballot comment calls for CCA definition, approved by WG [3]
    See motion text in right column
  Later, the term ED replaces “for any signal”
    No mentioning of ED in 802.11a-1999
“Motion #22: Define CCA sensitivity by stating that a valid OFDM frame at receive level eq or greater than the minimum 6Mbps specified sensitivity shall cause CCA to indicate busy with probability >90% within 5 microseconds. If the preamble portion was missed, the receiver shall hold the CS signal busy for any signal 20dB above minimum 6Mbps sensitivity (−62dB).
Moved by Dean Kawaguchi
Seconded by Richard van Nee
13/0/8 Approved” [4]

## Slide 7: Observations regarding ED
Used as fallback mechanism
  CCA turns busy “If the preamble portion was missed” [3]
  At −62 dBm CCA turns busy “for any signal” because ongoing transmissions cannot be identified as such
  At the end of the millennium, HiperLAN/2 and 802.11a were expected to be sole users of 5 GHz band
  IEEE 802.11 & ETSI BRAN agreed to use same OFDM PHY and preambles
Dependency on minimum sensitivity
  “20dB above minimum 6Mbps sensitivity” [3]
  BPSK½ (6 Mb/s) defined as lowest Modulation and Coding Scheme (MCS)
    Also used with PHY preamble signaling etc.
  If ED definition depends on lowest sensitivity, how is BPSK½ sensitivity specified?

## Slide 8: Minimum sensitivity in 802.11
BPSK½ sensitivity defines minimum MCS
  Minimum sensitivity was derived by simulations
  5 dB implementation margin & 10 dB Noise Figure (NF) added
    See right hand column
  Compromise value achievable with many implementations
Comment Seq. #131:
“The numbers for receiver sensitivity are small. These numbers are derived by adding 5dB margin to the computer simulation results with no degradation factor. […] These results are with NF = 10 dB” [3]
[2] outlines general CCA design considerations

## Slide 9: The evolution of 802.11 Clear Channel Assessment (CCA)
802.11 CCA evolved over time
  Right picture from [76] summarizes various aspects
  Logical “OR” of different conditions triggers busy status
    PHY dependency

## Slide 10: Optimal carrier sensing
Optimal carrier sensing balances protection for ongoing frame transmissions & gains from spatial frequency reuse
  Too sensitive designs cause medium underutilization
  Too insensitive designs reduce Signal to Interference ratio (SIR)
    Increased frame error probability
Adaptive carrier sensing thresholds considered in 1994 [1]
  Back then, considered to be too complex
  2011 proposed again [5]
Hence, spatial reuse optimizations are not a new topic
  Also debated in 802.11s (mesh) but 802.11ax reaches larger audience
  Legacy issues also discussed in [6]

## Slide 11: The Present

## Slide 12: IEEE 802.11ax SR ad hoc group – Retrospect
High Efficiency WLAN (HEW) Study Group (SG)
  Approved in March 2013
  First meeting in May 2013
802.11ax Project Authorization Request (PAR) and Criteria for Standards Development (CSD)
  Approved in March 2014
  First TGax meeting in May 2014
Spatial Reuse (SR) ad hoc group formation
  Approved in November 2014
  First SR ad hoc group meeting in March 2015

## Slide 13: Spatial reuse enhancements – Today
Various proprietary chipset optimizations exist
  Tackling raised noise floor issues etc.
Hot topic with 802.11ax because of its focus on dense deployments
  High spatial frequency reuse needed
  Improvement in b/s/Hz/m² targeted
Various submissions indicate that current 802.11 CCA might be too stringent, too careful, too sensitive
  Margins for improvements seem to exist
  Do current settings cause 802.11 to underperform?

## Slide 14: Where are we?
Almost 70 submissions related to spatial frequency reuse
  Pre-SG HEW submissions not counted but may be interesting to study too
Four ad hoc meetings à 2 h
  Typical number of attendees exceeds 50
  A lot of manpower gone into debates
A simulation calibration initiative has been formed
  Many offline debates, contributions from many parties
Why did all proposals adding SR text to the SFD fail?

## Slide 15: Classification
A classification scheme has been proposed in [XXX]. It reports the following design ideas:
  “Dynamic Sensitivity Control (DSC)
  Sensitivity modified based on RSSI modified by ‘Margin’
  Revised/Variable/Dynamic/Signaled/Per-Link CCA
  Revised CCA: CCA Threshold redefined for 11ax devices, with use of ‘BSS Color’
  Variable CCA: CCA Threshold variable for 11ax devices, centrally managed
  Dynamic CCA: CCA Threshold may change dynamically for 11ax devices
  Signaled CCA: CCA Threshold may be modified by transmitting device
  Per-Link CCA: CCA Threshold optimized on a per-link basis”
Will the 802.11ax SR ad hoc group identify and agree on one or more candidates (aforementioned or others) for inclusion in the Specification Framework Document (SFD)?

## Slide 16: The Future

## Slide 17: Quo vadis IEEE 802.11ax SR ad hoc group?
Are there majority supported answers to the following questions?
  How high are the gains?
  Is legacy operation affected?
    If yes, which level of SIR degradation is acceptable?
  How close to optimal SR can we get?
Next page shows the current status of the SR enhancement clause in the Specification Framework Document (SFD)

## Slide 19: Timeline
802.11ax TG intends to finalize its SFD in January 2016
  See below modified picture from [77]
This leaves the 802.11ax SR ad-hoc group with roughly three meetings (September, November, and January) to develop and agree on text for the SFD
  Any decision in the SR ad hoc group needs to be approved by the TG!

## Slide 20: Summary
A standardized SR solution benefits all users and vendors
  802.11ax is the right forum to balance concerns vs. gains
  Standardization provides interoperability, interoperability provides stability
  Overcome proprietary “enhancements” already in use
Attendees of the 802.11ax SR ad hoc group are encouraged to propose additions to the 802.11ax SFD
  At most 3 meetings remain to complete the 802.11ax SFD
Attendees should consider to develop joined proposals to amend the SFD
  Compromises should be considered to increase the likelihood of a proposal to be accepted
In general, a large number of submissions [7-75] to SG HEW & TGax prove that spatial reuse is of high interest
  A compromise may be better for everyone than no SFD addition at all

## Slide 21: References (pre-HEW) 1
L. H. Zuckerman, “Elaborate Clear-Channel Assessment for Indoor Communication Systems Operating in Uncontrolled UHF & Microwave Bands,” Submission IEEE 802.11-94/132, Jul. 1994.
K. Ishii, “CCA Threshold Definition to Guarantee Service Quality in Multicell Environment,” Submission IEEE 802.11-98/173, May 1998.
N. Chayat, “TGa Letter Ballot 16 Comment Resolution Report,” Submission IEEE 802.11-99/32, Jan. 1999
R. H. Paine, “IEEE 802.11 – Task Group A Minutes,” Submission IEEE 802.11-99/36, Jan. 1999.
L. H. Zuckerman, “Proposal to Investigate Advanced Clear Channel Assessment (CCA) &/or Specific Transmit Power Control (TPC) for Higher Network Throughput & Reduced Battery Drain,” Submission IEEE 802.11-11/392, Mar. 2011.
B. McFarland et al., “Energy Detect CCA Threshold,” Submission IEEE 802.11-06/1790, Nov. 2006.

## Slide 22: References (HEW & 802.11ax) 2
R. Porat and N. Jindal, “Improved Spatial Reuse Feasibility – Part I,” Submission IEEE 802.11-14/82, Jan. 2014.
R. Porat and N. Jindal, “Improved Spatial Reuse Feasibility – Part II,” Submission IEEE 802.11-14/83, Jan. 2014.
J. Jiang et al., “System Level Simulations on Increased Spatial Reuse,” Submission IEEE 802.11-14/372, Mar. 2014.
J. Kneckt et al., “Utilizing Unused Resources by Allowing Simultaneous Transmissions,” Submission IEEE 802.11-14/357, Mar. 2014.
G. Smith, “Dense Apartment Complex Throughput Calculations Channel Selection and DSC,” Submission IEEE 802.11-14/328, Mar. 2014.
G. Smith, “Dynamic Sensitivity Control Channel Selection and Legacy Sharing,” Submission IEEE 802.11-14/294, Mar. 2014.
J. Wang et al., “Spatial Reuse and Coexistence with Legacy Devices,” Submission IEEE 802.11-14/637, May 2014.
G. Smith, “Dynamic Sensitivity Control Implementation,” Submission IEEE 802.11-14/635, May 2014.
F. La Sita et al., “Residential Scenario CCA/TPC Simulation Discussion,” Submission IEEE 802.11-14/578, May 2014.
N. Jindal and R. Porat, “Performance Gains from CCA Optimization,” Submission IEEE 802.11-14/889, Jul. 2014.
J. Wang et al., “Increased Network Throughput with Channel Width Related CCA and Rules,” Submission IEEE 802.11-14/880, Jul. 2014.
S. Coffey et al., “A Protocol Framework for Dynamic CCA,” Submission IEEE 802.11-14/872, Jul. 2014.
J. Söder et al., “UL & DL DSC and TPC MAC simulations,” Submission IEEE 802.11-14/868, Jul. 2014.
S. Choudhury et al., “Impact of CCA adaptation on spatial reuse in dense residential scenario,” Submission IEEE 802.11-14/861, Jul. 2014.
B. Hart et al., “Evaluating Dynamic CCA/Receiver Sensitivity Algorithms,” Submission IEEE 802.11-14/856, Jul. 2014.
W. Carney et al., “DSC and Legacy Coexistence,” Submission IEEE 802.11-14/854, Jul. 2014.
J.-H. Son and J. S. Kwak, “Further Considerations on Enhanced CCA for 11ax,” Submission IEEE 802.11-14/847, Jul. 2014.
G. Barriac et al., “Changing CCA in the Residential Environment,” Submission IEEE 802.11-14/846, Jul. 2014.
F. La Sita et al., “Residential Scenario Sensitivity and Transmit Power Control Simulation Results,” Submission IEEE 802.11-14/833, Jul. 2014.
P.-K. Huang, “Performance Evaluation of OBSS Densification,” Submission IEEE 802.11-14/832, Jul. 2014.
G. Smith, “Dynamic Sensitivity Control Practical Usage,” Submission IEEE 802.11-14/779, Jul. 2014.
R. Hedayat et al., “Adaptive CCA for 11ax,” Submission IEEE 802.11-14/1233, Sep. 2014.
L. Jun et al., “Considerations on CCA for OBSS Opearation in 802.11ax,” Submission IEEE 802.11-14/1225, Sep. 2014.
B. Hart, “Link-Aware CCA,” Submission 802.11-14/1224, Sep. 2014.
G. Barriac et al., “Effect of CCA in residential scenario part 2,” Submission IEEE 802.11-14/1199, Sep. 2014.

## Slide 23: References (HEW & 802.11ax) 3
T. Itagaki et al., “DSC Simulation Results for Scenario 3,” Submission IEEE 802.11-14/1171, Sep. 2015.
R. Hedayat et al., “Considerations for Adaptive CCA,” Submission IEEE 802.11-14/1448, Nov. 2014.
H.-A. Safavi-Naeini et al., “Adapting CCA and Receiver Sensitivity,” Submission 802.11-14/1443, Nov. 2014.
J. Liu et al., “Considerations on OBSS Spatial Re-Use,” Submission 802.11-14/1435, Nov. 2014.
G. Wikström et al., “DSC Performance,” Submission 802.11-14/1427, Nov. 2014.
G. Wikström et al., “DSC and legacy coexistence,” Submission 802.11-14/1426, Nov. 2014.
C. Lukaszewski and L. Li, “Observed protocol violations caused by DSC with roaming STAs,” Submission IEEE 802.11-14/1416, Nov. 2014.
T. Itagaki et al., “Performance Analysis of BSS Color and DSC,” Submission IEEE 802.11-14/1403, Nov. 2014.
“DSC and Roaming,” G. Smith, “Dynamic Sensitivity Control Roaming,” Submission IEEE 802.11-15/25, Jan. 2015.
M. Shahwaiz Afaqui et al., “Simulation-based evaluation of DSC in residential scenario,” Submission IEEE 802.11-15/27, Jan. 2015.
T. Itagaki et al., “Performance Analysis of BSS Color and DSC,” Submission IEEE 802.11-15/45, Jan. 2015.
Y. Wang et al., “Modeling components impacting throughput gain from CCAT adjustment,” Submission IEEE 802.11-15/50, Jan. 2015.
J.-H. Son et al., “Legacy Fairness Issues of Enhanced CCA,” Submission IEEE 802.11-15/85, Jan. 2015.
S. Coffey et al., “Spatial Reuse AP Management,” Submission IEEE 802.11-15/105, Jan. 2015.
G. Wikström et al., “Potential of Modified Signal Detection Thresholds,” Submission 802.11-15/300, Mar. 2015.
A. Jafarian et al., “CCA Regime Evaluation Revisited,” Submission IEEE 802.11-15/318, Mar. 2015.
T. Itagaki et al., “Impact of TPC coupled to DSC for legacy unfairness issue,” Submission IEEE 802.11-15/319, Mar. 2015.
A. Kishida et al., “Discussions on the Definition of CCA Threshold,” Submission IEEE 802.11-15/338, Mar. 2015.
G. Barriac et al., “OBSS Preamble Detection,” Submission IEEE 802.11-15/367, Mar. 2015.
M. Shahwaiz Afaqui et al., “Proposal and simulation based evaluation of DSC-AP algorithm,” Submission IEEE 802.11-15/371, Mar. 2015.
J.-H. Son et al., “Further Considerations on Legacy Fairness with Enhanced CCA,” Submission IEEE 802.11-15/374, Mar. 2015
G. Smith, “TG ax Scenarios Proposed additions for frequency re-use,” Submission IEEE 802.11-15/543, May 2015.
G. Smith, “TG ax Enterprise Scenario and DSC,” Submission IEEE 802.11-15/548, May 2015.
A. Jafarian et al., “CCA Revisit,” Submission IEEE 802.11-15/588, May 2015.

## Slide 24: References (HEW & 802.11ax) 4
Y. Inoue et al., “Discussion on The Receiver Behavior for DSC/CCAC with BSS Color,” Submission IEEE 802.11-15/595, May 2015.
Y. Seok et al., “NAV Operation for Spatial Reuse,” Submission IEEE 802.11-15/797, Jul. 2015.
M. Mori et al., “DCCA/DSC Reference Simulation Results,” Submission IEEE 802.11-15/801, Jul. 2015.
G. Smith, “TG ax Outdoor Enterprise Scenario and DSC,” Submission IEEE 802.11-15/804, Jul. 2015.
G. Smith, “TG ax DSC Summary,” Submission IEEE 802.11-15/807, Jul. 2015.
X. Wang et al., “Topics for Consideration for Spatial Reuse,” Submission IEEE 802.11-15/811, Jul. 2015.
M. Shahwaiz Afaqui et al., “DSC leveraging uplink RTS/CTS control,” Submission IEEE 802.11-15/882, Jul. 2015.
Y. Inoue et al., “Follow up Discussion on The Receiver Behavior,” Submission IEEE 802.11-15/883, Jul. 2015.
C. Yu et al., “DSC Calibration Result,” Submission IEEE 802.11-15/886, Jul. 2015.
G. Smith, “E-Education Analysis HEW SG,” Submission IEEE 802.11-15/45, Jan. 2015.
G. Smith, “Airport Capacity Analysis,” Submission IEEE 802.11-13/1489, Jan. 2014.
G. Smith, “Dynamic Sensitivity Control Improvement to area throughput,” Submission IEEE 802.11-13/1012, Sep. 2013.
G. Smith, “Dynamic Sensitivity Control for HEW SG,” Submission IEEE 802.11-13/1290, Nov. 2013.
G. Smith, “Dense Apartment Complex Capacity Improvements with Channel selection and Dynamic Sensitivity Control,” Submission IEEE 802.11-13/1487, Nov. 2013.
I. Jamil et al., “MAC simulation results for Dynamic sensitivity control (DSC - CCA adaptation) and transmit power control (TPC),” Submission IEEE 802.11-14/523, May 2014.
M. Mori et al., “Reference Simulation Model for Dynamic CCA / DSC Calibration,” Submission IEEE 802.11-15/652, May 2015.
K. Odman, “802.11ax scenario 1 CCA,” Submission IEEE 802.11-15/357, Mar. 2015.
J.-H. Son et al., “Measurements on CCA Thresholds in OBSS Environment,” Submission IEEE 802.11-14/628, May 2014.
I. Jamil et al., “OBSS reuse mechanism which preserves fairness,” Submission IEEE 802.11-14/1207, Sep. 2014.
K. Odman, “802.11ax scenario 1 CCA,” Submission IEEE 802.11-15/332, Mar. 2015.

## Slide 25: References 5
M. Rison, “Resolutions for some comments on 11mc/D4.0 (SBmc1),” Submission IEEE 802.11-15/762, Aug. 2015.
O. Aboul-Magd, “TGax July 2015 Meeting Agenda,” Submission IEEE 802.11-15/735, Jul. 2015.
C. A. Rypinski, “Retrospective on Development of Radio and Wire Data Communication,” Submission IEEE 802.15-06/107, Mar. 2006.