## Slide 1: Simulation Scenarios for TGay PHY Layer Evaluation Methodology
Authors:
Name | Affiliation | Address | Phone | Email
Alexander Maltsev | Intel |  | +7(962)5050236 | alexander.maltsev@intel.com
Ilya Bolotin | Intel |  |  | 
Andrey Pudeyev | Intel |  |  | 
Artyom Lomayev | Intel |  |  | 

## Slide 2: Abstract
In this presentation the simulation scenarios for the TGay evaluation methodology document are introduced. The presentation includes legacy IEEE 802.11ad simulation scenarios with the proposal of their extension. Also the new proposed scenarios for access, device-to-device communication and backhauling are introduced.

## Slide 3: Agenda
NG60 use cases and channel scenarios
Legacy simulation scenarios and their extension for TGay PHY evaluation methodology
Proposed new simulation scenarios for TGay
References

## Slide 4: NG60 use cases summary [1]
# | Applications and Characteristics | Propagation conditions | Throughput | Topology
1 | Ultra Short Range (USR) Communications -Static,D2D, -Streaming/Downloading | LOS only, Indoor <10cm | ~10Gbps | P2P
2 | 8K UHD Wireless Transfer at Smart Home -Uncompressed 8K UHD Streaming | Indoor, LOS with small NLOS chance, <5m | >28Gbps | P2P
3 | Augmented Reality and Virtual Reality -Low Mobility, D2D -3D UHD streaming | Indoor, LOS/NLOS <10m | ~20Gbps | P2P
4 | Data Center NG60 Inter-Rack Connectivity -Indoor Backhaul with multi-hop* | Indoor, LOS only <10m | ~20Gbps | P2P P2MP
5 | Video/Mass-Data Distribution/Video on Demand System - Multicast Streaming/Downloading - Dense Hotspots | Indoor, LOS/NLOS <100m | >20Gbps | P2P P2MP
6 | Mobile Wi-Fi Offloading and Multi-Band Operation (low mobility ) -Multi-band/-Multi-RAT Hotspot operation | Indoor/Outdoor, LOS/NLOS <100m | >20Gbps | P2P P2MP
7 | Mobile Fronthauling | Outdoor, LOS <200m | ~20Gbps | P2P P2MP
8 | Wireless Backhauling with Single Hop -Small Cell Backhauling with single hop -Small Cell Backhauling with multi-hop | Outdoor, LOS <1km <150m | ~2Gbps | P2P P2MP
9 | Wireless office docking | Indoor LOS/NLOS < 3 m | ~13.2 Gbps | P2P P2MP

## Slide 5: Use cases vs. channel scenarios [2]
Use cases differ not only by environment, but also by throughput / latency / topology parameters, from the other hand, the same use cases may be realized in the different environments
Channel modeling scenario | Use cases | Channel modeling approaches, comments
Ultra-short range | 1 | Direct EM near-field calculation and measurements Los and device to device reflections – new approach needed
Living room | 2, 3 | IEEE 802.11ad model [3] as a base Enhancements: MIMO modes, Doppler and mobility effects, TX-Rx positions are changing
Data center | 4 | New static LOS scenario: Metallic constructions, ceiling reflections. No experimental data.
Enterprise/Mall/Exhibition Transportation | 5,9 | LOS/NLOS, frequent human blockage, multiple reflections IEEE 802.11ad models for cubicle and conference room. Experimental measurements and ray tracing simulations required for models development (analysis of METIS, AIRBUS data, etc.)
Open area (Access/Fronthaul/Backhaul) | 6,7,8 | Open area channel model in MiWEBA Q-D methodology [4-7] with extension to MIMO
Street canyon (Access/Fronthaul/Backhaul) | 6,7,8 | Street canyon channel model in MiWEBA Q-D methodology with extension to MIMO

## Slide 6: Legacy Simulation Scenarios in IEEE 802.11ad
The following indoor scenarios were considered in accordance with the developed 11ad evaluation methodology [8]:
  Conference room
  Home living room
  Enterprise cubicle
Home living room
Office conference room
Enterprise cubicle

## Slide 7: Extension of the legacy scenarios for TGay
Home living room (use cases 2,3)
  Use case 2: uplink SU-MIMO, channel bonding (TBD)
  Use case 3: downlink SU-MIMO, Doppler effects, blockage, channel bonding (TBD)
  LLS+SLS simulation results required
Conference room/Enterprise cubicle (use case 5, 9)
  SU-MIMO, channel bonding (TBD)
  Only LLS simulation results required

## Slide 8: Proposed New Simulation Scenarios for TGay PHY Evaluation Methodology
New proposed scenarios for TGay evaluation methodology :
  Access links:
    Indoor: large indoor area - hotel lobby (or shopping mall) (use case 5,6)
    Outdoor: open area (university campus), open air WiFi café (street canyon scenario) (use case 5, 6), mobile fronthauling with AP on the bus (use case 7)
  Backhaul links:
    Street canyon (lamppost mounting) (use case 8)
  D2D communication (use case 1)
    USR D2D

## Slide 9: Large indoor area - hotel lobby
The hotel lobby (indoor access large public area) simulation scenario represents typical indoor scenario: large hall with multiple users within.
The Hotel lobby access channel model from [5] with MIMO extension will be used
The SLS simulations required

## Slide 10: Outdoor open area hotspot access
The scenario represents large open areas with low and rare buildings like university campus, park areas, city squares.
Open area channel model from [5] with MIMO extension will be used.
The SLS simulations required.
To evaluate the range of possible mmWave system performance in different interference environments, two limiting cases are considered:
  “Isolated cell” In this case APs are dropped so rarely that we can neglect interference between them and estimate the mmWave network performance through simulating only single AP.
  “Dense deployment” In this opposite extreme case APs deployment has maximal density with the hexagonal structure and therefore the maximal inter-cell interference between APs is achieved.
Isolated cell
Dense hexagonal deployment

## Slide 11: Outdoor open area hotspot access
The APs are equipped with larger aperture antenna arrays. To increase the coverage area, the antenna arrays with a large number of elements (128 - 512) are considered.
Two options for the antenna array modeling may be implemented:
  Fully adaptive antenna array to evaluate the upper bound of possible performance
  Partially adaptive antenna array (subarray modules) with hybrid RF and BB beamforming
Considering the use of 3 directional antennas per AP:
  3 serving 1200 sectors
  3 frequency channels of 2.16 GHz channels
There are two options for frequency reuse:
  Frequency reuse-3. Each serving sector operates in only one of 3 channels.
  Frequency reuse-1. Each serving sector can operate in the whole band using all 3 channels

## Slide 12: Outdoor street canyon hotspot access
The street canyon (outdoor access ultra-high-rate hot-spots) simulation scenario represents typical urban scenario: city street with pedestrians’ sidewalks along the tall long buildings. The access link between the APs on the lampposts and the STAs at human hands is modeled in this scenario.
Street canyon channel model from [5] with MIMO extension will be used.
The SLS simulation results required.
Frequency reuse - 1,2,3 (TBD)

## Slide 13: Backhaul Scenario
Street canyon backhaul
  The street canyon backhaul model is derived from the street canyon access model by setting the RX antenna height equal to the AP height. The other parameters are not changed.
  Multi hop transmission with frequency reuse 1, 2, 3 (TBD).

## Slide 14: PHY Layer evaluation scenarios summary
Evaluation scenario | Use cases | Channel model scenario | Simulation level | Scenario codename | Interested Companies
USR D2D | 1 | LOS SU-MIMO | LLS | “Ultra short” | Panasonic…
Home living room (VR D2D included) | 2, 3 | 11ad with SU-MIMO extension | LLS | “HD TV” and “Dancing girl” | Intel, …
Conference room | 5 | 11ad with SU-MIMO extension | LLS | “Conference room” | …
Enterprise cubicle (docking included) | 5,9 | 11ad with SU-MIMO extension | LLS | “Docking station” | Intel, …
Hotel lobby | 5 | MiWEBA Hotel Lobby with MIMO extension | SLS | “Hotel lobby” | …
Outdoor open area hotspot access | 5,6,7 | MiWEBA Open area with MU-MIMO extension | SLS | “University campus” | Intel, …
Outdoor street canyon hotspot access | 5,6,7 | MiWEBA Street canyon with MU-MIMO extension | SLS | “Street canyon” | Intel, …
Street canyon backhauling | 8 | MiWEBA Street canyon | LLS | “Street canyon backhauling” | Intel, …

## Slide 15: References
“IEEE 802.11 TGay Use Cases”, https://mentor.ieee.org/802.11/dcn/15/11-15-0625-02-00ay-ieee-802-11-tgay-usage-scenarios.pptx
“NG60 channel modeling plan” https://mentor.ieee.org/802.11/dcn/15/11-15-0614-01-00ay-ng60-channel-modeling-plan.pptx
"Channel Models for 60 GHz WLAN Systems," IEEE 802.11ad 09/0334r8, 2010.
MiWEBA Project #608637 homepage: http://www.miweba.eu, FP7-ICT-2013-EU-Japan, 2013
MiWEBA project #608637, ‘Deliverable D5.1, Channel Modeling and Characterization’, Public Deliverable, Intel Editor, June 2014.
“Channel models for NG60”, http://mentor.ieee.org/802.11/dcn/14/11-14-1486-00-ng60-channel-models-in-ng60.pptx
A. Maltsev, A. Pudeyev, I. Karls, I. Bolotin, G. Morozov , R.J. Weiler, M. Peter, W. Keusgen “Quasi-deterministic Approach to mmWave Channel Modeling in a Non-stationary Environment”, IEEE GLOBECOM 2014, Austin, Texas, USA
doc.: IEEE 802.11-09/0296r16, “TGad Evaluation Methodology,” Eldad Perahia, January 2009.
“MU-MIMO-schemes for NG60”, http://mentor.ieee.org/802.11/dcn/15/11-15-0356-00-ng60-mu-mimo-schemes-for-ng60.pptx
A. Maltsev, A. Sadri, A. Pudeyev, A. Davydov, I. Bolotin, G. Morozov, “Performance evaluation of the MmWave Small Cells communication system in MU-MIMO mode”, EuCNC’2015