## Slide 1: Use of TG ax Scenarios for Spatial Reuse
Date: 2015- Nov
Authors:

## Slide 2: Background
Present scenario details do not include channel allocations that allow spatial re-use technologies to be fully evaluated
  The channel allocations are fixed in the simulation scenarios
  Spatial reuse technologies are tending to be assessed using the existing scenarios
This presentation proposes how to adjust the scenarios such that technologies that attempt to improve spatial reuse can be better simulated and evaluated
  DSC, Color, TPC, etc
Does not propose any changes to the Simulation Documents, BUT proposes (common) scenario conditions such that spatial reuse can be assessed.

## Slide 3: Channel Re-use
A basic aim of the Spatial Reuse sub TG is basically to increase the channel reuse across an area and hence increase the total throughput of that area.
Hence, some of the factors that are important are:
  The area size
    The more possibility of channel reuse
  The number of available channels
    Allocated in managed networks
    Random selection or intelligent selection in unmanaged networks
    20, 40MHz, 80MHz.
    Adaption and sharing

## Slide 4: Channel Allocations – 5GHz
Ref:Wikipedia
Spatial re-use schemes can take advantage of the use of multiple channels.

## Slide 5: Proposed Methodology for SR
Take existing Simulation Scenario THEN
Vary the channel allocations
  20, 40, 80MHz channels
Apply each SR technology
See effect on throughputs, etc. compared to legacy

## Slide 6: Apartment Sharing – 14/0328r2
Unmanaged scenario
Intelligent or random allocation of channels makes huge difference
Using DSC predicts no OBSS with 6-10 channels and intelligent selection
- is this true?

## Slide 7: Proposed SR variations for Residential Scenario
Operating channels:
Proposed Scenarios for SR
A - 5GHz: random assignment of channels
  Random selection of primary channel per operating channel
  4 80MHz channels
  (6), 9, 10 40 MHz non-overlapping channels,
B - 5GHz: Intelligent assignment of channels
  Intelligent selection entails looking for free channel then only if no free channel available, select one already in use.
  4 80MHz channels
  (6), 9, 10 40 MHz non-overlapping channels,
NOTE: Alternative is to fix the allocations (intelligently) thus allowing less variation in simulations

## Slide 8: Possible fixed channel allocations
4 Ch
6 Ch
9 Ch
10 Ch

## Slide 9: Enterprise Scenario
1 | 2 | 1 | 2 | 1 | 2 | 1 | 2
3 | 4 | 3 | 4 | 3 | 4 | 3 | 4
1 | 2 | 1 | 2 | 1 | 2 | 1 | 2
3 | 4 | 3 | 4 | 3 | 4 | 3 | 4
Present scenario
Four 80MHz channels
Legacy total OBSS 4-6 overlaps
DSC Approx 30% STA overlap
No AP overlap
1 | 2 | 3 | 1 | 2 | 3 | 1 | 2
4 | 5 | 6 | 4 | 5 | 6 | 4 | 5
7 | 8 | 9 | 7 | 8 | 9 | 7 | 8
1 | 2 | 3 | 1 | 2 | 3 | 1 | 2
Alternative
Nine 40MHz channels
Legacy All STAs & APs overlap
DSC No overlap
How does Throughput compare
With 4 x 80 channels

## Slide 10: Enterprise Scenario
Enterprise Scenario
Channel allocation
5GHz:
A - Four 80 MHz channels (Ch1, Ch2, Ch3, Ch4)
The channel distribution can be:
Ch1: BSS 4k-3
Ch2: BSS 4k-2
Ch3: BSS 4k-1
Ch4: BSS 4k
k=1~8, is the office index.
B - Nine 40MHz channels arranged across the 8 Offices as shown below:
1 | 2 | 3 | 1 | 2 | 3 | 1 | 2
4 | 5 | 6 | 4 | 5 | 6 | 4 | 5
7 | 8 | 9 | 7 | 8 | 9 | 7 | 8
1 | 2 | 3 | 1 | 2 | 3 | 1 | 2

## Slide 11: Indoor Small Scenario
Channel reuse 7.
Layout of BSSs channel allocations in case of 7 channel reuse.
Add Reuse 7 and wall loss.
With 10m cell radius and a topology of 180m across, the assumption of no obstruction losses is not realistic.
(people, walls, desks, furniture, etc.)
It is proposed that a simple wall loss for each cell wall should be added

## Slide 12: Indoor Small Scenario – reuse 7
STAs are placed randomly (uniform distribution) within the 61 cell area that covers the reuse 7 pattern. STA identifies which (of the 61) APs from which it receives the highest power (based on distance-based pathloss and shadowing). If the corresponding AP does not yet have N1 STAs associated to it, then STA associates to it; else STA is removed from the simulation. This process is repeated until each of the co-channel APs has exactly N1 STAs associated to it.
Channel Model
PL(d) = 40.05 + 20*log10(fc/2.4) + 20*log10(min(d,10)) + (d>10) * 35*log10(d/10) + 7*W Note: could use 3*W in place of 7
d = max(3D-distance [m], 1)
fc = frequency [GHz]
W = number of cell walls traversed
Primary Channels
5GHz:
40 MHz BSS
Per each 40MHz use same primary channel across BSSs

## Slide 13: Outdoor Large BSS scenario
Outdoor Large BSS Scenario
Center Frequency, BW and primary channels
Similar to indoor scenario
5GHz
[Same Primary channel]
BSSs use 40MHz channels with reuse 7

## Slide 14: Summary
There are 21 x 20MHz, 10 x 80MHz and 4 x 80 MHz channels in the USA for example, let’s use them!
The purpose of the Spatial reuse technologies is to allow better use of available channels over the areas of interest. If using 10 x 40MHz channels with SR technology provides better throughput than 10 x 40MHz channels legacy, or indeed 4 x 80MHz channels, then that is what we need to know
The basis for 11ax is to get a throughput increase across an area
The present Simulations Scenarios have fixed channel allocations BUT SR needs to evaluate SR use!
Hence, let’s see what happens when we apply SR techniques – let the channels vary! – get closer to reality – maybe we will see the magic 4 x improvement

## Slide 15: Straw Poll
Do you agree that when evaluating Spatial Reuse technologies the channel allocations should be allowed to be varied along the lines indicated in this document, rather than only use the fixed assignments as specified in the Simulation Document?
Y/N/A