## Slide 1: Report on 3GPP 5G Workshop Sept. 17-18 2015, Phoenix AZ
Date: 2015-11-11
Authors:

## Slide 2: Abstract
This report provides some 3GPP background and a summary of the 3GPP RAN 5G Workshop discussions, that I believe would be of interest to 802.11. Also provided are links to all of the 3GPP 5G Workshop contributions, reports and summaries. 3GPP like 802 is contributions driven.

## Slide 3: Outline
Workshop Overview
3GPP Overview
3GPP 5G Workshop Chairman’s Summary
Workshop Contributions Summary:
  Status of IMT 2020
  Inputs from other Organizations
  Status of SMARTER SI (SA1)
  Contributions from 3GPP Members
  Synthesis Documents (multi-member contributions)
  Selected “Typical” Slides from the Contributions
References

## Slide 4: Workshop Overview
3GPP RAN kicked off its development of the next generation 3GPP cellular technology with this workshop. {Similar workshops were held for LTE (4G) and UMTS (3G)}
The Workshop was held in Phoenix, AZ, USA on September 17-18 2015. There were 550 participates from 159 organisations and 90 contributed documents.
The Workshop was Chaired by the 3GPP RAN Chair Dino Flore (Qualcomm), at the close of the meeting he provided a summary of the Workshop [1].
All workshop documents are available: 5G Workshop Documents

## Slide 5: Just for background: Who are 3GPP
3GPP is: “The 3rd Generation Partnership Project”
It unites seven telecommunications standards development organizations (ARIB, ATIS, CCSA, ETSI, TSDSI, TTA and TTC), the organizational partners.
3GPP has four Technical Specification Groups:
  Radio Access Networks (RAN)
  Service & Systems Aspects (SA)
  Core Network & Terminals (CT)
  GSM EDGE Radio Access networks (GERAN)
These groups have Working Groups and are responsible for developing reports and specifications.
These specifications define the Cellular Phone System

## Slide 6: Differences between 3GPP and 802
3GPP is a company based organization
  Corporate members pay a fee to join 3GPP
  Corporate members have a vote, individuals do not
  Meetings are sponsored by Corporate members
Decisions are made by consensus
  Voting on technical issues is rare in 3GPP, because there is a heavy emphasis on reaching consensus
  Consensus is defined as the absence of sustained opposition
Work is accomplished by:
  Delegate empowerment (compromise/consensus is often found by delegate to delegate offline discussion)
  Voluntarism (delegates take on various leadership tasks)
  Distributed decision making (most decision are made in WGs)

## Slide 7: From the Chairman’s Summary [1](RWS-150073)
The starting point of the 5G activity is the “5G” timeline [2](SP-150149)
  This timeline considers the ITU-R agreed workplan for IMT 2020
  Submissions to ITU-R will be made by RAN as in the timeline
  This work: 5G development is to provide solutions for IMT 2020
  3GPP will use a phased multi release plan to achieve 5G.
High Level Use Cases:
  Enhanced Mobile Broadband
  Massive Machine Type Communications
  Ultra-Reliable and Low Latency Communications
Supporting New Services:
  Automotive, Health, Energy, Manufacturing… (SA1 SMARTER project)

## Slide 8: From the Chairman’s Summary (cont.)
Focus of 5G Study Item (SI)
A New Radio
  LTE evolution continues in parallel
  New radio requirements and scope will be defined in the SI
  A Channel model for high frequencies is in development
The 5G System Architecture will be discussed
Interworking of the New Radio and legacy systems
  Next Steps for RAN
  Identify status and expectations on high frequencies
  Approve SI in December
  Approve RAN WF SI to evaluate technologies in March
  Companies should work towards convergence on outstanding items
The WS Agenda [3] and Report [4] are also available

## Slide 9: Status of IMT 2020
The status of the ITU-R Work on IMT-2020 for 5G, reported by Stephen Blust, Chairman of ITU-R Working Party 5D (RWS-150082)
Synopsis:
Working Party 5D has developed an overarching and coordinated plan
Continues the Partnership with industry as the success model for 5G
Much foundation work has already been completed
A lot of work is still required
Next steps are to define the radio interface technology minimum performance requirements and evaluation details

## Slide 10: Inputs from other Organizations
Alliance for Telecommunications Industry Solutions (ATIS) (RWS-150021)
5G Forum (Korea) (RWS-150055)
IMT2020 (5G) Promotion Group (China) (RWS-150050)
5GMF (Japan) (RWS-150081)
TAICS (Taiwan) (RWS-150059)
5G-PPP (EU) (RWS-150007)
COHERENT (5G-PPP project) (RWS-150086)
METIS (METIS was a EU FP7 project, METIS II is an EU 5G-PPP project (RWS-150070)
NGMN (Next Generation Mobile Networks) (RWS-150088)
Small Cell Forum (RWS-150071)
TSDSI (India) (RWS-150060)
Theses Organizations provided their views on 5G:
How they see 5G developing
What they see 5G addressing: use cases, requirements, needs, spectrum, legacy support
What they are working on to provide solutions for 5G

## Slide 11: Status of SMARTER SI (SA1 - Services)
The progress and content of 3GPP SA1 5G study item was reported by Toon Norp (KPN) the SA1 Chair and Adrian Neal (Vodafone) the SI Rapporteur (RWS-150032)
Summary:
More extreme connection density, data rate, capacity being considered for the wide area NW, often in conjunction with one another
New localised, isolated types of 3GPP access.
Many different flavours of access NW according to market requirements
But…Still in informative phase and RAN performance requirements largely unvalidated

## Slide 12: Contributions from 3GPP Members
51 – Presentations by individual members companies
3 - Views on the way forward by 3 groups of Companies (45)
Most of the contributions were variations on the same theme.
There is basically a consensus that:
  There will be radios <6 GHz and >6 GHz
  There will be a backwards compatible RAT – LTE Evolution
  There will be a non-Backwards compatible RAT – 5G New RAT
  Dynamic/flexible duplex: FDD and TDD modes
  5G will do everything for everyone

## Slide 13: Technology Areas from Contributions (this is not a complete list)
Massive MIMO (>64 antennas)/Beamforming
Unlicensed Access (LAA)
Ultra Dense Network (UDN) / Massive MTC / multi-layer NW
  UE Centric No Cell Radio Access (UCNC), cell virtualization,
  Flexible backhaul/fronthaul
  Small cells
  New Codes (Polar Code, LDPC)
New Multiple Access (Orthogonal and Non-Orthogonal)
  Pattern Division MA (PDMA), Full Duplex, Sparse Code MA (SCMA)
New Waveforms (QAM-FBMC, FQAM)
mm Wave (6GHz-100GHz, >10 Gbps, 10Tbps/km2)
Low Latency (1ms over the air)
UE collaboration (Mesh, Relay, D2D, eD2D)
Enhanced Carrier Aggregation (CA), Cellular/Wi-Fi Integration
RAN virtualization, Network Function virtualization (NFV)-Network Slicing

## Slide 14: Synthesis Documents (multi-member contributions)
3 joint way forward documents were provided by: 45 member companies joining together in 3 groups:
Industry Vision and Schedule for the New Radio Part of the Next Generation Radio Technology (RWS-150036) (Nokia Networks, Ericsson, Qualcomm, NTT DOCOMO, Samsung, SK-Telecom, Sony, Intel, KT, Panasonic, Verizon, Softbank, Kyocera, Mitsubishi, Sumitomo Electric, Hitachi, NEC, Fujitsu, Sharp, ETRI, Straight Path Communications, KDDI, InterDigital)
Views on 5G New RAT in 3GPP (RWS-150085) (CATR, CATT, CMCC, China Telecom, China Unicom, Coolpad, Hi-Silicon, Huawei, OPPO, Potevio, ZTE Alcatel-Lucent, Alcatel Lucent Shanghai Bell)
Group of operators’ common vision and priorities for Next Generation Radio Technology (RWS-150090) (Orange, Deutsche Telekom, Telefonica, Telecom Italia, KPN, Telenor, Telia Sonera, Telus, Swisscom, Dish Network)

## Slide 15
Note:
The following are slides taken from workshop contributions, all the contributions are publically available [5].
These slides were chosen to illustrate some of the perspectives shared at the workshop, that I thought were interesting. Note: they are taken out of context of their presentations.
These slides do not represent a consensus of the workshop, nor do they necessarily represent my views.
  Selected “Typical” Slides from the Contributions

## Slide 16
From: RWS-150036

## Slide 17
From: RWS-150085
These Items not agreed in 3GPP

## Slide 18
From: RWS-150090

## Slide 19
From: RWS-150029

## Slide 20
From: RWS-150010
MAC: Medium Access Control
PHY: Physical Layer
RF: Radio Frequency Layer
BTS: Base Transceiver Station
RRC: Radio Resource Control
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Control
Key:

## Slide 21: References
RAN workshop on 5G:Chairman Summary, Dino Flore, TGS-RAN Chairman RWS-150073
“5G” timeline in 3GPP, Dino Flore, TGS-RAN Chairman; Balaza Bertenyi, TGS-SA Chairman, SP-150149
Agenda for 3GPP RAN Workshop on 5G RWS-150001
Report on: 3GPP RAN workshop on 5G (includes report, participants list, and Tdoc list) RWS-150076
All documents (Tdocs) from 3GPP RAN Workshop on 5G, and those noted in this report: RWS-1500xx can be found: Docs