## Slide 1: Simulation results for spatial reuse in 11ax
Date: 2015-11-09
Authors:
Jinmin Kim, LG Electronics

## Slide 2: Abstract
In this contribution, we observe the performance of static OBSS PD level and transmit power control in the integrated(PHY+MAC) simulation

## Slide 3: Spatial Reuse Schemes
Static OBSS PD level
  To apply a fixed OBSS PD level after BSS COLOR filtering
    OBSS PD level : -76(RX sensitivity in 80MHz), -71, -66, -61, -56dBm
Transmit power control (TPC)
  To change transmit power based on path-loss
    Case A. TPC is applied to both AP and STA
    Case B. TPC is only applied to STA
  Detail is explained in slide.#16

## Slide 4: Simulation Scenario
Simplified residential scenario (SS1)
  Considering only 1st floor in SS1
  80MHz BSS at 5GHz
  20 APs and 10 STAs per AP
  A CBR traffic model, which is heavier than [1], is considered
    DL: 100Mbps per BSS (cf. 60Mbps in [1])
    UL: 10Mbps per BSS (cf. 6Mbps in [1])
  Each BSS randomly selects a channel among 3 channels

## Slide 5: PHY/MAC-Integrated Simulation Parameter
Simulation Time | 10s (+initial 1s)
Number of Drops | 10
Default Tx Power (AP/STA) | 20/15dBm
Default Rx Sensitivity | -76dBm(80MHz)
CCA-ED | -56dBm(80MHz)
Antenna Gain (AP/STA) | 0/-2 dBi
Channel | TGn Channel D (pathloss, fading)
Noise Figure | 7dB
Noise Floor | -101dBm per 20MHz
Rate Control Algorithm | 10 % PER based MCS selection [2]
Feedback | GENIE
MSDU size (bytes) | 1472
Max Aggregation number | 64
Max Retransmission | 10
Metrics | Throughput, SIR, # of DL/UL transmission1)
RTS/CTS | off
1) Total # of DL/UL transmission per AP/STA through the whole simulation time, respectively

## Slide 6: Classification of BSSs
According to the received interference level
  Category I: high interference by the same channel nearby
  Category II: medium interference by the same channel one BSS away
  Category III: low interference by the same channel two BSS away

## Slide 7: Static OBSS PD level

## Slide 8: Simulation Result - Static OBSS PD level (1/7)
5% Tput gain when OBSS PD level is increased to -56dBm
Observation point:
When OBSS PD level gets higher, performance is slightly improved since categories II&III do not provide gains
- see the following slides
5% gain
DL offered rate
UL offered rate
Increasing

## Slide 9: Simulation Result - Static OBSS PD level (2/7)
Result on Category I (high interference case)
  12% throughput gain when OBSS PD level is -56dBm
Observation point:
Performance gain gets higher when OBSS PD level increases
- reason in the following slide
Increasing
12% gain
DL offered rate
UL offered rate

## Slide 10: Simulation Result - Static OBSS PD level (3/7)
Analysis on Category I (high interference case)
Observation point:
The increased number of transmission can cover up the decreased SIR when OBSS PD level gets higher.
Slightly
Decreasing
Increasing
Increasing
Slightly
Decreasing
1) Total # of DL transmission per AP through the whole simulation time
1)

## Slide 11: Simulation Result - Static OBSS PD level (4/7)
Result on Category II (medium interference case)
  Throughput gain is not observed
Observation point:
Even if performance is higher than category I, throughput gain is not observed
So, no gain in category II makes large impact on the small gain of overall performance
DL offered rate
UL offered rate

## Slide 12: Simulation Result - Static OBSS PD level (5/7)
Analysis on Category II (medium interference case)
Observation point:
SIR and the number of transmission do not get better when OBSS PD level increase.

## Slide 13: Simulation Result - Static OBSS PD level (6/7)
Result on Category III (low interference case)
  Throughput gain is not observed
Observation point:
Throughput gain is not observed
As mentioned in previous slide, no gain in category III makes the largest impact on the small gain of overall performance
DL offered rate
UL offered rate

## Slide 14: Simulation Result - Static OBSS PD level (7/7)
Analysis on Category III (low interference case)
Observation point:
As mentioned in category II, SIR and the number of transmission do not get better when OBSS PD level increase.

## Slide 15: TPC (Case a. TPC is applied to both AP and STA)

## Slide 16: TPC algorithm
TPC is modified from [1] for 80MHz BW
  Updated TxPower = max(LowerLimitationLevel, RX sensitivity + TPC Margin + Estimated Path Loss)
    TPC margin : 20, 25dB
    LowerLimitationLevel : -56dBm
    Max Updated TxPower : 20dBm

## Slide 17: Simulation Result (Case a. TPC is applied to AP&STA)
There is no performance gain when TPC is applied to both AP and STA
Observation point:
When TPC is applied to AP&STA, throughput gain is not observed since all categories do not provide gains
- see the following slides
DL offered rate
UL offered rate

## Slide 18: Simulation Result (Case a. TPC is applied to AP&STA)
Result on Category I (high interference case)
  Throughput gain is not observed
DL offered rate
UL offered rate
Observation point:
throughput gain is not observed
- reason in the following slide

## Slide 19: Simulation Result (Case a. TPC is applied to AP&STA)
Analysis on Category I (high interference case)
Observation point:
The increased number of DL transmission compensates barely for the loss by decreased SIR and decreased number of UL transmission
Decreasing
Increasing
Decreasing
Decreasing

## Slide 20: Simulation Result (Case a. TPC is applied to AP&STA)
Result on Category II (medium interference case)
  Throughput gain is not observed
DL offered rate
UL offered rate
Observation point:
Even if performance is higher than category I, throughput gain is not observed
The reason of this trend is same as category I

## Slide 21: Simulation Result (Case a. TPC is applied to AP&STA)
Result on Category III (low interference case)
  Throughput gain is not observed
DL offered rate
UL offered rate
Observation point:
Even if performance is higher than category II, throughput gain is not observed
The throughput of DL/UL corresponds to the offered data rate(100/10Mbps)

## Slide 22: TPC (Case b. TPC is only applied to STA not AP)

## Slide 23: Simulation Result (Case b. TPC is only applied to STA not AP)
30% throughput gain when TPC margin is 20dB
30% gain
DL offered rate
UL offered rate
20% gain
Observation point:
When TPC is applied to only STA, performance is improved
- see the following slides

## Slide 24: Simulation Result (Case b. TPC is only applied to STA not AP)
Result on Category I (high interference case)
  66% throughput gain when TPC margin is 20dB
66% gain
DL offered rate
UL offered rate
44% gain
Observation point:
The DL performance is significantly improved when TPC is applied to only STA
- reason in the following slide

## Slide 25: Simulation Result (Case b. TPC is only applied to STA not AP)
Analysis on Category I (high interference case)
Observation point:
The increased DL SIR and increased number of DL transmission makes the performance gain. So, DL performance can be enhanced significantly.
Increasing
Increasing
Decreasing

## Slide 26: Simulation Result (Case b. TPC is only applied to STA not AP)
Result on Category II (medium interference case)
  12% throughput gain when TPC margin is 20dB
12% gain
DL offered rate
UL offered rate
8% gain
Observation point:
The reason of this trend is same as category I

## Slide 27: Simulation Result (Case b. TPC is only applied to STA not AP)
Result on Category III (low interference case)
  Throughput gain is not observed
DL offered rate
UL offered rate
Observation point:
Even if performance is higher than category II, throughput gain is not observed
The throughput of DL/UL corresponds to the offered data rate(100/10Mbps)

## Slide 28: Conclusion
We simulated 2 spatial reuse schemes
  Static OBSS PD level, TPC
Considering static OBSS PD level, the performance can be enhanced slightly
  This gain is derived from increased number of transmissions (enhanced Tx opportunity)
  Performance gain can be dependent on traffic model. So, we will simulate with other traffic model for the future work
If TPC is applied to STA, performance can be enhanced significantly by reduced OBSS UL interference and increased number of DL transmissions

## Slide 29: Reference
[1] 11-15/10415r0 Dynamic CCA control and TPC Simulation Results with SS1~SS3
[2] 11-14/620r0 link adaptation for PHY SLS calibration

## Slide 30: Appendix A: Selected Channel Index
2 | 2 | 1 | 2 | 1 | 1 | 2 | 1 | 0 | 2
1 | 1 | 2 | 1 | 1 | 0 | 1 | 2 | 0 | 0
0Drop
2 | 2 | 2 | 0 | 2 | 1 | 2 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 2 | 2
1Drop
2 | 1 | 0 | 2 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 2 | 0 | 1 | 1 | 1 | 1 | 2 | 1
2Drop
0 | 0 | 2 | 0 | 2 | 0 | 0 | 0 | 1 | 2
0 | 1 | 1 | 1 | 0 | 0 | 1 | 2 | 1 | 1
3Drop
0 | 0 | 0 | 2 | 2 | 0 | 0 | 1 | 2 | 0
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0
4Drop
1 | 2 | 1 | 0 | 1 | 2 | 0 | 2 | 1 | 2
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 2
1 | 1 | 2 | 2 | 2 | 2 | 0 | 1 | 0 | 2
1 | 2 | 1 | 0 | 1 | 0 | 1 | 2 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1 | 2 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 0
2 | 0 | 2 | 1 | 1 | 0 | 1 | 1 | 1 | 0
0 | 2 | 0 | 2 | 1 | 2 | 0 | 1 | 1 | 2
2 | 2 | 0 | 0 | 2 | 0 | 1 | 0 | 2 | 1
0 | 1 | 2 | 0 | 1 | 0 | 0 | 2 | 1 | 2
5Drop
6Drop
7Drop
8Drop
9Drop
Low interference case
Medium
interference case
High interference case