## Slide 1
DL MU Transmission Sequence
Date: 2015-11-09
Authors:

## Slide 2: Background
During July meeting, TGax accepted several new features such as
  Cascaded DL/UL MU transmission
  Unicast/Broadcast Trigger frame for UL MU transmission
However, several UL MU transmission procedures in current SFD text are not clearly defined when we consider those new features.
In this document, we want to extend currently accepted UL MU transmission feature to cascaded DL and UL MU transmission cases.

## Slide 3: Trigger Frame Transmission
Current SFD says:
  An UL OFDMA MPDU/A-MPDU is the acknowledgement of the trigger frame. When the AP receives MPDU correctly from at least one STA indicated by trigger frame, the frame exchange initiated by the trigger frame is successful.
Primary 20MHz channel.
STA2 A-MPDU to AP
TXOP
Backoff
DL
UL
STA3 A-MPDU to AP
STA0 A-MPDU to AP
STA1 A-MPDU to AP
Multi-STABA
Multi-STA BA
Multi-STA BA
Trigger
Trigger
40MHz

## Slide 4: Trigger Frame Transmission
The intention is as long as there’s any response frame following the Trigger frame, the Trigger frame transmission is considered to be success.
However, as TGax allows multiple Trigger frames to be transmitted simultaneously in DL MU manner, we may need to define “response frame” for Trigger frame more clearly.
As long as there’s any response frame regardless of the number of Trigger frames transmitted simultaneously, the Trigger frame transmission should be considered to be success.

## Slide 5: Trigger Frame Transmission
Operation Example:
  AP schedules STA1/STA2/STA3 for UL MU transmission.
  But, only STA2 receives the Trigger frame correctly.
  Case 1: Use of Broadcast Trigger frame only
  Case 2: Simultaneous transmission of Unicast/Broadcast Trigger frame
CASE 1: Transmission success
CASE 2: Transmission failure for TRIG1

## Slide 6: Trigger Frame Transmission
In principle, current UL MU transmission success can be extended to:
  When the AP receives MPDU correctly from at least one STA indicated by any trigger frame, the frame exchange initiated by all trigger frame(s) is successful.
As this modified sequence happens when more than one Trigger frame is sent simultaneously in DL MU transmission manner, the same principle can also be stretched to transmission success for DL MU transmission.

## Slide 7: DL MU Transmission
Operation cases for DL MU transmission that solicits more than one UL PPDU as immediate response:
  DL Data (with no immediate ACK/BA) and a Trigger frame
    Same rule applies to current SFD:
    When the AP receives MPDU correctly from at least one STA indicated by a trigger frame in a DL MU transmission, the frame exchange initiated by the DL MU transmission is successful.

## Slide 8: DL MU Transmission
  More than one Trigger frames
    Similar rule applies to current SFD:
    When the AP receives MPDU correctly from at least one STA indicated by any trigger frame in a DL MU transmission, the frame exchange initiated by the DL MU transmission is successful.

## Slide 9: DL MU Transmission
Regardless of the number of Trigger frames in a DL MU transmission, similar rule can be applied in deciding transmission success of the DL MU transmission:
  When an AP initiates a DL MU transmission, the DL MU transmission is successful if the AP receives MPDU correctly from at least one STA indicated by any trigger frame in the DL MU transmission.

## Slide 10: Summary
We suggest to extend current SFD text on Trigger frame transmission success to DL MU transmission case as it shares the same principle.

## Slide 11: Straw Poll
Do you agree to add to the TG Specification Framework:
  4.y.z When an AP initiates a DL MU transmission soliciting more than one immediate response frames, the DL MU transmission is successful if the AP receives the response frame correctly from at least one STA indicated by any trigger information in the DL MU transmission.

## Slide 12: References
[1] 11-15-0132r9, “Specification Framework for TGax"