## Slide 1: LTF Sequence Designs
Date: 2015-11-09
Authors:

## Slide 2: Introduction
As shown in [1], there are two design approaches; 1) full-band design and 2) per-subband design
The per-subband design guarantees better PAPRs than the full-band design, and it is a natural way which is similar to HT and VHT designs
In this contribution, we propose detailed methods to construct LTF sequences in the per-subband design, and proposes LTF sequences for OFDMA and OFDM

## Slide 3: Sequence Design Structure
Full-band design
  Design a LTF sequence in 20, 40, or 80MHz, and chop it up depending on the STA’s allocated subband
  Less sets of LTF sequences and simple LTF receiving procedure
  But, not optimized PAPR for subband in UL OFDMA
Per-subband design
  LTF sequence design for each subband size, e.g., 26RU, 52RU, and etc.
  More optimized PAPR performance in subband
1, -1, 1, ..0, 0, 0, …,1, -1,1
A LTF sequence designed in 20MHz
1,.,1
1, …,1
1,.,1
26RU
26RU
52RU
Same length but different sequence, i.e., different PAPRs
1,.,1
1, …,1
1, -1, …,-1, 1
1, -1, 1, ..0, 0, 0, …,1, -1,1
106RU
52RU
26RU.
242RU
LTF sequences designed for every possible subband sizes
Chop up the base seq. depending on subband sizes and positions
Choose one depending on subband sizes
…

## Slide 4: PAPR Analysis of Full-Band Design
Distribution of maximum PAPR of any 26, 52, 106, or 242 RUs when LTF sequence for 26, 52, and106 RUs use a “direct” subset of the LTF sequence of the 242 RU.
The search space for a optimal LTF sequence of length 242 that has good subset PAPR properties is 2242 = 7x1072. (Modern computers with good algorithms can number crunch 105 ~ 106 sequences per hour. At this rate we will need 1063 years of search for finding the optimal solution)
242 LTF sequence
52
26
106
LTF sequence of 26 RU
LTF sequence of 26 RU
LTF sequence of 106 RU
Finding max PAPR to be smaller than 7.5 dB is astronomically difficult (if not impossible)
Reasonable PAPRs couldn’t be achieved with the full-band design

## Slide 5: Extensions for Per-Suband Design
The per-subband design is more preferred in terms of PAPR optimization
As designed in previous 11’s, a longer sequence can be constructed from combinations of blocks of shorter sequences
    Adding one or two tones at the end or beginning of a design sequence doesn’t significantly destroy the designed PAPR
A phase rotation can be considered when four duplicated sequence block is used
  With four duplicated sequence blocks, a phase rotation of [1, -1, -1, -1] can gives good PAPR (Appendix A)
    Difference with other combinations are marginal
  A phase rotation of two blocks doesn’t provide much gain, as seen in L-STF and L-LTF in 40MHz
    E.g., L-STF and L-LTF PAPRs of 40MHz are larger than those of 80MHz

## Slide 6: Pilot Considerations for LTF Seq. Design
P matrix and pilot positions change the designed PAPRs
  P matrix changes LTF sequences every symbol except ones in pilot positions, and it causes different PAPRs
    P matrix has six different values : 1, exp(-j2π·1/6), exp(-j2π·2/6), exp(-j2π·3/6), exp(-j2π·4/6), exp(-j2π·5/6)
  The same size RUs can have different relative pilot positions depending on the RU positions [2]
    E.g., 26RU has three pilot positions depending on RU locations
Therefore, the designed sequence should be verified if it has sill low PAPRs in other pilot positions and P matrix values
26
6th
19th
26
7th
21th
Pilot Position 1
Pilot Position 2
<Three pilot positions in case of 26RU>
13+7dc+13
Pilot Position 3
7th
27th

## Slide 7: LTF Sequences in HELTF
Based on the numerology[2], nine sizes of 4xLTF should be defined
  OFDMA : 26RU, 26RUc (center block), 52RU, 106RU, 242RU, 484RU
  OFDM : 242SU (242+3 DCs), 484SU (484+5 DCs), 996SU (996+5 DCs)
In 2xLTF,
  If a designed half-sized sequence exists, it could be reused for 2xLTF, which guarantees the similar PAPR as designed
  For the center 26RU and 242SU, sequences of the lengths 14 and 122 are needed, respectively due to tone mappings [1]
{a, b, c, …,z}
{a, 0, b, 0, c, 0,… y, 0, z, 0, 1}
Design sequence for PAPR of x dB
n
≈ 2·n
PAPR of near x dB
2xLTF
Additional tones can be added to fill the gap

## Slide 8: Possible Extensions
RUs < 242: Extensions from a basis sequence of 26-length
RUs ≥ 242: Extensions from a basis sequence of 242-length
26
26RU or 26RUc
52RU
106RU
484RU or 484SU
996SU
242
242
242RU or 242SU
242
26
26
x [1, -1, -1, -1]
x [1, -1, -1, -1]
x [1, -1, -1, -1]
x [1, -1, -1, -1]
Note: a and b are gap filling tones
Note: each SU sequence has 3 or 5 zeros in the center
Phase rotation
b
a
26
26
26
26
242
242
242
242
26
a
b

## Slide 9: Basis Sequence for 26
There are three existing sequences, LTFleft, LTFright, 11ah LTF for the 26-length, but all the options have relatively higher PAPRs than VHT LTF and data PAPRs
  Among those, LTFright has the lowest PAPRs of 5.0167~6.0499 dB for different pilot positions and P matrix elements, which are quite higher than expected PAPRs
Therefore, based on computer searches, a sequence which has a low min-max PAPRs has been found:
  HELTF26RU={1,-1,1,1,-1,-1,-1,-1,1,1,1,-1,1,1,1,-1,1,1,1,-1,1,1,-1,-1,-1,-1}
  It has PAPRs of 3.5527 ~ 4.9170 dB with different pilot positions* and P matrix values (Appendix B)
    As a reference, the median PAPR of 26-tone random data is 6.7dB (Appendix C)
* It considers PAPRs of the center 26RU position
26
New search

## Slide 10: 52RU
Two blocks of the basis 26 sequences are concatenated with a phase rotation of [1, -1, -1, -1]
  The PAPR of the proposed sequence shows 3.8075 ~ 5.5197 dB, which is much lower than 7.2dB, the median PAPR of random data
  HELTF52RU={HELTF26RU(1:13), -HELTF26RU(14:26), -HELTF26RU}
Note: The extension from the existing sequences, e.g., [LTFleft, LTFright] couldn’t provide good PAPRs
  Changing the length of the designed sequence destroys the PAPR property
    LTFleft and LTFright is designed for a form of [LTFleft, a, LTFright] as seen in previous 11’s, where a is +1, -1, or 0
      E.g., VHTLTF-28,28 = {1, 1, LTFleft, 0, LTFright, -1, -1}
26
26
x [1, -1, -1, -1]
Phase rotation ‘-1’ is applied
Phase rotation ‘+1’ is applied

## Slide 11: 106RU
The designed 26RU sequence can be duplicated four times with two tone fillings, and a phase rotation of [1, -1, -1, -1] is applied
  Among all combinations of positions and values of a and b, the best sequence comes when a and b located between 26 sequences and those are both ‘-1’
  The PAPR of the proposed sequence is 5.9710 ~ 6.5991 dB, which is much lower than 7.7 dB, the median PAPR of random data
  HELTF106RU = {HELTF26RU, 1, -HELTF26RU, -HELTF26RU, 1, -HELTF26RU}
b
a
26
26
26
26
x [1, -1, -1, -1]
Phase rotation ‘-1’ is applied
Phase rotation ‘+1’ is applied

## Slide 12: Basis Sequence of 242
For 242RU, VHT-122,122 can be reused with removing three zeros and rotating a phase every 60 tones with [1, -1, -1, -1]
  With the phase rotation, the range of PAPR is 5.5164 ~ 6.4357 dB, while it is 7.9905 ~ 9.1896dB without the phase rotation
    The median PAPR 242-tone of random data have is 8.1dB
  HELTF242RU = {VHTLTF-122,122left(1:60), -VHTLTF-122,122left(61:121), -VHTLTF-122,122right(1:121)}, where VHTLTF-122,122left and VHTLTF-122,122right are 121-length sequences in the left and right sides of 3 DCs in VHTLTF-122,122, respectively
For 242SU (242+3DCs), the sequence length is the same as VHT-122,122 , and thus, it can be exactly reused with a phase rotation [1, -1, -1, -1] defined in VHT80
  The PAPRs /w the phase rotation are 5.1906 ~ 6.4811 dB
242
Modified from VHT-122,122

## Slide 13: 484RU and 484SU
For 484RU, the designed 242 sequence can be duplicated twice, and a phase rotation [1, -1, -1, -1] is applied
  The PAPR of the proposed sequence for 484RU is 5.4000 ~ 6.7264 dB, which is much lower than 8.2dB, the median of random data
  HELTF484RU = {HELTF242RU (1:121), -HELTF242RU(122:242), -HELTF242RU}
For 484SU(484+5 DCs), 5 zeros are added in the center of 484RU
  The PAPR of the proposed sequence for 484SU is 5.3997 ~ 7.0077 dB
  HELTF484SU = {HELTF242RU (1:121), -HELTF242RU(122:242), 0, 0, 0, 0, 0, -HELTF242RU}
242
242
x [1, -1, -1, -1]

## Slide 14: 996SU
For 996SU (996 + 5 DCs), it can be concatenated from four HELTF242RU blocks and one HELTF26RU with filling two tones and a phase rotation of [1, -1, -1, -1]
  Among all the position and values of the two tone fillings, the best option is to add ‘1’ at the beginning and ‘-1’ at the end
  After applying the phase rotation, the PAPR of the proposed sequence is 6.8896 ~ 7.3248 dB, which is much lower than the median of random sequence, 8.2dB
  HELTF996SU = {1, HELTF242RU, -HELTF242RU, -HELTF26RU(1:13), 0,0,0,0,0, -HELTF26RU(14:26), -HELTF242RU, -HELTF242RU, 1}
242
242
242
242
26
x [1, -1, -1, -1]
a
b
5 zeros for DC

## Slide 15: Summary of PAPRs
 | Sequences | PAPRs of the Proposed Seq. (dB) | Median PAPR of Random Data (dB)
OFDMA | HELTF26RU | 3.5527 ~ 4.9170 | 6.7100
 | HELTF52RU | 3.8075 ~ 5.5197 | 7.2470
 | HELTF106RU | 5.9710 ~ 6.5991 | 7.7279
 | HELTF242RU | 5.5164 ~ 6.4357 | 8.0931
 | HELTF484RU | 5.4000 ~ 6.7264 | 8.1786
OFDM | HELTF242SU | 5.1906 ~ 6.4811 | 8.0931
 | HELTF484SU | 5.3997 ~ 7.0077 | 8.1786
 | HELTF996SU | 6.8896 ~ 7.3248 | 8.2177
The maximum PAPRs of all the proposed sequences are much less than the median PAPRs of the random data

## Slide 16: Summary of Proposed Sequences
OFDMA
    HELTF26RU ={1,-1,1,1,-1,-1,-1,-1,1,1,1,-1,1,1,1,-1,1,1,1,-1,1,1,-1,-1,-1,-1}
    HELTF52RU = {HELTF26RU(1:13), -HELTF26RU(14:26), -HELTF26RU}
    HELTF106RU = {HELTF26RU, 1, -HELTF26RU, -HELTF26RU, 1, -HELTF26RU}
    HELTF242RU = {VHTLTF-122,122left(1:60), -VHTLTF-122,122left(61:121), -VHTLTF-122,122right(1:121)}
      where VHTLTF-122,122left and VHTLTF-122,122right are 121-length sequences in the left and right sides of 3 DCs in VHTLTF-122,122, respectively
    HELTF484RU = {HELTF242RU (1:121), -HELTF242RU(122:242), -HELTF242RU}
  OFDM
    HELTF242SU = VHTLTF-122,122 with the phase rotation of VHT80
    HELTF484SU = {HELTF242RU (1:121), -HELTF242RU(122:242), 0, 0, 0, 0, 0, -HELTF242RU}
    HELTF996SU = {1, HELTF242RU, -HELTF242RU, -HELTF26RU(1:13), 0,0,0,0,0, -HELTF26RU(14:26), -HELTF242RU, -HELTF242RU, 1}

## Slide 17: Conclusion
In order to lower PAPRs for RUs smaller than 242, new basis sequences for 26 should be designed
  52RU and 106RU is extended by the designed 26RU and a phase rotation
For 242RU in OFDMA and 242SU in OFDM, the existing VHT-122,122 sequence can be reused with a phase rotation
  For RUs larger than 242, the design sequence block of 242 can be concatenated with some tone fillings and a phase rotation
For 2xLTF, the designed half-sized sequence is reused and additional tones can be attached
  Detailed sequences are TBD

## Slide 18: Straw Poll #1
Do you agree to add the following texts into the SFD?
  A HE LTF for 242SU shall reuse VHT-122,122 with the same phase rotation [1, -1, -1, -1].
    HELTF242SU = VHTLTF-122,122 with the phase rotation of VHT80

## Slide 19: Straw Poll #2
Do you agree to add the following texts into the SFD?
    HE LTFs for 26RU, 52RU, and 106RU shall use the following sequences:
      HELTF26RU ={1,-1,1,1,-1,-1,-1,-1,1,1,1,-1,1,1,1,-1,1,1,1,-1,1,1,-1,-1,-1,-1}
      HELTF52RU = {HELTF26RU(1:13), -HELTF26RU(14:26), -HELTF26RU}
      HELTF106RU = {HELTF26RU, 1, -HELTF26RU, -HELTF26RU, 1, -HELTF26RU}

## Slide 20: Straw Poll #3
Do you agree to add the following texts into the SFD?
  A HE LTF for 242RU shall use VHT-122,122 removing zeros with the phase rotation [1, -1, -1, -1].
      HELTF242RU = {VHTLTF-122,122left(1:60), -VHTLTF-122,122left(61:121), -VHTLTF-122,122right(1:121)},
          where VHTLTF-122,122left and VHTLTF-122,122right are 121-length sequences in the left and right sides of 3 DCs in VHTLTF-122,122, respectively

## Slide 21: Straw Poll #4
Do you agree to add the following texts into the SFD?
  HE LTF sequences for 484RU, 484SU, and 996SU shall be made from concatenations of the HELTF sequence for 242RU in frequency domain, as shown in the followings:
      HELTF484RU = {HELTF242RU, HELTF242RU}
      HELTF484SU = {HELTF242RU, 0, 0, 0, 0, 0, HELTF242RU}
      HELTF996SU = {1, HELTF242RU, -HELTF242RU, -HELTF26RU(1:13), 0,0,0,0,0, -HELTF26RU(14:26), -HELTF242RU, -HELTF242RU, 1}

## Slide 22: References
[1] 11-15/0584r1, “Considerations on LTF Sequence Design”, May 2015
[2] 11-15/0132r7, “Specification Framework for TGax”, July 2015

## Slide 23: Appendix A: Phase Rotations
In the concatenate sequence from 4 random-sequence blocks, the gain in PAPR with a phase rotation are evaluated for all 63 possible combination of phase rotation, e.g., [1, 1, 1, -1], …., [+j, +j, +j, +j]
Best Group
There are three groups in PAPR gains
The best group has a gain of 2.5dB, and 16 combinations of phases are the case
[1, -1, -1, -1] is one of the cases in the best group

## Slide 24: Appendix B: 26-Length Sequences
Among nine 26RUs in 20MHz, there are three types of RUs depending on pilot positions
For all the combinations of pilot positions and P matrix values, PAPRs are calculated and those are 3.5527 ~ 4.9170 dB
P matrix values | Position 1 | Position 2 | Position 3
1 | 3.7952 | 3.7952 | 4.4446
exp(-j2π·1/6) | 4.6237 | 4.4183 | 4.6259
exp(-j2π·2/6) | 4.1386 | 4.4166 | 4.9170
exp(-j2π·3/6) = -1 | 3.5527 | 4.1814 | 4.2543
exp(-j2π·4/6) | 3.9696 | 4.7628 | 4.8554
exp(-j2π·5/6) | 4.4527 | 4.7564 | 4.5735
26
6th
19th
26
7th
21th
Pilot Position 1
26
Pilot Position 2
26
13+7dc+13
Pilot Position 3
26
26
26
26
7th
27th

## Slide 25: Appendix C: Reference PAPRs
PAPR is one of key metric to design LTF sequences
  The optimization of PAPR in HELTF is needed to acquire more room for power boosting in data
  Considering PAPRs of legacy and data, it seems reasonable to design LTF sequences to have near the minimum PAPR and less than the median PAPR of data
PAPR of Legacy
PAPR of Data
Bandwidth | L-STF | L-LTF | VHT-LTF
20 MHz [ 1 ] | 2.2394 | 3.2245 | 3.7247
40 MHz [1 +j] | 5.2497 | 5.8208 | 6.2343
80 MHz [1 -1 -1 -1] | 4.3480 | 5.3827 | 5.1041
#of tones | Median
26 | 6.7100
52 | 7.2470
106 | 7.7279
242 | 8.0931
484 | 8.1786
996 | 8.2177
Note: the values in square brackets “[ ]” are phase rotation values used to reduce the overall PAPR