## Slide 1: Supported Resource Allocations in SIG-B
Date: 2015-11-09
Authors:

## Slide 2: Background
The following structures were agreed in the September meeting[1]:
  The RU allocation signaling in the common field of HE-SIG-B signals an 8 bit, per 20 MHz PPDU BW for signaling
  The RU arrangement in frequency domain
  Number of MU-MIMO allocations: The RUs allocated for MU-MIMO and the number of users in the MU-MIMO allocations.
    The exact mapping of the 8 bit to the RU arrangement and the number of MU-MIMO allocations is TBD.
    Signaling for the central 26 RU in 80 MHz is TBD
This contribution is talking about the mapping table and the center 26 RU supports

## Slide 3: Resource Mapping for 8 bits
The 8 bits should indicate the RU allocations and the number of users in the MU-MIMO allocations [2]
Therefore, the RU allocations can be listed from the smallest size to the largest, and the number of users in MU-MIMO can be enumerated for a given RU size
However, there are some consideration points as follows:
  Number of MU-MIMO multiplexed STAs in each RU
  Center 26RU support in 80MHz and 160MHz
  Some exceptional cases

## Slide 4: Number of Supported STAs in MU-MIMO
For a given RU (> 106), multiple STAs can be multiplexed by MU-MIMO
  Without any restriction, the number of assigned STAs can be up to 17 in case of 106RU(8 STAs)+26RU(1 STA)+106RU(8 STAs) allocation, and it can be up to 19 when two center 26RUs in 160MHz are assigned to different STAs
Scheduling 17 users per 20MHz seems to be an overdesign, and is not likely be implemented in the near future (even with advancements in H/W).
Is this absolutely necessary for 11ax?
106
106
106
106
106
106
106
106
106
106
106
106
106
106
106
106
26
8 MU-MIMO + 1 SU-MIMO + 8 MU-MIMO

## Slide 5: Number of Supported STAs in MU-MIMO (cont.)
Maximum of 9 (or 10) users per 20MHz seems to be good target for 11ax
  9 of 26 RUs (= 9)
  4 MU-MIMO 106 RUs + 26 RU + 4 MU-MIMO 106 RU (=9)
  8 MU-MIMO 242 RUs (=8)
Design goals
  Number of spatially multiplexed STAs for 106 RU limited to 4
  Full flexibility in the spatially multiplexed STAs for 242/484/996/2*996 RU
  Maximum of 9 (or 10) users per 20MHz block.
    10 is if we include the central 26 RU in 80MHz

## Slide 6: Signaling for the Center 26RU in 80MHz
In 80MHz and 160MHz, there is one or two center 26RUs, respectively, but it not included in the current SIG-B structure
In order to utilize the center 26RU, two methods can be considered
  Alternative 1: Explicit signaling for the existence of the center 26RU allocation in SIG-B common field
    A STA-specific field for the center 26RU is considered as part of the STA-specific field encoding pair (a single encoding block may contain up to 2 STA-specific field).
80MHz
12
Edge
12
Edge
12
Edge
12
Edge
1
3
1
3
1
3
1
3
1
3
1
3
1
3
1
3
11 Edge
11 Edge
11 Edge
11 Edge
11 Edge
7
DC
7
DC
7
DC
7
DC
12 Edge
996 usable
tones +5 DC
242
242
2
6
26
52
102+4
102+4
2
2
2
6
52
2
6
2
6
52
26
102+4
102+4
2
6
2
6
2
6
26
2
6
2
6
52
1
1
2
6
1
2
6
52
2
1
2
1
1
1
26
2
6
2
52
1
1
2
2
6
2
2
6
52
1
2
1
2
6
2
6
2
6
2
6
2
52
1
1
2
1
1
1
1
2
1
242
242
2
6
26
52
102+4
102+4
2
2
2
6
52
2
6
2
6
52
26
102+4
102+4
2
6
2
6
2
6
26
2
6
2
6
52
1
1
2
6
1
2
6
52
2
1
2
1
1
1
26
2
6
2
52
1
1
2
2
6
2
2
6
52
1
2
1
2
6
2
6
2
6
2
6
2
52
1
1
2
1
1
1
1
2
1
central 26 RU

## Slide 7: Signaling for the Center 26RU in 80MHz (cont.)
  Alternative 2: No explicit signaling in the common field, detection of additional STA-specific field at the end of SIG-B.
    The STA-specific field is encoded separated contains and contains CRC (and tail bits).
    The existence of the STA-specific field can be validated by STA-ID and CRC
Alternative 1 is preferred.
Common (A)
A
B
Common
(B)
C
D
Common (C)
Common
(D)
80MHz
STA-specific
(STA1)
STA-specific
(STA2)
STA-specific
(STA5)
STA-specific
(STA6)
Duplication of SIG-B in Channel A
Duplication of SIG-B in Channel B
Padding
…
tail
tail
CRC
tail
CRC
tail
STA-specific
(STA3)
CRC
tail
STA-specific
(STA4)
CRC
tail
STA-specific
(STA5)
STA-specific
(STA6)
CRC
tail
Separately encoded STA-specific info. for central 26 RU

## Slide 8: Discussions for Exceptional Cases
484RU (STA3)
484RU (STA2)
‘2x996SU’ is not needed among the RU allocation states
  In 160MHz, no other STA can be multiplexed more in frequency domain, and thus, it is the case of SU PPDU in which no SIG-B is transmitted
‘No STA Assigned’ state is needed
  Some RU allocation subfield (8bits) can have no STA-specific subfield
    For example, the common (C) in the below figure has no STA to be assigned, and no related STA-specific field is needed
    The common (C) can indicate ‘No STA Assigned’ state not to transmit unnecessary STA-specific subfield
Common (A)
A
B
Common
(B)
C
D
Common (C)
Common
(D)
80MHz
STA-specific
(STA1)
STA-specific
(STA2)
STA-specific
(STA3)
STA-specific
(STA4)
Duplication of SIG-B in Channel A
Duplication of SIG-B in Channel B
Padding
Padding
484RU (STA1)
…
…
Spatially multiplexed (MU-MIMO)
484RU (STA4)
No assignment
…
…
SIG-B
Data

## Slide 9: Supported Resource Allocation
All combinations of RUs which are smaller than 106, and each has SU format
All combinations of SU and MU, and MU is allowed up to 4 STAs in the RU size of 106
2*996 SU is excluded
‘No STA assigned’ state is added
All combinations of SU and MU, and MU is allowed up to 8 STAs
99 states

## Slide 10: Supported Resource Allocation (cont’d)
Same set of states when the center 26RU in 80MHz is supported
99 states

## Slide 11: Conclusions
A set of supported resource allocation with 8 bits is suggested
  Total number of states is 198 including the following states
    1 state for ‘No STA Assigned (NA)’
    8 states each for MU-MIMO of 484, 996, 2x996 RU
    No SU-MIMO state for 2x996 RU
    States for all possible OFDMA multiplexing (full flexibility)
      States for ‘center 26RU in 80MHz’ is included
    States for MU-MIMO multiplexing with the following restrictions:
      No MU-MIMO in RUs smaller than 106
      Maximum of 4 STAs in MU-MIMO in the RU of 106
      Maximum of 8 STAs in MU-MIMO in RUs larger than 106

## Slide 12: Straw Poll #1
Do you agree to add the following text into the SFD?
  The 8 bits in the common field of HE SIG-B includes a state of ‘No STA Assigned’ for which no STA-specific field is transmitted

## Slide 13: Straw Poll #2
Do you agree to add the following text into the SFD?
  The number of spatially multiplexed STAs for 106 RU limited to 4
    For RUs larger than 106, it can be 8 STAs as maximum

## Slide 14: Straw Poll #3
Do you agree to support the following text?
  The 8 bits in the common field of HE SIG-B includes explicit states for the existence of the center 26RU of 80MHz

## Slide 15: Reference
[1] 11-15/0132r9, “Specification Framework for TGax”, Sept. 2015
[2] 11-15/1066r0, “HE-SIG-B Contents”, Sept. 2015