## Slide 1: Authors
11ax Spectral Masks
Date: 2015-11-09
Name | Affiliation | Address | Phone | Email
Lin Yang | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Blvd, Suite 475, RichardsonTX, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com

## Slide 3: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 10: Introduction
11ax 20/40/80/160MHz tone plans have been adopted in previous meetings. The number of edge tones in these tone plans are determined based on the following suggestions of 11ax spectrum masks[1]
  For 4x symbol 20MHz bandwidth, its spectral mask is based on 11ac 80MHz mask down-clocked by 4
  For 4x symbol 40MHz bandwidth, its spectral mask is based on 11ac 80MHz mask down-clocked by 2
  For 4x symbol 80MHz bandwidth, its spectral mask is based on 11ac 160MHz mask down-clocked by 2
This presentation clarifies the spectral masks for HE 20/40/80MHz and also proposes the spectrum masks for 160/80+80MHz
  Main focus is on non-OFDMA PPDU
    In case of OFDMA, PSD of data portion may be higher than that of the legacy preamble. Different rules may be needed
  Spectral mask requirements discussed here do not apply to TX LO leakage
    Same as 11ac

## Slide 11: Methodology
IEEE spectral masks are generally decoupled from regulatory rules
  Regulatory has many variations for specific regions and countries
Similar to 11ah, use downclocking to derive 11ax masks
  The narrower tone spacing leads to sharper spectrum roll off
    Each sinc is narrower in frequency and longer in time
  Tightening 11ac masks by a downclocking factor (10 for 11ah) does not add additional difficulty for the mask compliance
160MHz 11ax mask leverages 11ac design and maintains the same Tx filtering requirements
  OOBE comparable to 11ac 160MHz

## Slide 12: Overview of 11ac Spectral Mask
Remarks:
1st rolloff has same slope for all BWs
  Transition from 0 dBr to -20dBr takes 2 MHz frequency span
Mask skirt is proportional to PPDU BW
80+80 mask is combination of two 80 MHz interim spectral masks
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11ac 20 | 9 | 11 | 20 | 30
11ac 40 | 19 | 21 | 40 | 60
11ac 80 | 39 | 41 | 80 | 120
11ac 160 | 79 | 81 | 160 | 240
BW(MHz) | 0dBr | -20dBr | -28dBr | -40dBr
11ac 20 |  |  |  | 
11ac 40 |  |  |  | 
11ac 80 |  |  |  | 
11ac 160 |  |  |  | 

## Slide 13: Spectral Mask for HE 20 MHz PPDU
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
9.75
10.25
20
30
-
9.75
-
10.25
-
20
-
30
Freq
[
MHz
]
Propose HE 20MHz spectral mask to be 11ac 80MHz mask down-clocked by 4
  (6,5) guard tones

## Slide 14: Spectral Mask for HE 40/80 MHz PPDU
Propose HE 40/80MHz spectral mask to be 11ac 80/160MHz mask down-clocked by 2
  (12,11) guard tones
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
19.5
20.5
40
60
-
19.5
-
20.5
-
40
-
60
Freq
[
MHz
]
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
39.5
40.5
80
120
-
39.5
-
40.5
-
80
-
120
Freq
[
MHz
]
Transmit Spectral Mask for HE 80 MHz PPDU
Transmit Spectral Mask for HE 40 MHz PPDU

## Slide 15: Spectral Mask for a HE 160/80+80 MHz PPDU
Propose spectral mask for HE 80+80/160MHz to be similar to 11ac
  For HE 80+80 MHz, the mask is combination of two 80 MHz interim spectral masks
  For HE 160MHz, the mask has the same skirt as that of 11ac 160MHz and 1st rolloff identical to HE 40/80MHz
    160MHz tone plan has same number of guard tones ([12, 11]) as HE 40/80MHz
PSD
0
dBr
-
20
dBr
-
28
dBr
-
40
dBr
79.5
80.5
160
240
-
79.5
-
80.5
-
160
-
240
Freq
[
MHz
]
Spectral Mask for a HE 160 MHz PPDU
Spectral Mask for a HE 80+80 MHz PPDU

## Slide 16: Straw-poll
Do you support to add the following to 11ax SFD?
The spectral masks for 11ax non-OFDMA 20/40/80/160/80+80 MHz PPDU are defined as in slides 13-15?
  The bandwidth of the applied spectrum mask for a (non-OFDMA) PPDU shall be determined by the bandwidth occupied by the pre HE-STF portion of the preamble in this PPDU, regardless of the BSS bandwidth
  The spectral mask requirements do not apply to LO leakage

## Slide 17: References
[1] IEEE 802.11-15/0330r5 OFDMA Numerology and Structure

## Slide 18: Appendix HE 20MHZ ACI effects from 11ax 4x symbol with 11 guard tones HE 80MHz mask compliance testing HE 160Mhz Mask Compliance Testing

## Slide 19: Blocker Performance Evaluation Setup
20MHz system, no impairment
  1x: 11ac 64FFT tone plan (1 DC, 7 guards, 52 data & 4 pilots)
  4x: 11ax 256FFT tone plan (3 DC, 11 guards, 234 data & 8 pilots)
AWGN channel
Six scenarios
  ACI is from an unsynchronized adjacent 20MHz system
Desired and ACI signals share same MCS
  MCS0
    If ACI exists, ACI has power of 16dB above transmit signal
  MCS8
    If ACI exists, ACI has power of -7dB above transmit signal
Packet size of 1000 bytes, 1000 packets per SNR point
Transmit Signal | w/o ACI | ACI of 1x Signal | ACI of 4x Signal
1x | √ | √ | √
4x | √ | √ | √

## Slide 20: Blocker Performance of MCS0 and MCS8
At PER =10%, SNR shifts ~0.2- 0.4dB for both MCS0 and MCS8
  For a 1x desired signal, wider inband spectrum from a 4x ACI, compared to that from a 1x ACI, does not result in noticeable degradation
  For a 4x desired signal, the OOB emission roll-off of a 1x ACI is not as sharp as that of a 4x ACI. But the PER with a 1x ACI does not differ from that with a 4x ACI
@ PER=10% | MCS0 w/ 1x ACI of 16dB | MCS0 w/ 4x ACI of 16dB | MCS8 w/ 1x ACI of -7dB | MCS8 w/ 4x ACI of -7dB
1x signal | 0.25 dB | 0.25 dB | 0.35 dB | 0.4 dB
4x signal | 0.2 dB | 0.2 dB | 0.25 dB | 0.2 dB
Table: SNR degradation comparing to without ACI
Wider inband spectrum from 4x symbol with 11 guard tones does not cause noticeable degradation in ACI performance

## Slide 21: 80MHz Mask
The following plots show that 11ax has lower OOBE than 11ac, and hence the spectral mask is met even if only (6,5) guard tones are considered.
  The legend “edge 506” indicated the case of (6,5) guard tones

## Slide 22: Feasibility of 11 guard tones for 11ax 80MHz Transmission
Setup:
  Both 1x and 4x assume total 11 guard tones at the band edge, and 4x has 7DC and 1x has 3DC
  IEEE 802.11ac 80MHz mask as reference, with RBW of 100kHz
  8x IFFT
Observation:
  OOBE: 1x and 4x are quite similar, both waveforms can meet the mask with margin even for 4 dB PA backoff (assuming P=3).

## Slide 23: 160MHz Mask
PA IBO requirement to meet mask:
Assuming Rapp PA with P=3, 64QAM
4dB IBO is needed with margin