## Slide 1: MU BAR Frame Format
Date: 2015-11-08
Authors:
Name | Affiliations | Address | Phone | email
Reza Hedayat Young Hoon Kwon Yongho Seok Vida Ferdowsi | Newracom | 9008 Research Drive, Irvine, CA 92618 |  | reza.hedayat at newracom.com younghoon.kwon at newracom.com yongho.seok at newracom.com vida.ferdowsi at newracom.com

## Slide 2: Outline
In past meetings, the TGax passed the following MU motions:
  “802.11ax amendment shall include a mechanism to multiplex BA/ACK responses to DL MU transmission”
  “The spec shall define a MU-BAR frame to solicit BA/ACKs from multiple STAs in UL MU transmissions.”
  “The amendment shall include a mechanism to multiplex acknowledgment frames in response to Multicast receptions under GCR BA operation.”
In this contribution three options for MU BAR frame format is presented and pros and cons of above options will be discussed

## Slide 3: Multiuser Block-ACK Request
Multiuser Block-ACK Request (MU BAR) solicits BA or ACK frames from STAs to be multiplexed in an uplink MU transmissions [15/1053]
MU BAR solicit ACK/BA frames similar to a DL MU frame …
MU-BAR
AP
STA1
STA2
DL MU
BA
BA
BA
BA
STA3
STA4

## Slide 4: Multiuser Block-ACK Request
MU BAR solicits ACK/BA frames in other ways too:
  An MU BAR frame can solicit ACK/BA frames for payloads that were previously delivered either in SU and/or MU PPDUs
  An MU BAR frame can solicit ACK/BA frames for payloads that were delivered in a multicast service
MU-BAR
BA
BA
AP
STA1
STA2
Multicast frame

## Slide 5: MU BAR Frame Format - 1
The first option for MU BAR frame format is to modify a multi-TID BAR frame so that it acts as a Trigger frame
The following is the structure of multi-TID BAR

## Slide 6: MU BAR Frame Format - 1
Similar to multi-TID BA that was adopted by 11ax SFD as multi-STA BA, multi-TID BAR can be used as multi-STA BAR
  Similar change to Per-TID info can be made to accommodate each STA AID
Moreover, the following sub-fields is added to convey the scheduling info so that each STA can participate in the following UL MU PPDU:
  Added to BAR information field for each STA
    RU indication subfield
    MCS subfield
    …
  Added to BAR Control field
    LTF length indication subfield
    GI indication subfield
    …

## Slide 7: MU BAR Frame Format - 1
Pros and cons of option 1
  Since the content of BAR/Trigger frames are combined, it avoids fields duplications
  This option proposes a new control frame and a new sub-type is required
MU BAR
Control
MU BAR
Information
AID, RU Index, MCS, …
Repeat for each STA
GI indication, LTF indication, …

## Slide 8: MU BAR Frame Format - 2
The second option for MU BAR frame format is to aggregate a Trigger frame with a multi-TID BAR
Trigger frame has been adopted in 11ax SFD to trigger responses from multiple STAs within a UL MU frame
FC
Duration
(A1)
A2
Common Info
Per-STA Info
…
Per-STA Info
FCS
Trigger Frame
Multi-STA(TID) BAR

## Slide 9: MU BAR Frame Format - 2
A STA that receives multi-STA (multi-TID) BAR with one AID matching the AID of the STA shall respond with a BA frame after TBD IFS if the same PPDU carries a Trigger frame with a matching AID in a per-user info field of the Trigger frame
Pros and cons of option 2
  Due to aggregation of two frames, each receiving STA need to process two frames to be able to respond with BA. If either of the two frames are not decoded successfully then there is no chance to respond with the BA frame
  Due to aggregation of two frames, a lot of fields are duplicated. Particularly, the AID for each STA (that is expected to send a BA frame in response to the MU BAR) is repeated in both Trigger frame and multi-TID BAR frame

## Slide 10: Trigger Frame
Trigger frame in 11ax SFD:
  … a new control frame format that carries sufficient information to identify the STAs transmitting the UL MU PPDUs and allocating resources for the UL MU PPDUs. Trigger frame has the following additional fields: Common Info, Per-User Info (one for each resource allocation) [15/877]
Trigger frame might be used for various purposes
  For instance, a Trigger frame can be used to poll several STAs to send buffer status report [15/1120]
  Or a Trigger frame can be used to poll several STAs to send BA frames
Therefore, a Trigger frame can carry a Trigger Type subfield where it indicates the purpose of the Trigger frame
FC
Duration
(A1)
A2
Common Info
Per-STA Info
…
Per-STA Info
FCS

## Slide 11: MU BAR Frame Format - 3
The third option for MU BAR frame format is to use a Trigger frame that has additional sub-fields necessary for BAR
Trigger frame with type MU BAR can carries the following subfields:
  BAR Info (Block ACK Starting Sequence Number) in each per-STA info
  BAR Control (TBD content and size) in the Common Info field
    Not all the subfields in the current BAR Control field may be present in MU BAR. E.g., “BAR ACK policy” need not be present since all the participating STAs are expected to respond with BA right after the MU BAR frame.
FC
Duration
(A1)
A2
Common Info
Per-STA Info
…
Per-STA Info
FCS
Duration, GI indication, LTF indication …
Trigger Type = BAR, BAR Control (TBD)
AID, RU index, MCS, …
BAR Information

## Slide 12: MU BAR Frame Format - 3
Pros and cons of option 3
  A recipient STA need to decode a single frame to be able to participate in the following UL MU frame
  The use of Trigger Type gives a structure to use Trigger frame for various purposes such as MU BAR
  …
FC
Duration
(A1)
A2
Common Info
Per-STA Info
…
Per-STA Info
FCS
Duration, GI indication, LTF indication …
Trigger Type = BAR, BAR Control (TBD)
AID, RU index, MCS, …
BAR Information

## Slide 13: Conclusion
MU BAR recently was added to 11ax SFD.
MU BAR solicits multiplexed ACK/BA frames several ways: (a) for payloads that were delivered either in SU and/or MU PPDUs, (b) for payloads that were delivered in a multicast service
In this contribution three options for MU BAR format was proposed
Considering the pros and cons of the three options, it seems that a Trigger frame with type BAR suits best to be used for MU BAR frame format

## Slide 14: Strawpoll
Do you agree the following to be added to 11ax SFD:
7.2.X: The MU BAR frame is a Trigger frame whose Trigger Type subfield is MU BAR that carries additional BAR Control subfield (TBD) and an additional BAR Information subfield (TBD) in Common Info and/or each Per-User info.