## Slide 1: MU-RTS/CTS Follow Up
Date: 2015-11-09
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 4: Authors (continued)
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Leo Montreuil |  |  |  | 
Vinko Erceg |  |  |  | 
Durai Thirupathi |  |  |  | 

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi’an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple | Cupertino, CA | +1-408-974-5967 | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 10: Abstract
In [1], MU-RTS/CTS has been introduced to resolve the hidden node problem of DL MU transmission
This presentation discusses the following topics of MU-RTS/CTS procedure
  Application to UL MU and Cascading TXOP
  MAC Frame format of MU-RTS
  CTS response for wide channel

## Slide 11: MU-RTS/CTS for UL MU and Cascading TXOP
The current spec defines MU-RTS/CTS for DL MU
However, there are also reasons to allow MU-RTS/CTS to protect UL MU and Cascading TXOP
  For UL MU, the MU ACK from AP may have duration possibly longer than EIFS, and legacy STAs may interfere with MU ACK frame. Hence, protection on the STA side may be required. (Details provided in Appendix)
  Cascading TXOP [2] mixes DL MU and UL MU transmission, and protection for DL MU may be required
Propose to allow MU-RTS/CTS to protect MU transmission during that TXOP
  Note that AP has flexibility to decide if MU-RTS/CTS is used or not

## Slide 12: MU-RTS MAC Format
There are two options:
  Modify current RTS frame and use a group address at RA
    Require group formation, which introduces additional signaling
    There may be 2^31 groups for total 32 stations
    Each station may need to store many multicast IDs (up to 2^31)
    Hard to add other signaling
    Does not scale well for dense environment
  Define a new MAC frame format
    Due to similar requirement of simultaneous CTS response and UL MU response, we expect that the frame format is similar to trigger frame
Propose to use a variant of trigger frame format as the MAC format of MU-RTS

## Slide 13: CTS Response to MU-RTS
CTS response should set NAV of the neighboring STAs to achieve protection
  To achieve this goal, propose the following
    The CTS sent in response to a frame that solicits simultaneous CTS shall be transmitted on one or more 20 MHz channels so the minimum requirement for the neighbouring STAs to decode the CTS response is met
    Allow MU-RTS to request STAs to send non-HT CTS immediate response for protection from legacy STAs

## Slide 14: CTS Response For Wide Channel
We expect that CTS response to MU-RTS would be sent with (duplicate) non-HT PPDU most of the time, and we focus on this option in this presentation
In MU operation, STA may only be allocated on a specific sub-band, which only requires the STA to protect certain 20MHz bands
When the CTS is sent in (duplicate) non-HT PPDU, we think there may be three options
  CTS is responded on the entire band used by MU-RTS
  CTS is responded on the primary 20MHz and band required for protection with valid mode, ex: Primary 40 MHz when Primary 80MHz is used by MU-RTS if only secondary 20MHz requires protection.
  CTS is responded on only the band indicated by MU-RTS for protection. Ex: only secondary 20MHz

## Slide 15: Three Options of CTS Response to MU-RTS with non-HT PPDU
AP needs STA to protect secondary 20MHz and sends MU-RTS in Primary 80MHz
Option 2 and 3 enables the ability to increase protection range on the required band, but option 3 may require further PHY support
For full flexibility, propose that MU-RTS will carry signaling for each STA to indicate the 20MHz channel(s) for CTS response to enable all options based on capability and future design
  The indicated 20 MHz channel(s) can be either Primary20, Primary40, Primary80 or 160/80+80 MHz for now. Other indications are TBD.
CTS from STA
CTS from STA
CTS from STA
CTS from STA
20 MHz
Secondary 20 MHz
Secondary 40 MHz
CTS from STA
CTS from STA
20 MHz
Secondary 20 MHz
Secondary 40 MHz
CTS from STA
20 MHz
Secondary 20 MHz
Secondary 40 MHz
(1)
(2)
(3)

## Slide 16: Conclusion
We propose the following for MU-RTS/CTS procedure
  Allow MU-RTS/CTS to protect MU transmissions during that TXOP
  The MAC format of MU-RTS is a variant of trigger frame format
  The CTS sent in response to a frame that solicits simultaneous CTS shall be transmitted on one or more 20 MHz channels
  MU-RTS may request STAs to send non-HT CTS immediate response
  MU-RTS will carry signaling for each STA to indicate the 20MHz channel(s) for transmitting CTS response when CTS is sent in (duplicate) non-HT PPDU

## Slide 17: Straw Poll 1
Do you agree to add to the TG Specification Frame work document?
  x.y.z. MU-RTS/CTS frame exchange may be used for protection of MU transmissions during that TXOP

## Slide 18: Straw Poll 2
Do you agree to add to the TG Specification Frame work document?
  x.y.z. The MAC format of MU-RTS is a variant of trigger frame format

## Slide 19: Straw Poll 3
Do you agree to add to the TG Specification Frame work document?
  x.y.z. The CTS sent in response to a frame that solicits simultaneous CTS shall be transmitted on one or more 20 MHz channels.

## Slide 20: Straw Poll 4
Do you agree to add to the TG Specification Frame work document?
  x.y.z. MU-RTS may request STAs to send non-HT CTS immediate response

## Slide 21: Straw Poll 5
Do you agree to add to the TG Specification Frame work document?
  x.y.z. MU-RTS will carry signaling for each STA to indicate the 20MHz channel(s) for transmitting CTS responses when CTS is sent in (duplicate) non-HT PPDU
    When a STA sends CTS in response to MU-RTS, the CTS response shall be transmitted in the 20MHz channel(s) indicated in MU-RTS
      provided other transmission conditions TBD are met (e.g. channel idleness)
    The indicated 20 MHz channel(s) can be either Primary20, Primary40, Primary80 or 160/80+80 MHz. Other indications are TBD.
    Exact Signaling TBD

## Slide 22: Reference
11-15-0867-01 MU-RTS/CTS for DL MU
11-15-0841-01 Cascading Structure

## Slide 23: Appendix: MU-RTS/CTS for UL MU
Without MU-RTS/CTS
With MU-RTS/CTS
Trigger
AP
Triggered STAs
UL MU
MU ACK
Legacy STAs
EIFS
Transmit and Interfere
Data Tx
Legacy STA does not hear Trigger from AP
Legacy STA receives UL MU but can not decode the frame
Trigger
AP
Triggered STAs
UL MU
MU ACK
Legacy STAs
MU-RTS
CTS(s)
NAV (CTS)