## Slide 1: NAV Consideration for UL MU Response Follow Up
Date: 2015-11-09
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Leo Montreuil |  |  |  | 
Vinko Erceg |  |  |  | 
Durai Thirupathi |  |  |  | 
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple | Cupertino, CA | +1-408-974-5967 | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi’an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 11: Abstract
It has been agreed that NAV is considered for UL MU response [1]
  Only NAV not set by AP will be considered
  May not need to consider NAV set by Intra-BSS frame in general [2]
However, NAV set by Inter-BSS frame (or equivalently OBSS frame) may be overridden by AP/Intra-BSS frame very often
  AP creates CFP period to control Intra-BSS transmission
  AP schedules different set of users in consecutive UL MU [Appendix]
  NAV may be set by TXOP duration in HE-SIGA [2]
As a result, capability to protect existing Inter-BSS transmission under UL MU response is lost, and we explore the ideas of letting each STA maintain two NAVs to resolve the issue

## Slide 12: NAV Consideration for UL MU Response
Ex: AP creates CFP period to control Intra-BSS transmission
  Note that similar examples under cascading TXOP can be constructed
  Other examples are provided in the Appendix
Trigger for 1,2,3,4
AP
UL MU
STA1
UL MU
STA2
UL MU
STA3
STA4
Trigger for 1,2,3,4
MU BA
STA4 NAV set by Inter-BSS Frame
UL MU
UL MU
UL MU
UL MU
MU BA
STA4 can not consider NAV set by Inter-BSS frame because NAV is overridden by AP
CTS-to-Self
STA4 NAV set by Intra-BSS Frame
UL MU

## Slide 13: Proposed Solution
A STA maintains two NAVs, and one is the NAV for Intra-BSS frame
  NAV set by Inter-BSS frame can be preserved and considered for UL MU response
Trigger for 1,2,3,4
AP
UL MU
STA1
UL MU
STA2
UL MU
STA3
STA4
Trigger for 1,2,3,4
MU BA
STA4 NAV set by Inter-BSS Frame
UL MU
UL MU
UL MU
UL MU
MU BA
If STA4 maintains NAV set by Intra-BSS frame separately, STA4 can consider NAV set by Inter-BSS Frame
CTS-to-Self
STA4 NAV set by Intra-BSS Frame

## Slide 14: Consideration for Distinguishing NAV Set by Intra-BSS Frame
Having TXOP duration [3] and BSS color [4] in HE-SIGA already differentiates if NAV is set by Intra-BSS or Inter-BSS frame
Passed motion about TXOP Truncation [5] also distinguishes NAV set by Intra-BSS or Inter-BSS frame
It is natural to add NAV for Intra-BSS frame such that existing Inter-BSS transmission can be better protected under UL MU response
Note that there may be some frame (e.g., CTS) that can not be determined to be Intra-BSS or Inter-BSS
  In this case, a simple rule for maintaining two NAVs is that one is the NAV for Intra-BSS frame, and another one is the NAV for Inter-BSS frame or frame that cannot be determined to be Intra-BSS or Inter-BSS

## Slide 15: Implementation Consideration for Maintaining Two NAVs
The idea of maintaining more than one NAV is not new [6-8], and there may be concerns that more than one timer is required
We think that many possible methods can be used to maintain 2 NAVs, and we list a few methods below.
  Have one timer for each NAV
    Simple but increasing the implementation complexity because of maintaining two NAV timers
  Use a timer for the longer NAV and record the difference with the shorter NAV (appendix)
  Use a timer for the shorter NAV and record the difference with the longer NAV (appendix)

## Slide 16: Conclusion
We discuss the situations that NAV set by Inter-BSS frame may be overridden by AP/Intra-BSS frame in UL MU transmission
To better protect the existing Inter-BSS transmission under UL MU response, we propose that a STA maintains two NAVs
  One is the NAV for Intra-BSS frame, and another one is the NAV for Inter-BSS frame or frame that cannot be determined to be Intra-BSS or Inter-BSS

## Slide 17: Straw Poll
Do you agree to add to the TG Specification Frame work document?
  x.y.z. A STA maintains two NAVs
    One is the NAV for Intra-BSS frame, and another one is the NAV for Inter-BSS frame or frame that cannot be determined to be Intra-BSS or Inter-BSS
    Note that maintaining two NAVs does not imply maintaining two NAV timers
    The detailed method of maintaining two NAVs (e.g., two NAV timers or one NAV timer with difference of two NAV values, etc.) is TBD
    Mandatory or Optional TBD

## Slide 18: Reference
11-15-1062-01 NAV Consideration for UL MU Response to Trigger Frame
11-15-1301-00 NAV Rule for UL MU Response
11-15-1077-00 HE-SIGA content
11-15-1122-00 Identifiers in HE PPDUs for power saving
11-15-1067-00 MU TXOP Truncation
11-01-0372-00 a new approach to the nav
11-03-0565-03 nav protection
P802.11REVmc_D4.0

## Slide 19: Appendix: NAV Consideration for UL MU Response
Ex: AP schedules different set of users in consecutive UL MU
  Note that similar examples under cascading TXOP can be constructed
Trigger for 1,2,3,4
AP
UL MU
STA1
UL MU
STA2
UL MU
STA3
STA4
Trigger for 1,2,3,5
MU BA
STA5 NAV set by Intra-BSS Frame
STA5 NAV set by Inter-BSS Frame
UL MU
UL MU
UL MU
MU BA
STA5 can not consider NAV set by Inter-BSS Frame because NAV is overridden by AP
Trigger for 1,2,3,4
UL MU
UL MU
UL MU
UL MU
MU BA
STA5
UL MU
UL MU

## Slide 20: Appendix: NAV Consideration for UL MU Response
Ex: NAV set by TXOP duration in HE-SIGA [2]
  Note that similar examples under cascading TXOP can be constructed
Trigger for 1,2,3,4
AP
UL MU
STA1
UL MU
STA2
UL MU
STA3
STA4
Set NAV by Intra-BSS transmission
Trigger for 1,2,3,4
MU BA
STA4 NAV set by Intra-BSS Frame
STA4 NAV set by Inter-BSS Frame
UL MU
UL MU
UL MU
UL MU
MU BA
STA4 can not consider NAV set by Inter-BSS frame because NAV is overridden by Intra-BSS HE-SIGA
Trigger for 1,2,3,4
UL MU
UL MU
UL MU
UL MU
MU BA

## Slide 21: Appendix: Method 1 of Maintaining Two NAVs with One NAV Timer
When the current NAV set by Intra-BSS frame (i.e., Intra-BSS NAV) is updated by a frame which is not Intra-BSS frame or vice versus, STA calculates NAV difference value and stores it
  NAV difference value = Either (NAV of the received frame – Intra-BSS NAV) or (NAV of the received frame – Non-Intra-BSS NAV)
When the NAV needs to be checked (e.g., before UL MU response), the STA checks if two NAVs are valid or not
  E.g.,) Two NAVs are valid if the value of (current NAV – NAV difference value) is greater than 0. Otherwise, only the current NAV (e.g., Intra-BSS NAV or Non-Intra-BSS NAV) is valid
If two NAVs are valid, STA operates considering two NAVs. Otherwise, STA operates considering only the current NAV
  The current NAV is either Intra-BSS NAV or Non-Intra-BSS NAV

## Slide 22: Appendix: Method 2 of Maintaining Two NAVs with one Timer
Assume NAV1 is shorter than NAV2
Stores the difference of NAV2 with NAV1
Timer is set for the shorter NAV, i.e., NAV1
  If timer is greater than 0, NAV1 and NAV2 have not expired
When timer reaches 0, NAV1 expires, and we set the timer using the stored difference
NAV1
NAV2
Difference of NAV2 and NAV1
Timer counts toward end point of NAV1