## Slide 1: Scheduling Information for UL OFDMA Acknowledgement
Date: 2015-11-09
Authors:

## Slide 2: Background
The current SFD[1] allows that the scheduling information of OFDMA acknowledgement from STAs is contained in the MAC header of DL MPDU
  The contents of the scheduling information include UL PPDU length and RU allocation.
  Other scheduling information TBD
This simplified Trigger frame for UL OFDMA acknowledgement can be carried in HE Control field[2]
In this submission, other scheduling information is taken into account to trigger UL OFDMA ACK/BA frames

## Slide 3: OFDMA Acknowledgement
With allowing cascaded operation consisting of DL/UL MU PPDU transmission within TXOP, AP/STAs may exchange any types of frames efficiently and quickly
If Acknowledgement frames from multiple STAs are required which received DL OFDMA frame, OFDMA Acknowledgement as an immediate response can reduce overhead
Given Acknowledgement frames multiplexed with A-MPDU in UL OFDMA manner, some scheduling information can not be omitted
UL MU ACK/BA is TBD
BA
A-MPDU
DL A-MPDU
AP’s A-MPDU Trigger to STA3
AP’s A-MPDU with Trigger to STA1
AP’s A-MPDU with Trigger to STA2
BA
BA
BA
UL OFDMA Acknowledgement
TXOP
AP’s (MU MIMO) A-MPDU with Trigger to STA4 and STA5
…
…

## Slide 4: Simplified Trigger Field
Simplified Trigger Field is used instead of unicast Trigger Frame to save overhead.
Unicast Trigger Frame can control all of TXVECTORs of the uplink MU transmission.
To save overhead, simplified trigger field omits some of the TXVECTOR parameters and implicitly defines them.
We discuss TXVECTOR parameters needed for uplink MU transmission and determine which parameters is required to be transmitted and which parameters can be omitted.

## Slide 5: Parameters Needed for Uplink MU Transmission
Parameters for Data Transmission
  RU Allocation (TBD bits)
  MCS (4 bit)
  GI (2 bit)
  NSTS (3 bit)
  Starting NSTS (in case of MU-MIMO) (3 bit)
  NLTF (3 bits): number of LTF symbol
  LTF Type (1 bit)
  BF (1 bit)
  Coding (1 bit)
  PE (3 bits)
  DCM (1 bit)
  STBC (1 bit)
Parameters for Preamble format configuration
  SIG-A repetition (1 bit)
  Packet Duration (9 bits)
  TXOP Duration
  BW
Parameters in RED are agreed to be included in simplified Trigger Frame

## Slide 6: Potential Parameters in Simplified Trigger Field
Parameter | Comments | Necessary
RU Allocation | Already agreed to be included | YES
MCS | If simplified TF is used for Block ACK (BA) transmission, MCS may be derived based on PPDU length and RU allocation information. [3] Derived from PPDU length and RU allocation. | NO
GI | Same GI value used for DL PPDU that contains the simplified TR field may be applicable to UL PPDU. However, we may need to investigate whether use of 0.8us GI for UL MU is wise when DL uses 0.8us. UL OFDMA ACK/BA are from multiple STAs which may require longer GI to cover delay difference and inaccurate timing among different STAs. Therefore, explicit signaling may be needed. Choose among) Set to be same as DL transmission containing simplified TR field Some mapping between GI of DL transmission containing simplified TR field and GI of UL transmission. (e.g. 0.8us DL – 1.6us UL) Explicit signaling of 1 bit | MAYBE
NSS | Transmission of BA may be limited to 1 spatial stream. Set to NSS = 1. | NO

## Slide 7: Potential Parameters in Simplified Trigger Field (cont.)
Parameter | Comments | Necessary
Starting NSTS | Use of MU-MIMO for BA might be useful. However, MU-MIMO support 11ax is limited to 106 RU or above. So use cases might be limited. Set to SU-MIMO. | NO
NLTF | Number of LTF symbols for uplink MU transmission. Although [3] suggests that same value as DL can be used for UL. The number of LTF symbols for uplink MU has significant impact to uplink performance under the presence of residual CFO. For UL OFDMA ACK/BA frame transmission, the same number of NLTF as DL OFDMA can be burden considering AP can transmit DL OFDMA frame with large number of space-time-streams (e.g. NLTF = 4 or 8). The number of LTF symbols required for other UL MU transmissions may not match with DL transmission. Explicitly indicate NLTF of uplink MU transmission. | YES
BF | Even though beamforming is used in DL, it may not be available for UL. This is because UL beamforming requires sounding from the STA to AP, which may or may not have occurred prior to UL MU transmission. Therefore, we propose to not use beamforming. Some performance loss can be expected from not able to support beamforming. Set to BF = 0. | NO

## Slide 8: Potential Parameters in Simplified Trigger Field (cont.)
Parameter | Comments | Necessary
LTF Type | 2xLTF or 4xLTF indication. The channel conditions (selectivity of the channel) that required 2x or 4x LTF mode is likely to be same between DL and UL. However, the 2x and 4x LTF symbol duration does impact uplink transmission performance [4] under residual CFO. Choose between) Set to be same as DL transmission containing simplified TR field Explicit signaling of 1 bit | MAYBE
Coding | We may able to use the same coding scheme as DL transmission that contains the simplified trigger field. However, the payload size of the BA is small, and LDPC coding gain for such small payload size is small. Therefore, we can simply use BCC by default. For RU sizes that BCC does not support, 484, 996, 2*996 RU, we can use LDPC. Set to BCC by default. LDPC for 484, 996, 2*996 RU (if supported) | NO
PE | a-factor and PE ambiguity bit is agreed to be common in UL MU transmission [1]. Given that PE is a receiver capability, use of same parameters between DL and UL doesn’t make sense. Explicit signaling of 3 bits for PE. | YES

## Slide 9: Potential Parameters in Simplified Trigger Field (cont.)
Parameter | Comments | Necessary
STBC | Separate capability for Tx and Rx STBC exist. However, it is likely that Tx and Rx STBC capabilities are implemented together. The scenarios which require use of STBC in DL is likely going to require use of STBC in UL. Therefore, there are some reasons to use the same settings as DL transmission that contained simplified TR field. Choose between) Set to be same as DL transmission containing simplified TR field Set to STBC = 0 | NO
DCM | DCM was introduced to cope with narrow band interference. Even if DCM is applied for downlink transmission, the narrow band interference may not directly apply to uplink given that RU allocations for BA is going to be narrow. For larger RU allocations, if DL uses DCM, UL should use DCM as well. It should be noted that DCM may be a optional feature and some STAs may not have implemented such feature. Choose between) Set to be same as DL transmission containing simplified TR field Set to DCM = 0 | NO
Packet Duration | Already agreed to be included | YES

## Slide 10: Potential Parameters in Simplified Trigger Field (cont.)
Parameter | Comments | Necessary
SIG-A repetition | SIG-A repetition is used to extend range of SIG-A for intended users. The link quality that required use of SIG-A repetition for DL is likely to also apply for UL. Set to be same as DL transmission containing simplified TR field | NO
TXOP Duration | The downlink frame that contains the simplified TR field already includes TXOP duration field. Each STA can compute the TXOP duration to be configured in SIG-A of the uplink MU transmission. Information already informed. | NO
BW | BW is not strictly needed for actual UL OFDMA data transmission. However, this information may be needed for transmitting the preamble portion of the UL transmission and determining the transmit spectral mask. In cascading OFDMA procedure, the UL transmission BW should be identical to DL transmission. However, there might be cases where AP may want to control the UL transmission BW. Choose between) Set to be same as DL transmission containing simplified TR field Determine BW based on allocated RU position Explicit Signaling | MAYBE

## Slide 11: Summary of Necessity of Parameter Signaling
Parameter | # Bits | Necessary
RU Allocation | TDB | YES
MCS | - | NO
GI | 1 | MAYBE
NSS | - | NO
Starting NSTS | - | NO
NLTF | 3 | YES
BF | - | NO
LTF Type | 1 | MAYBE
Coding | - | NO
PE | 3 | YES
STBC | - | NO
DCM | - | NO
Parameter | # Bits | Necessary
SIG-A repetition | - | NO
Packet Duration | 9 | YES
TXOP Duration | - | NO
BW | 2 | MAYBE

## Slide 12: How Many Bits Left for RU Allocation?
Based on summary in slide 11, if we include all the YES parameters (i.e. NLTF, PE), we have 15 bits left in HT control.
    VHT/HE (2) + TBD header (TBD) + UL PPDU length (9) + RU allocation (TBD) +NLTF (3) + PE (3) = 17 + TBD bits = 4 Bytes >>> TBD = 15
Out of 15 bits, Control ID and EOH subfield proposed in [2] may potentially take away 6 bits. Leaving 9 bits left.
      VHT/HE (2) + Control ID (5) + EOH (1) + UL PPDU length (9) + RU allocation (TBD) +NLTF (3) + PE (3) = 23 + TBD bits = 4 Bytes >>> TBD = 9
VHT (1)
HE (1)
Control ID
EOH (0)
PPDU length
PE
NLTF
OFDAM acknowledgement scheduling information
9
TBD
3
3
RU
allocation
reserved
TBD
TBD

## Slide 13: Is Inclusion of NLTF and PE Parameter Possible?
Required Bitwidth for RU Allocation
160MHz (137): 26 RU (74), 52 RU (32), 106 RU (16), 242 RU (8) , 484 RU (4), 996 RU (2), 2*996 RU (1)
In order to support worst case 137 combinations (160 MHz) we will need 8 bits.
Conclusion:
Inclusion of (NLTF, PE) parameters to simplified trigger frame poses no problems.

## Slide 14: Summary
Scheduling information of OFDMA acknowledgement from STAs is contained in HE Control field in the MAC header of DL MPDU
Considering UL OFDMA A-MPDU multiplexed, additional contents in simplified Trigger Frame was discussed.
We propose to also include NLTF (number of LTF symbols) and PE parameters to the simplified trigger field.
  Inclusion of such parameters to not pose any restrictions to RU allocation signaling.
TGax will also need to decide on additional signaling of BW, GI, and LTF type subfields, and decide on default values for parameters that are derived implicitly.

## Slide 15: Straw Poll #1
Do you agree to add the following to the SFD?
Scheduling information for UL OFDMA Acknowledgement from STA may be contained within the “HE variant of the HT Control Field”

## Slide 16: Straw Poll #2
Do you agree to add the following to the SFD?
HE variant of HT control field that contains scheduling information for UL MU Acknowledgement from STAs shall also include
  number of LTF symbols, NLTF,
  and PHY padding and packet extension signaling, PE,
for UL MU transmission. The signaling format of the scheduling information for UL MU Acknowledgement is defined as
VHT (1)
HE (1)
TBD
PPDU length
PE
NLTF
9
TBD
3
3
RU
allocation
bits
1
1
TBD

## Slide 17: References
[1] 11-15/0132r9, Specification Framework for TGax
[2] 11-15/0121r0, HE A-Control field
[3] 11-15/1123r1, Acknowledgement to DL MU
[4] 11-15/0349r0, HE-LTF Proposal
[5] 11-15/1068r0, Reliable Dual Sub-Carrier Modulations (DCM) for HE-SIG-B and Data