## Slide 1: A method of transmitting Multi-STA Block ACK
Date: 2015-11-08
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jay (Hyunhee) Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Authors:

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com
November 2015

## Slide 3: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
November 2015

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
November 2015

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
November 2015

## Slide 7: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
November 2015

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com
November 2015

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
November 2015

## Slide 10: Introduction
SFD texts for Multi-STA BA and OFDMA BA [1]
  The spec shall define a control frame that can carry ACK/BA information for multiple STAs. [Motion 5, January 9, 2015]
  The spec shall allow DL OFDMA transmission of BA/ACK frame in response to UL OFDMA transmissions. [Motion 7, March 6, 2015]
Multi-STA BA generally is sent by using non-HT PPDU format like ACK/BA
Multi-STA BA can also be sent using 11ax PPDU for large coverage support or when there are only HE STAs in a BSS
We propose OFDMA M-BA as a method to transmit the M-BA using 11ax PPDU format
  It also provides less overhead compared to M-BA frame (using non-HT PPDU) or DL OFDMA ACK/BA[1]

## Slide 11: Background
ACK/BA TX in legacy system [2]
  In legacy system ACK/BA is sent via the same bandwidth as the bandwidth of the received frame
Received frame
20MHz
ACK/BA
Received frame
40MHz
ACK/BA
ACK/BA
Received frame
80MHz
ACK/BA
ACK/BA
ACK/BA
ACK/BA
EIFS
ACK/BA
ACK/BA
Non-HT
HT/VHT
Non-HT
VHT

## Slide 12: M-BA TX using SU PPDU (1/2)
M-BA TX using SU PPDU
  AP can send the M-BA via the full bandwidth which Trigger frame is sent
Example of SU M-BA TX
Trigger
Frame
UL MU Frame (STA1)
UL MU Frame (STA2)
UL MU Frame (STA3)
UL MU Frame (STA4)
Trigger
Frame
UL MU Frame (STA5)
UL MU Frame (STA6)
UL MU Frame (STA7)
UL MU Frame (STA8)
40MHz
SU M-BA (STA1~8)

## Slide 13: M-BA TX using SU PPDU (2/2)
While STA 1 sends a UL frame via the resource allocated by trigger frame, OBSS STA(hidden from AP) may send a frame through the sub-channels where STA1 does not send
In this case the OBSS’s TX can interfere the M-BA reception of the STA1
STA 1 can not receive the M-BA that cannot be protected by EIFS operation
The reliability of M-BA will be lower than that of ACK/BA in legacy system
Trigger
Frame
Trigger
Frame
Trigger
Frame
Trigger
Frame
UL MU frame of STA 1
SU M-BA
(STA1~N)
* One of easy methods to solve the ACK reliability issue is sending M-BA frame via the sub-channel in which UL MU frame is received (like legacy)
OBSS STA’s transmission
UL MU frame of STA 2
Frame RX/TX in STA1
80MHz

## Slide 14: M-BA TX using OFDMA PPDU (1/3)
AP sends M-BA frames using OFDMA PPDU in response to UL MU PPDU.
Case 1) M-BA can be sent via 242 tone unit
Trigger
Frame
UL MU Frame (STA1)
UL MU Frame (STA2)
UL MU Frame (STA3)
UL MU Frame (STA4)
OFDMA M-BA (STA1~4)
Trigger
Frame
UL MU Frame (STA5)
UL MU Frame (STA6)
UL MU Frame (STA7)
UL MU Frame (STA8)
OFDMA M-BA (STA5~8)
242 tone unit
40MHz
Example 1
Trigger
Frame
UL MU-MIMO Frame (STA1~STA4)
OFDMA M-BA (STA1~4)
Trigger
Frame
UL MU Frame (STA5)
UL MU Frame (STA6)
UL MU Frame (STA7)
UL MU Frame (STA8)
OFDMA M-BA (STA5~8)
242 tone unit
Example 2

## Slide 15: M-BA TX using OFDMA PPDU (2/3)
Case 2) M-BA can be sent via 106 tone unit
  When UL MU-MIMO fame is received through 106 tone unit
Trigger
Frame
UL MU-MIMO Frame (STA1, STA2)
UL MU-MIMO Frame (STA3, STA4)
OFDMA M-BA (STA1,2)
Trigger
Frame
UL MU Frame (STA5)
UL MU Frame (STA6)
UL MU Frame (STA7)
UL MU Frame (STA8)
OFDMA M-BA (STA5~8)
106 tones unit
40MHz
Example of OFDMA M-BA
OFDMA M-BA (STA3,4)

## Slide 16: M-BA TX using OFDMA PPDU (3/3)
Since OFDMA M-BA is sent via the sub-channel in which the UL MU frame was received, the reliability of OFDMA M-BA will be same as that of legacy ACK/BA
  That is, the reliability of OFDMA M-BA will be better than SU M-BA
Trigger
Frame
Trigger
Frame
Trigger
Frame
Trigger
Frame
UL MU frame of STA a
M-BA
(STA a~ b)
M-BA
(STA c~ d)
M-BA
(STA e~ f)
M-BA
(STA g~ h)
Trigger
Frame
Trigger
Frame
Trigger
Frame
Trigger
Frame
M-BA
(STA a~ b)
M-BA
(STA c~ d)
M-BA
(STA e~ f)
M-BA
(STA g~ h)
OBSS STA ’s transmission
UL MU frame of STA b
RX/TX in STA a
OBSS STA ’s transmission
UL MU frame of STA e
UL MU frame of STA f
RX/TX in STAe
80MHz

## Slide 17: Example of OFDMA M-BA Signaling
Using Group ID
  M-BA is a frame which is intended to multiple STAs (like multicast data)
  A part of AIDs (e.g., unused AIDs) can used as Group ID
  Group ID (s) for M-BA (s) is (are) indicated to STAs before receiving M-BA
    E.g.,) Group ID(s) for M-BA(s) is (are) temporally allocated by Trigger frame
Other methods can be possible
HE-SIG B
RA of Group ID = 1
RA of Group ID 2
OFDMA M-BA PPDU (Group ID)
M-BA MPDU
(STA 1~ 3)
M-BA MPDU
(STA 4~ 5)
L-STF/LTF/SIG, HE-SIG A
HE-STF/HE-LTF
* RA: Resource allocation

## Slide 18: Overhead comparison (1/4)
Assumptions
  N: # of STAs (2, 4, 8, 16 (>=40MHz)), MCS0, Single stream
  GI (0.8 μs), 11a Preamble (20 μs ), RL-SIG(4 μs), HE-SIG A (4 μs), HE-SIG B(12 μs)
  Tones (242/484/994 in 20/40/80MHz), HE-STF (4 μs, 1x), HE-LTF (8 μs, 2x)
  MAC frame size
    M-BA(11a) : 22 + 12 * N bytes (N: # of Users)
    BA : 32 bytes
PPDU Duration calculation
  M-BA (non-HT PPDU format)
    Time : Ceiling[((22+12N)*8+16+6)/(48*1/2)]*4 μs
    Duplicated transmission in each 20 MHz
    Preamble overhead(11a): 20 μs

## Slide 19: Overhead comparison (2/4)
PPDU Duration calculation (HE PPDU)
  OFDMA BA (O-BA)
    Time (20MHz): ceiling[(32*8+16+6)/(242/N*1/2)]*13.6 μs, where N=2, 4, 8
    Time (40MHz): ceiling[(32*8+16+6)/(484/N*1/2)]*13.6 μs, where N=4, 8, 16
    Time (80MHz): ceiling[(32*8+16+6)/(994/N*1/2)]*13.6 μs, where N=8, 16, 32
    Preamble overhead(11a + 11ax): 52 μs
  OFDMA M-BA (O-M-BA)
    M: the total number of 242 tones units in BW (i.e., 1 in 20MHz, 2 in 40MHz, 4 in 80MHz)
    Time of M-BA
      Time (20MHz): Ceiling[((22+12(N/M))*8+16+6)/(242*1/2)]*13.6 μs, where N= 2, 4, 8
      Time (40MHz): Ceiling[((22+12(N/M))*8+16+6)/(242*1/2)]*13.6 μs, where N= 4, 8, 16
      Time (80MHz): Ceiling[((22+12(N/M))*8+16+6)/(242*1/2)]*13.6 μs, where N= 8, 16, 32
    Preamble overhead(11a + 11ax): 52 μs
  SU M-BA
    Time (40MHz): Ceiling[((22+12N)*8+16+6)/(484*1/2)]*13.6 μs, where N=4, 8, 16
    Time (80MHz): Ceiling[((22+12N)*8+16+6)/(996*1/2)]*13.6 μs, where N=8, 16, 32
    Preamble overhead(11a + 11ax): 52 μs

## Slide 20: Overhead comparison (3/4)
BW (MHz) | N | M-BA (μs) | O-BA (μs) | O-M-BA (μs) | Gain (%) of O-M-BA | 
 |  |  |  |  | Vs. M-BA | Vs. O-BA
20 | 2 | 88 | 120 | 106.4 | -20.9 | 11.3
 | 4 | 120 | 188 | 120 | 0 | 36.2
 | 8 | 184 | 310.4 | 160.8 | 12.6 | 48.2
40 | 4 | 120 | 120 | 106.4 | 11.3 | 11.3
 | 8 | 184 | 188 | 120 | 34.8 | 36.2
 | 16 | 312 | 310.4 | 160.8 | 48.5 | 48.2
80 | 8 | 184 | 120 | 106.4 | 42.2 | 11.3
 | 16 | 312 | 174.4 | 120 | 61.5 | 31.2
 | 32 | 568 | 296.8 | 160.8 | 71.7 | 45.8
Chart: 80MHz, N= 16
| M-BA | O-BA | S-M-BA
80MHz | 312 | 188 | 120
(μs)
O-M-BA
61.5 %
31.2 %
* M-BA (11a PPDU) vs. OFDMA BA (O-BA) vs. OFDMA M-BA(O-M-BA)

## Slide 21: Overhead comparison (4/4)
Assumptions
  11ax Symbol length: 13.6us (CP size = 0.8us)
  Even distribution of STAs, N (# of STAs): 4/8/16/32
BW (MHz) | N | SU M-BA (μs) | OFDMA M-BA (μs) | Difference (us)
40 | 4 | 92.8 | 106.4 | 13.6
 | 8 | 106.4 | 120 | 13.6
 | 16 | 160.8 | 160.8 | 0
80 | 8 | 79.2 | 106.4 | 27.2
 | 16 | 106.4 | 120 | 13.6
 | 32 | 147.2 | 160.8 | 13.6
UL MU Frames, 4 STAs
(STA1~STA4)
40MHz
242 tones unit
The difference between SU M-BA and OFDMA M-BA is not big (almost 1 symbol)
Example of even distribution
(40MHz, 8 STAs)
UL MU Frames, 4 STAs
(STA4~STA8)
* SU M-BA vs. OFDMA M-BA

## Slide 22: Conclusion
We propose to allow the AP to send M-BA using OFDMA PPDU as a method to send M-BA using HE PPDU format
  Advantages
    OFMDA M-BA will provider the reliability very similar to legacy ACK/BA
      i.e., it provides better reliability than M-BA using HE SU PPDU
    It provides less overhead than M-BA using non-HT PPDU and OFDMA BA
      Up to 71.7% compared to M-BA using non-HT PPDU
      Up to 48.2% compared to OFDMA BA

## Slide 23: Reference
[1] 11-15-0132-09-00ax-spec-framework
[2] IEEE 802.11REVmc_D4.3

## Slide 24: Straw Poll
Do you agree to add to SFD?
  The spec shall allow DL OFDMA transmission of Multi-STA Block ACK (M-BA) frame in response to UL MU PPDUs
  Yes
  No
  Abstain

## Slide 25: Appendix: Examples of using OFDMA M-BA (1/2)
Example 1: Multiplexing M-BA and BA
  Can reduce the padding overhead
Trigger
Frame
UL Frame (STA1)
UL Frame (STA2)
UL Frame (STA3)
UL Frame (STA4)
OFDMA M-BA (STA1~4)
Trigger
Frame
UL Frame (STA5)
OFDMA BA (STA5)
Example of multiplexing M-BA and BA using OFDMA PPDU
Padding
Trigger
Frame
UL Frame (STA1)
UL Frame (STA2)
UL Frame (STA3)
UL Frame (STA4)
OFDMA-BA
Trigger
Frame
UL Frame (STA5)
OFDMA BA (STA5)
40MHz
Example of OFDMA BA
Padding
OFDMA-BA
OFDMA-BA
OFDMA-BA
Padding Overhead
Padding Overhead
UL Frame (STA4)

## Slide 26: Appendix: Examples of using OFDMA M-BA (2/2)
Example 2: Multiplexing M-BA and Data
Trigger
Frame
UL Frame (STA1)
UL Frame (STA2)
UL Frame (STA3)
UL Frame (STA4)
M-BA (STA1~4)
Trigger
Frame
UL Frame (STA5)
Example of multiplexing M-BA and Data using OFDMA PPDU
Data (STA5)
BA (STA5)