## Slide 1: Implicit Sounding for HE WLAN
Date: 2015-11-09
Authors:

## Slide 2: Abstract
We will discuss on support of implicit sounding for APs with self antenna calibration capability.

## Slide 3: Explicit vs. Implicit Sounding
Beamformer (TX)
Beamformee (RX)
NDPA
NDP
CSI Feedback
Explicit Sounding
Beamformer (TX)
Beamformee (RX)
PPDU
HE-LTF must be full dimension (i.e. full rank)
Implicit Sounding (assume antennas are calibrated)
Size of feedback may vary between 104 Bytes ~ 450 KBytes

## Slide 4: Uncalibrated Antenna Chains
If uncalibrated
  ATX ≠ ARX, BTX ≠ BRX
  BRX HAB ATX ≠ (ARX HABT BTX )T
ATX
ARX
BTX
BRX
KA
KB
HAB
Calibration Matrix
Calibration Matrix
If not calibrated ATX and ARX do not match
Beamformer
Beamformee
TX
TX
RX
RX

## Slide 5: Implicit Sounding without Antenna Calibration
Antenna calibration procedure is the main reason implicit sounding becomes an unattractive solution.
  Calibration procedure between each AP and STA requires several exchanges of information. Resulting in large overhead.
Is spec-supported antenna calibration procedure absolutely necessary for implicit sounding?
  Quick answer: No
  Simulation results show antenna calibration at the AP side is sufficient for SU/MU beamforming.
  STA side antenna calibration is not necessary.
  APs with self-antenna calibration do not require any additional procedure support from 802.11 specification.

## Slide 6: Few Antenna Self-Calibration Methods
AP
External Calibration Device
connected either wired or wireless
Feedback Loop
Method 3) Using external calibration device
(possible in enterprise deployments)
Method 1) chip manufactoring level calibration
Method 2) On-chip calibration loop
DUT
in
out
Test Module
Feedback loop
(adjusts firmware)
Baseband
Tx RF
Rx RF
Feedback loop
Note: Typically very complex and difficult to implement
Note: One time adjustment
All of these methods are available now and some vendors may have already implemented them at the AP

## Slide 7: Beamforming Simulation Results
Simulation Parameters
Antenna Setup: Tx-Rx: 4x2 and 8x2
Channel Model: TGac
BW: 20MHz (assumed 64 FFT)
STA positions: Equal distance without shadowing (i.e. equal average SNR)
Performance metric: Average sum rate computed using capacity formula, log2(1+SINR)
Feedback Latency: zero latency assumed
Channel estimation (CE): CE error modeled both for implicit and explicit FB, CE gain assumption: 6 dB

## Slide 8: Simulated Algorithms & Plot Legends
Simulated Algorithms
  DPC bound with perfect channel knowledge
    assumed equal power loading between users
  SU-MIMO based on right singular vector/matrix precoding
    Implicit FB
    Explicit FB with Low fidelity SU, 2 bit PSI, 4 bit PHI
    Explicit FB with High fidelity SU, 4 bit PSI, 6 bit PHI (used as reference in MU-MIMO plots)
  MU-MIMO based on modification of MSE minimization precoding
    Implicit FB
    Explicit FB with Low fidelity MU, 5 bit PSI, 7 bit PHI
    Explicit FB with High fidelity MU, 7 bit PSI, 9 bit PHI
Plot Legend
  MU BFer [±X dB, ±Y°] Bfee [±X dB, ±Y°]
  Beamformer side (i.e. AP) or each Beamformee (i.e. STA) has mis-calibrated Tx and Rx antennas. Each RF chain may have up to ±X dB difference in amplitude and ±Y° difference in phase.

## Slide 9: Simulation Results (1/2)
Effect of Tx/Rx Antenna calibration of Beamformer (i.e. AP)
with completely un-calibrated Beamformee (i.e. STA)
Effect of Tx/Rx Antenna calibration of Beamformer (i.e. AP)
With perfectly calibrated Beamformee (i.e. STA)
Conclusion: Tx/Rx antenna calibration at the STA side is NOT essential for obtaining MU-MIMO performance
It is less sensitive to mis-calibration as the receiver has enough degree of freedom to reject interference (Ntotal,SS = NRX)

## Slide 10: Simulation Results (2/2)
Effect of Tx/Rx Antenna calibration of Beamformer (i.e. AP)
with completely un-calibrated Beamformee (i.e. STA)
Effect of Tx/Rx Antenna calibration of Beamformer (i.e. AP)
With perfectly calibrated Beamformee (i.e. STA)
Loss from un-calibrated Beamformer side is higher when Tx antenna dimension is larger (e.g. 8 Tx antenna)
Still with acceptable performance when AP antenna can be self-calibrated to within ±0.5 dB amplitude and ±5°phase.
It is more sensitive to mis-calibration as the receiver has enough degree of freedom to reject interference (Ntotal,SS > NRX)

## Slide 11: Support for Implicit Sounding in 802.11
In 802.11n, implicit sounding is supported by a procedure that is based of message exchanges for antenna calibration
However, with the efficient calibration methods used in industry, above 11n antenna calibration procedure did not become a necessity in practice
In 802.11ac, the legacy implicit sounding mechanism was not updated and as a result implicit sounding is limited to implementation-specific solutions and for one transmit/receive antenna cases

## Slide 12: Implicit Sounding in 11ax
Given an AP with calibrated antenna chains, with either of the methods mentioned earlier, it takes the following to harvest the efficiency of implicit sounding:
  A STA sends a frame with full-dimension HE-LTF to a calibrated AP, assuming the AP is ready to process it accordingly for subsequent SU/MU BF, or
  A STA, instead of CSI report, sends NDP with full-dimension HE-LTF to a calibrated AP during a sounding period.
It would more desirable if the possibility of a response frame with full-dimension HE-LTF is part of the HE sounding procedure

## Slide 13: Conclusion
In case AP has self-antenna calibration capability (or at least has antennas that are calibrated within certain accuracy), implicit sounding is a very practical and efficient method of obtaining channel state information.
Performance
  Almost no loss is observed for SU-MIMO case with implicit sounding for APs with self-antenna calibration.
  Comparable MU-MIMO performance between explicit and implicit sounding with APs with self-antenna calibration.
Minimal specification support is needed for implicit sounding for APs with self-antenna calibration.

## Slide 14: Straw Poll #1
Do you agree that:
Implicit sounding is supported for APs with self-antenna calibration capability.
  Note: no explicit procedure to enable antenna calibration for AP or STA is supported in 11ax.
Y/N/A

## Slide 15: Straw Poll #2
Do you agree to include into 11ax SFD that:
Beamforming sounding procedure shall provide a mechanism to solicit a full dimensioned (i.e. full rank) NDP response from beamformee.
Y/N/A

## Slide 16: APPENDIX: Additional Simulation Results

## Slide 17
4x2 - 1SS - SU-MIMO

## Slide 18
4x2 - 1SS - MU-MIMO
(2 STAs)

## Slide 19
8x2 - 1SS - SU-MIMO

## Slide 20
4x2 - 1SS - MU-MIMO
(4 STAs)

## Slide 21
4x2 - 2SS - SU-MIMO

## Slide 22
4x2 - 2SS - MU-MIMO
(2 STAs)

## Slide 23
8x2 - 2SS - SU-MIMO

## Slide 24
8x2 - 2SS - MU-MIMO
(4 STAs)