## Slide 1: HE-SIG-B Contents
Date: 2015-11-09
Authors:
Name | Affiliation | Address | Phone | Email
Le Liu | Huawei | F1-17, Huawei Base, Bantian, Shenzhen | +86-18028794213 | liule@huawei.com
Ming Gan |  |  |  | ganming@huawei.com
Meilu Lin |  |  |  | linmeilu@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | zhangjiayin@huawei.com
Jun Luo |  |  |  | jun.l@huawei.com
Yingpei Lin |  |  |  | 
 |  |  |  | linyingpei@huawei.com
Jiyong Pang |  |  |  | pangjiyong@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
Junghoon Suh |  |  |  | Junghoon.Suh@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yi Luo |  |  |  | Roy.luoyi@huawei.com

## Slide 2: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Tianyu Wu | Mediatek USA |  |  | tianyu.wu@mediatek.com
Thomas Pare |  | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Leo Montreuil | Broadcom |  |  | leo.montreuil@broadcom.com
Ron Porat |  |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Andrew Blanksby |  |  |  | 
Matthias Korb |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 10: Re-cap
Agreement on HE-SIG-B common field [1]
  The RU allocation signaling in the common field of HE-SIG-B signals an 8 bit per 20 MHz PPDU BW for signaling
    The RU arrangement in frequency domain
    Number of MU-MIMO allocations: The RUs allocated for MU-MIMO and the number of users in the MU-MIMO allocations
  The exact mapping of the 8 bit to the arrangement and the number of MU-MIMO allocations is TBD.
  Signaling for the center 26 unit in 80 MHz is TBD.
Agreement on HE-SIG-B user specific field [1]
  The user specific subfields of HE-SIG-B containing the per user dedicated information include the following fields
    STA-ID
    For single-user allocations in a RU: NSTS (Number of Spatial Streams), TxBF (transmit beamforming ), MCS (Modulation and Coding Scheme) and Coding (Use of LDPC)
    For each user in a multi-user allocation in a RU: Spatial Configuraiton Fields, MCS and Coding.
  Other fields are TBD.

## Slide 11: In this presentation
We further discuss the details based on the agreements from the last meeting
  In HE-SIG-B common
    Based on the tone plan and RU pattern in 20MHz [2], we design ‘the exact mapping of the 8 bit to the arrangement and the number of MU-MIMO allocations’
  In HE-SIG-B user specific field
    Specify the size of STA-ID
    Add DCM indication for data portion with reliable performance
7
DC
26
26
26
26
26
26
26
52
52
52
52
26
242 + 3 DC
102+4 pilots
102+4 pilots
1
1
1
1
13
1
1
1
1
13
13
13
5 Edge
5 Edge
5 Edge
5 Edge
6 Edge
6 Edge
6 Edge
6 Edge
7
DC
13
13
7
DC
HE20 with 7DC for OFDMA

## Slide 12: OFDMA RU Allocation Signalling
In case of OFDMA transmission, we design the RU allocation signaling considering the following typical cases  176 cases
  All the possible combinations of 26/52/106/242-RU allocation within 20MHz
  Also the allocation of 484/996/2*996-RU allocation larger than 20MHz
  MU-MIMO allocation (on RU>=106) position and the number of MU-MIMO STAs
    Separately indicate the MU-MIMO allocation on the CHs within the RU>242.
    The total number of MU-MIMO STAs is the summation of the number of MU-MIMO STAs per 20MHz on the RU>242.
For partial OFDMA (with unallocated RU), the indication of all the possible combination in HE-SIG-B common costs unbearable overhead.
  There are already 2448 combination cases of partial OFDMA if RU<106.
  Whether to prioritize and indicate some special cases is TBD.

## Slide 13: Hierarchical Indication RU allocation signaling
    Note:
    ‘yyy’ indicate the number of STAs on the RU (1-8)
    If ‘b=0’, ‘aa’ is to differentiate 242-RU (00), 484-RU (01), 996-RU (10) or 2*996-RU(11).
    If ‘b=1’, ‘11,1xxxx’ entries are TBD, e.g., used for special cases such as load balancing with 0STA on 484 and 996-RU
11,b,aa,yyy
(8bits)
010,xx,yyy for (106)+(<106)
000,0,1111
000,0,0000
>=242 or 106+106
‘0’
Left 106
Right 106
52
52
52
52
26
26
26
26
26
26
26
26
26
26
26
2nd bit=‘0’
3rd bit=‘0’
‘0’
‘0’
‘0’
‘0’
‘1’
2nd bit= ‘1’
3rd bit= ‘1’
‘1’
‘1’
‘1’
‘1’
2nd bit
>=
242
106
106
26
‘1’
‘0’
2nd bit
3rd bit
10,yyy,yyy
(8bits)
1st bit
001,xx,yyy for (<106)+106
‘000,0,xxxx’ for (<106)+(<106)
Summary of 8-bit RU allocation signaling:
‘000,0,xxxx’: 26/52 combinations;
‘010,xx,yyy’: 106 on the left +(26/52 combinations) on the right
‘001,xx,yyy’: (26/52 combinations) on the left + 106 on the right
‘10,yyy,yyy’: 106 on the left +106 on the right
‘11,0,aa,yyy’: large RU with (>242)
TBD entries: ‘011,xxxx’, ‘000,1,xxxx’, ‘11,1,xxxx’

## Slide 14: Lookup Table for 8-bit RU allocation signaling
8-bit hierarchical mapping form is equivalent as a table with unique index
8 bits indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Num of entries
000 0 0000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 0001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 0010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 0011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 0100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 0101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 0110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 0111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
000 0 1000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 1001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 1010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 1011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 1100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 1101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 1110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 1111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
000 1 xxxx | Definition TBD |  |  |  |  |  |  |  |  | 16
00100 yyy | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 8
00101 yyy | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 8
00110 yyy | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 8
00111 yyy | 52 |  | 52 |  | 26 | 106 |  |  |  | 8
01000 yyy | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 8
01001 yyy | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 8
01010 yyy | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 8
01011 yyy | 106 |  |  |  | 26 | 52 |  | 52 |  | 8
011 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
10 yyy yyy | 106 |  |  |  | 26 | 106 |  |  |  | 64
11 0 00yyy | 242 |  |  |  |  |  |  |  |  | 8
11 0 01yyy | 484 |  |  |  |  |  |  |  |  | 8
11 0 10yyy | 996 |  |  |  |  |  |  |  |  | 8
11 0 11yyy | 2*996 |  |  |  |  |  |  |  |  | 8
11 1 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
Note: ‘yyy’ = 000~111 indicates number of MU-MIMO STAs.
Definition for entries with ‘x’ bits are TBD.

## Slide 15: STAID Options for HE-SIG-B
STAID is to identify the user specific subfields for the tended STAs.
  Option1: MAC address (48bit)
    unique in the whole network, no ambiguity.
    but unbearable overhead in PHY preamble
  Option2: AID (11bit)
    unique within BSS,
    already exist in MAC
    moderate overhead, not always fully used
  Option3: new defined STAID
    assigned STAID to the active STA, e.g. STA with MU capability
    Small overhead or variable overhead
    AP require special mechanism to manage these ID to avoid ambiguity in scheduling.

## Slide 16: STA ID Ambiguity within BSS
Although 9-bit AID is used to generate PAID in 11ac, STAs may have same PAID when the number of STA in one BSS is large (even sleeping STA occupies AID), especially for 11ax dense scenarios.
The scheduler must set restriction not to schedule more than one STA with same PAID considering the complexity in STA.
Otherwise, we have to rely on the RA in MAC header to let the STA finally identify the packet within BSS.
  The overall overhead is not saved.
  It is also not energy efficient for the STA with same PAID because he must decode the PSDU not for himself.
Opt2 of 11-bit STAID is preferred to uniquely indicate the scheduled STA.

## Slide 17: DCM for Data payload
Dual Sub-carrier Modulation (DCM) modulates the same information on a pair of sub-carrier n and m separated far apart, which is beneficial for performance improvement of SIGB as well as data portion [3].
  Extend range for outdoor scenarios by enhancing the PER performance
  Improve robustness against narrow-band interferences under dense deployment
    MU-MIMO detection over RU>=106 also needs robust against instantaneous narrow-band interference.
We has passed the motion [Motion 12, September 12, 2015]
  Move to include dual sub carrier modulation (DCM) schemes for HE-SIGB and Payload in the SFD
    DCM schemes are optional
    DCM schemes are only applied to BPSK, QPSK, and 16-QAM modulations

## Slide 18: DCM Indication
For each user’s data portion, we need 1-bit DCM indication in per user dedicated info in HE-SIG-B.
  The per user dedicated info (in SIG-B) includes the following:
    STA_ID + the following fields
      For allocation that includes one user – Nsts, TxBF, MCS, DCM, Coding
      For MU-MIMO allocation – Spatial config, MCS, DCM, Coding
    Other fields are TBD.
DCM bit per-user specific field of HE-SIGB | Modulation Schemes of Payload
1 | MCS x with DCM
0 | MCS x
1-bit DCM bit indicates the modulation of payload

## Slide 19: Conclusion
In HE-SIG-B common, we design ‘the exact mapping of the 8 bit to the arrangement and the number of MU-MIMO allocations’ per 20MHz.
  The 8-bit lookup table is summarized in slide 12.
In HE-SIG-B user specific field, we propose
  STAID size is 11bits to uniquely indicate the tended STA.
  For SU/MU-MIMO allocation,1-bit DCM indication is added for data portion with reliable performance.

## Slide 20: References
[1] 11-15-1066-00-00ax-he-sig-b-contents
[2] 11-15-0330-05-00ax-ofdma-numerology-and-structure
[3] 11-15-1068-01-00ax-reliable-transmission-schemes-for-he-sig-b-and-data

## Slide 21: SP#1
Do you agree to modify the text in IEEE 802.11ax SFD(r9) as follows
  Change “The exact mapping of the 8 bit to the arrangement and the number of MU-MIMO allocations is TBD.” to “The mapping of the 8 bit to the arrangement and the number of MU-MIMO allocations is defined in the following lookup table.”
Note: ‘yyy’ = 000~111 indicates number of MU-MIMO STAs.
Definition for entries with ‘x’ bits are TBD.
8 bits indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Num of entries
000 0 0000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 0001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 0010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 0011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 0100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 0101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 0110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 0111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
000 0 1000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 1001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 1010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 1011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 1100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 1101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 1110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 1111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
000 1 xxxx | Definition TBD |  |  |  |  |  |  |  |  | 16
00100 yyy | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 8
00101 yyy | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 8
00110 yyy | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 8
00111 yyy | 52 |  | 52 |  | 26 | 106 |  |  |  | 8
01000 yyy | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 8
01001 yyy | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 8
01010 yyy | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 8
01011 yyy | 106 |  |  |  | 26 | 52 |  | 52 |  | 8
011 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
10 yyy yyy | 106 |  |  |  | 26 | 106 |  |  |  | 64
11 0 00yyy | 242 |  |  |  |  |  |  |  |  | 8
11 0 01yyy | 484 |  |  |  |  |  |  |  |  | 8
11 0 10yyy | 996 |  |  |  |  |  |  |  |  | 8
11 0 11yyy | 2*996 |  |  |  |  |  |  |  |  | 8
11 1 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32

## Slide 22: SP#2
Do you agree to add the STAID size in the user specific subfields of HE-SIGB is 11bits?
Y
N
A

## Slide 23: SP#3
Do you agree to add a DCM subfield (1-bit) to the user-specific subfields of HE-SIG-B in IEEE 802.11ax SFD(r9) (as shown in red)
  For single-user allocations in a RU: NSTS (Number of Spatial Streams), TxBF (transmit beamforming ), MCS (Modulation and Coding Scheme), DCM (Dual Sub-Carrier Modulation) and Coding (Use of LDPC)
  For each user in a multi-user allocation in a RU: Spatial Configuration Fields, MCS, DCM and Coding
Y
N
A