## Slide 1: Improving Spatial Reuse During OBSS UL MU Procedure
Date: 2015-11-09
Authors:

## Slide 2: Introduction
According to the current SFD [1],
  HE STA can determine whether HE PPDU is from OBSS using BSS Color in HE-SIG-A field.
  Revising NAV may be considered depending on conditions at the recipient of the ongoing OBSS frame.
The conditions for revising NAV considering the recipient of OBSS frame have not been defined so far.
We need further discussions on considering the potential interference to the recipient of OBSS frame to improve spatial reuse.
In this contribution, it is shown that revising NAV is possible during OBSS UL MU procedure.

## Slide 3: Recap: Revising NAV During TXOP [2]
With the current CCA rule
  STA determines the channel status regardless of the destination of the frame.
  Even the transmission to OBSS hidden node is blocked.
    Although transmission of STA C may not interfere the frame from STA A to STA B, if STA A is in the coverage of STA C, then STA C does not transmit a frame.
With the recipient consideration
  Most of frame exchanges are multiple exchanges. e.g. (Data + Ack), (RTS + CTS + Data + Ack)
  The STA is far enough from the OBSS recipient and if some conditions are met, spatial reuse is enhanced, e.g.,
    After measuring RSSI of two OBSS frame exchanges, if it is determined that STA B is far from STA C, STA C enhances spatial reuse.
STA C
(BSS 2)
STA B
(BSS 1)
STA A
(BSS 1)
STA D
(BSS 2)
Frame
Response Frame
RSSI AC
RSSI BC
Coverage of STA A
Coverage of STA C

## Slide 4: Spatial Reuse During OBSS UL MU Procedure
During OBSS UL MU procedure, earlier decision to improve spatial reuse may be possible.
  In 11ax, we defined UL MU procedure [1].
  Recipient of a data frame starts the frame exchange sequence by transmitting a Trigger frame.
    Receiver-initiated trigger frame transmission is different from the conventional frame exchange sequences such as (RTS + CTS + Data + Ack) and (Data + Ack).
  STAs of another BSS can decide whether to improve spatial reuse before the end of two frame exchanges (in the middle of the second frame (UL MU) transmission).

## Slide 5: Standalone Trigger Case (1)
11ax PHY format Trigger
AP 1
STA 1
Trigger
UL MU PPDU
Multi-STA BA
STA 2
RSSI < OBSS PD
3. Enhancing spatial reuse is possible.
1. STA 2 decodes Trigger frame (RSSI < OBSS PD) until HE-SIG-A
and recognizes this frame as DL SU frame from OBSS.
2. When HE-SIG-A ends,
it is confirmed that UL MU PPDU is
from the same BSS with the previous Trigger frame.
STA 2
(BSS 2)
STA 1
(BSS 1)
AP 1
(BSS 1)
AP 2
(BSS 2)
Trigger
STA 3
(BSS 1)
STA 4
(BSS 1)
STA 5
(BSS 1)
Trigger
Trigger
Trigger
Trigger
* It is assumed that MU PPDU can be distinguished btw. UL and DL at the end of HE-SIG-A.

## Slide 6: Standalone Trigger Case (2)
Legacy PHY format Trigger
AP 1
STA 1
Trigger
UL MU PPDU
Multi-STA BA
STA 2
RSSI < OBSS PD
3. Enhancing spatial reuse is possible.
1. STA 2 decodes Trigger frame (RSSI < OBSS PD)
and recognizes this frame as Trigger frame from OBSS.
STA 2
(BSS 2)
STA 1
(BSS 1)
AP 1
(BSS 1)
AP 2
(BSS 2)
Trigger
STA 3
(BSS 1)
STA 4
(BSS 1)
STA 5
(BSS 1)
Trigger
Trigger
Trigger
Trigger
2. When HE-SIG-A ends,
it is confirmed that UL MU PPDU is
from the same BSS with the previous Trigger frame.

## Slide 7: Trigger in Cascading Structure Case
Trigger in cascading structure
AP 1
STA 1
DL MU PPDU
(incl. Trigger)
STA 2
RSSI < OBSS PD
3. Enhancing spatial reuse is possible.
1. STA 2 decodes Trigger frame (RSSI < OBSS PD) until HE-SIG-A
and recognizes this frame as DL MU frame from OBSS.
2. When HE-SIG-A ends,
it is confirmed that UL MU PPDU is
from the same BSS with the previous DL MU frame.
STA 2
(BSS 2)
STA 1
(BSS 1)
AP 1
(BSS 1)
AP 2
(BSS 2)
Trigger
STA 3
(BSS 1)
STA 4
(BSS 1)
STA 5
(BSS 1)
Trigger
Trigger
Trigger
Trigger
* It is assumed that MU PPDU can be distinguished btw. UL and DL at the end of HE-SIG-A.
Trigger
Trigger
DL Data
Trigger
DL Data
Preamble
UL MU PPDU
…
…
TXOP

## Slide 8: Conclusions
Considering the potential interference to the recipient of OBSS frame, spatial reuse may be improved.
In case that RSSI of OBSS frame that triggered UL MU PPDU is below OBSS PD, STA may revise NAV from the middle of the UL MU PPDU regardless of RSSI of the UL MU PPDU.
  Not only for standalone Trigger frame but OFDMA Trigger frame in cascading

## Slide 9: References
[1] 11-15/0132r9 Specification Framework for TGax
[2] 11-15/1104r4 TXOP Consideration for Spatial Reuse

## Slide 10: Straw poll
  Do you agree to add the following text into sub-clause 5.1 in 11ax SFD ?
  5.1 Features for operation in dense environments
  The specification to consider a procedure that may revise the NAV depending on TBD conditions at the recipient of the ongoing OBSS frame.
  OBSS UL MU PPDU is detected and RSSI of the frame that triggered the UL MU PPDU was below OBSS PD level.
  Y
  N
  A