## Slide 1: Sounding for Uplink Transmission
Date: 2015-11-09
Authors:

## Slide 2: Background
The SFD defines a new channel sounding sequence to multiplex the Compressed Beamforming Action frame (CSI feedback)
However, it can be used to measure downlink channel, i.e., channel from an AP to STAs, and there is no sounding sequence for uplink channel
This contribution is talking about UL sounding sequence, i.e. to measure uplink channels from STAs to an AP

## Slide 3: Necessity of UL Sounding
Multiple Tx. antennas in STA are more popular than before, and thus the beamforming for UL transmission is necessary
  In the narrow band transmission such as UL OFDMA, the beamforming is more important to achieve frequency selective gains from the cost of diversity gain in wideband transmission
However, STAs have limited ways to estimate CSI of uplink channel
  For example, a STA doesn’t have enough capability of Tx/Rx calibration to perform implicit uplink CSI estimates from downlink
Therefore, a feasible way to measure uplink CSI is to perform a sounding procedure for uplink channel

## Slide 4: UL Sounding of the Existing Sequence
Without AP’s TXOP, each STA can use the existing 11ac sounding sequence
  Each STA will send NDP-A and NDP frames sequentially through contentions and receive a CB from the AP
  Using the received CB, the STA can beamform and send its UL data or wait for a Trigger frame for UL MU transmission
  After contentions, another STA can perform the same sounding for an UL transmission
NDP-A
NDP
Comp BF for STA1
NDP-A
NDP
Comp BF for STA2
SIFS
SIFS
SIFS
SIFS
Contentions
AP (beamformee)
STA1 (beamformer1)
STA2(beamformer2)
…
…

## Slide 5: UL Sounding with AP’s Control
With an AP’s TXOP, an UL sounding may be needed before a Trigger frame
  The AP can initiate an UL MU transmission by sending a Trigger frame, and each STA may need a CB for beamforming before receiving the Trigger frame
However, the current 11ac sounding sequence is initiated by a beamformer (STA in uplink), not by a beamformee (AP), and thus the AP (TXOP holder) can’t control the UL sounding sequence if the existing 11ac mechanism is reused
AP (beamformee)
STA1 (beamformer1)
STA2(beamformer2)
Trigger frame
UL MU
UL MU
UL Sounding may be needed before a Trigger frame
…
…
TXOP holder

## Slide 6: Requirements for UL Sounding Sequence
Within a TXOP of AP, AP should initiate a UL sounding sequence(s)
  Since a UL MU transmission is started from AP’s trigger frame, the AP should have the controllability of UL sounding as well
Remove unnecessary frame exchanges in a sequence(s)
  For example, there is only one beamformee (AP) and thus, most of information in NDP-A sent by multiple beamfomers (STAs) will be the same or unnecessary. Therefore, multiple NDP-A frames sent by STAs can be merged or omitted
  Reduce the air-time of the entire sequence
  Multiple NDP-A or NDP frames can be multiplexed as an MU transmission
    Before starting an UL sounding, AP may know preferred subband or spatial streams for each STA, and then NDP can be multiplexed in UL MU

## Slide 7: Example of UL Sounding
An AP initiates a sounding procedure by sending a specific sounding trigger frame
Each STA sends NDP frames to the AP in the UL MU manner as a response of the sounding trigger frame
  Most of information for NDP-A can be included in the UL sounding trigger frame, and in this case, NDP-A frames sent by STAs are not necessary
AP (beamformee)
STA1 (beamformer1)
STA2(beamformer2)
…
TXOP holder
UL sounding Trigger frame
NDP-A
NDP-A
NDP
NDP
NDPA + NDP
Or just NDP

## Slide 8: Conclusion
The beamforming is needed even in UL MU transmissions due to more popular multiple Tx. antennas in a STA
The UL sounding using the existing 11ac sounding sequence will cause large overhead because multiple beamformers are involved in a UL MU transmission
HE needs a new UL sounding sequence which is initiated by an AP
  Further discussion will be needed for details of the UL sounding sequence

## Slide 9: Straw Poll #1
Do you agree to add the following texts into SFD?
  AP may initiate uplink sounding sequence.