## Slide 1: Spatial Configuration And Signaling for MU-MIMO
Date: 2015-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Yakun Sun | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com

## Slide 3
Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Jinmin Kim |  |  |  | Jinmin1230.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 4
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 5
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Authors (continued)

## Slide 6
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Alice Chen |  |  |  | 
Lin Yang |  |  |  | 
Authors (continued)

## Slide 7
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn
Authors (continued)

## Slide 8: MU-MIMO Transmission in 11ac
Up to 4 users in a MU-MIMO is grouped with a GROUP_ID (GID).
  Maximum 62 groups per BSS.
Each MU-MIMO transmission supports up to 8 space-time streams, and no more than 4 streams for each user.
MU-MIMO spatial stream configuration is signaled in VHTSIGA.

## Slide 9: MU-MIMO Transmission in 11ax
11ax is targeted at supporting dense network with higher population.
  It is desirable to increase the number of users that can be multiplexed in a MU-MIMO transmission toward this target.
  Increase the number of spatially multiplexed users in a MU-MIMO RU to be 8.
Meanwhile, it is reasonable to maintain the number of space-time streams for each user in a MU-MIMO transmission to be no more than 4 as in 11ac.
  It is more suitable for a STA who can support a large number of space-time streams to use SU-MIMO.
  Also enable reusing 11ac MU-MIMO receiver design to reduce implementation cost for chip vendors.

## Slide 10: Current HESIGB Content Design
Recall the agreed HESIGB content design [1]:
  “The RU allocation signaling in the common field of HE-SIG-B signals an 8 bit, per 20 MHz PPDU BW for signaling
    The RU arrangement in frequency domain
    Number of MU-MIMO allocations: The RUs allocated for MU-MIMO and the number of users in the MU-MIMO allocations”
  “The user specific subfields of HE-SIG-B containing the per user dedicated information include the following fields:
    STA-ID
    For single-user allocations in an RU: NSTS (Number of Spatial Streams), TxBF (transmit beamforming ), MCS (Modulation and Coding Scheme) and Coding (Use of LDPC)
    For each user in a multi-user allocation in an RU: Spatial Configuration Fields, MCS and Coding.”

## Slide 11: MU-MMO Spatial Configuration Signaling
What needs to be signaled in spatial configuration field in a user’s specific subfield?
  The number of space-time streams for this user
  The indices of the space-time streams for this user
  The total number of space-time streams for this MU-MIMO RU.
Why to signal the total number of space-time streams (Nsts,total)?
  The number of HELTF symbols in a MU frame is determined by the maximum Nsts across all RUs  Nsts,total for a given RU cannot be inferred.
  A user needs to build the MIMO equalizer per Nsts,total to reliably suppress multi-user interference.
  It is also desirable for each intended user to decode its own user specific subfield for the sake of performance and complexity.

## Slide 12: Compression of Spatial Configuration Info.
A large number of all possible space-time stream allocations but with a lot of redundant information
  Compress spatial configuration info to reduce the bits needed.
Fact 1: Nuser is known before parsing the spatial configuration field
   a particular spatial configuration table can be constructed for each value of Nuser.
Fact 2: Also, since STA_ID is signaled in each user specific subfield , there is no reason to fix users’ order in signaling.
   Users are ordered such that the number of streams is non-increasing across users in a MU-MIMO transmission.
    Namely, Nsts[1] ≥ Nsts[2]≥… ≥Nsts[Nuser]
    This ordering has no performance impact at all.

## Slide 13: Example, Nuser=2
For an example, a two-user MU-MIMO transmission. Space-time streams are allocated such that:
  Nsts for each user is no more than 4.
  Nsts,total (= Nsts[1] + Nsts[2]) is no more than 8.
  Nsts[1] ≥ Nsts[2].
Given all those constraints, all possible space-time stream allocations are:
Nuser | Nsts[1] | Nsts[2] | # entries
2 | 1~4 | 1 | 10 (4bit)
 | 2~4 | 2 | 
 | 3~4 | 3 | 
 | 4 | 4 | 

## Slide 14: How to Use Spatial Config Field?
Nuser | B0…B3 | Nsts[1] | Nsts[2]
2 | 0000~0011 | 1~4 | 1
 | 0100~0110 | 2~4 | 2
 | 0111~1000 | 3~4 | 3
 | 1001 | 4 | 4
Nsts[1]=2, Nsts[2]=2
Nsts,total=4, the 3rd and 4th stream for the intended user (2 streams)
Spatial Config
“0100”
Common Block
“242-RU with 2 user”
……
2nd user specific subfield

## Slide 15: Complete Spatial Configuration Table
For all possible Nuser > 1, the spatial configuration table is
Nuser | B0…B3 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | #Entries
2 | 0000~0011 | 1~4 | 1 |  |  |  |  |  |  | 10
 | 0100~0110 | 2~4 | 2 |  |  |  |  |  |  | 
 | 0111~1000 | 3~4 | 3 |  |  |  |  |  |  | 
 | 1001 | 4 | 4 |  |  |  |  |  |  | 
3 | 0000~0011 | 1~4 | 1 | 1 |  |  |  |  |  | 13
 | 0100~0110 | 2~4 | 2 | 1 |  |  |  |  |  | 
 | 0111~1000 | 3~4 | 3 | 1 |  |  |  |  |  | 
 | 1001~1011 | 2~4 | 2 | 2 |  |  |  |  |  | 
 | 1100 | 3 | 3 | 2 |  |  |  |  |  | 
4 | 0000~0011 | 1~4 | 1 | 1 | 1 |  |  |  |  | 11
 | 0100~0110 | 2~4 | 2 | 1 | 1 |  |  |  |  | 
 | 0111 | 3 | 3 | 1 | 1 |  |  |  |  | 
 | 1000~1001 | 2~3 | 2 | 2 | 1 |  |  |  |  | 
 | 1010 | 2 | 2 | 2 | 2 |  |  |  |  | 
5 | 0000~0011 | 1~4 | 1 | 1 | 1 | 1 |  |  |  | 6
 | 0100~0101 | 2~3 | 2 | 1 | 1 | 1 |  |  |  | 
6 | 0000~0010 | 1~3 | 1 | 1 | 1 | 1 | 1 |  |  | 4
 | 0011 | 2 | 2 | 1 | 1 | 1 | 1 |  |  | 
7 | 0000~0001 | 1~2 | 1 | 1 | 1 | 1 | 1 | 1 |  | 2
8 | 0000 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Nuser from RU signaling
“Spatial config” signals one entry corresponding to Nuser
Max 4bit for any Nuser.
1
2

## Slide 16: Conclusions
The number of spatially multiplexed users in a MU-MIMO transmission is up to 8 (for a given RU).
The number of space-time streams for each user in a MU-MIMO transmission is up to 4 as in 11ac.
The spatial config field in each use specific subfield of 4 bits indicates the value of Nsts for each spatially multiplexed user in this MU-MIMO RU.
  The value of 4 bits are defined differently per Nuser, as shown in the spatial configuration table.
  A very efficient signaling for MU-MIMO stream allocations.

## Slide 17: SP #1
Do you support to add the following text in Section x.x.x in current SFD:
  The number of spatially multiplexed user in a DL or UL MU-MIMO transmission is up to 8 (in a given RU)?

## Slide 18: SP #2
Do you support to add the following text in Section x.x.x current SFD:
  The Nsts value for each user in a MU-MIMO RU is less than or equal to 4?

## Slide 19: SP #3
Do you support to add the following text in Section x.x.x in current SFD:
  A MU-MIMO user block includes a “spatial config” field of 4bit indicating the number of spatial streams for each multiplexed STA. The field is constructed by using the entries corresponding to the value of Nuser of this RU in the following table?
Nuser | B0…B3 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | #Entries
2 | 0000~0011 | 1~4 | 1 |  |  |  |  |  |  | 10
 | 0100~0110 | 2~4 | 2 |  |  |  |  |  |  | 
 | 0111~1000 | 3~4 | 3 |  |  |  |  |  |  | 
 | 1001 | 4 | 4 |  |  |  |  |  |  | 
3 | 0000~0011 | 1~4 | 1 | 1 |  |  |  |  |  | 13
 | 0100~0110 | 2~4 | 2 | 1 |  |  |  |  |  | 
 | 0111~1000 | 3~4 | 3 | 1 |  |  |  |  |  | 
 | 1001~1011 | 2~4 | 2 | 2 |  |  |  |  |  | 
 | 1100 | 3 | 3 | 2 |  |  |  |  |  | 
4 | 0000~0011 | 1~4 | 1 | 1 | 1 |  |  |  |  | 11
 | 0100~0110 | 2~4 | 2 | 1 | 1 |  |  |  |  | 
 | 0111 | 3 | 3 | 1 | 1 |  |  |  |  | 
 | 1000~1001 | 2~3 | 2 | 2 | 1 |  |  |  |  | 
 | 1010 | 2 | 2 | 2 | 2 |  |  |  |  | 
5 | 0000~0011 | 1~4 | 1 | 1 | 1 | 1 |  |  |  | 6
 | 0100~0101 | 2~3 | 2 | 1 | 1 | 1 |  |  |  | 
6 | 0000~0010 | 1~3 | 1 | 1 | 1 | 1 | 1 |  |  | 4
 | 0011 | 2 | 2 | 1 | 1 | 1 | 1 |  |  | 
7 | 0000~0001 | 1~2 | 1 | 1 | 1 | 1 | 1 | 1 |  | 2
8 | 0000 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 20: Reference
[1] 11-15-0132-09-00ax-spec-framework