## Slide 1
Energy consumption with Scheduled PSP
Date: 2015-11-09
Authors:
Name | Affiliations | Address | Phone | Email
Dmitry Akhmetov | Intel | 2111 NE 25th AVE, Hillsboro, OR, 97123 | +1-503-264-8081 | dmitry.akhmetov@intel.com
Ghosh Chittabrata | Intel | 2200 Mission College Blvd., Santa Clara, CA, 95054 | +1-415-244-8904 | chittabrata.ghosh@intel.com

## Slide 2: Abstract
This presentation provides simulation results on energy consumption for Scheduled PSP in comparison with regular PSP
  Quantify the reduced energy consumption in Listen/Receive states and increased time in Shallow sleep state

## Slide 3: PSP
STA wakes every DTIM to check if it has any data in DL
If TIM bit is set STA transmits PS-Poll frame to indicate it’s presence to an AP
  STA remains in active state until it receive DATA from an AP
AP access the medium and transmit data in DL followed by an ACK frame from a STA
STA enters Sleep state

## Slide 4: PSP using Target transmission time
In September meeting in 15/1107r0 a concept of target transmission time for TF-R was introduced
SFD 15/0132r09 states:
  “The spec shall include a mechanism that allows the Beacon frame to indicate the target transmission time(s) of one or more Trigger frame(s) that allocate resources for random access.”
Target Transmission Times(s) (TTT) can be used by power save STAs for increased energy efficiency
  Power saving through decreased Listen and Receive times
  Improved BSS performance by grouping/combining PS STAs for faster service

## Slide 5: Observations & Improvements for Reduced Energy Consumption
In legacy PSP
  STA shall remain in Listen state after receiving ACK to PS-Poll frame
  Time between PS-Poll frame and DL data is undefined, there is no guarantee DL data to come immediately after PS-Poll/ACK Ack exchange
  STA is forced to listen/receive frames while waiting for DL data and thus spends energy in such operation
    Large number of STAs or saturated network traffic will create extreme power consumption overhead for PSP-enabled STAs
Improvement for PSP or Scheduled PSP (S-PSP):
  Announced target time for DL frame reception
  Reduced Listen time following reception of an ACK to an STA’s PS-Poll frame
    STAs enter Shallow Sleep state after receiving ACK and wake up at defined intervals for DL frame reception

## Slide 6: Illustration of S-PSP
STA wakes every DTIM to check if it has any data in DL
If TIM bit is set STA transmits PS-Poll frame to indicate it’s presence to an AP
  STA enter into Sleep state and remains there until Target Transmission time
AP gather PS Poll responses from other STAs and serve them in optimal manner at TTT event

## Slide 7: Initial simulation results
3 simulation scenarios
  1 AP, 1 power saving STA
    DL link, 1 frame of 1.5k every 100ms
  1 AP, 1 power saving STAs, 3 active STAs
    DL link to power saving STA, 1 frame of 1.5k every 100ms
    3 DL/UL links (VoIP) to 3 VoIP clients
  1 AP, 8 power saving STA
    DL links, 1 frame of 100bytes every BI
MCS0 for all transmissions
BI is 102.4ms
PSP and improved T-PSP
Metrics of interest
  Total TX , RX, LISTEN and SLEEP time at power saving device

## Slide 8: Initial simulation results, 1 AP, 1 STA
STA1 spends 1.8x less time in Listen state
Corresponding increase of time in Sleep state
1 power saving device |  |  |  | difference
 |  | PSP | S-PSP | 
STA1 | TX time,s : | 0.097 | 0.097 | 
 | RX time,s : | 1.971 | 1.971 | 
 | Listen time, s : | 0.229 | 0.130 | 56% reduced listen time to PSP
 | Sleep time, s: | 97.646 | 97.795 | 

## Slide 9: Initial simulation results, Mix case, 1 Ap, 1 PS STA, 3 ActiveSTAs
In this scenario STA1 spend almost 1.5x less time in Listen mode
Mix of 1 PS device and 3 active devices |  |  |  | difference
 |  | PSP | S-PSP | 
STA1 | TX time,s : | 0.098 | 0.098 | 
 | RX time,s : | 2.005 | 2.005 | 
 | Listen time, s : | 0.260 | 0.159 | 63% reduced listen time to PSP
 | Sleep time, s: | 97.545 | 97.680 | 

## Slide 10: Initial simulation results, 1 AP, 8 STAs
Chart: RX time, s
PSP | 1.5843 | 1.5782 | 1.6211 | 1.3155 | 1.757 | 1.5616 | 1.5539 | 1.6461
T-PSP | 1.3226 | 1.3366 | 1.3472 | 1.3076 | 1.3708 | 1.3786 | 1.3978 | 1.3852
Chart: TX time, s
PSP | 0.11132 | 0.11403 | 0.11607 | 0.10794 | 0.1266 | 0.12074 | 0.12232 | 0.12551
T-PSP | 0.10656 | 0.10904 | 0.11096 | 0.10349 | 0.11564 | 0.11797 | 0.12294 | 0.12032
Chart: Listen time, s
PSP | 0.92937 | 0.92754 | 0.95317 | 0.77921 | 1.0404 | 0.92687 | 0.92267 | 0.98036
T-PSP | 0.45461 | 0.46821 | 0.48086 | 0.43662 | 0.50995 | 0.51947 | 0.54708 | 0.53057
Chart: Sleep time, s
PSP | 97.4031 | 97.4162 | 97.2055 | 97.8327 | 97.1044 | 97.4758 | 97.3341 | 97.2143
T-PSP | 98.1562 | 98.1265 | 98.1008 | 98.1891 | 98.0457 | 98.0267 | 97.9776 | 98.0053
On average STAs spend 50% less time in Listen mode and 15% time less in Receive mode

## Slide 11: Conclusion
Provided simulations shows performance benefit of Scheduled PSP by reducing 50-60% time in Listen mode and around 15% in Receive mode
Designated/centralized wake up time allow to save more energy by
  Removing/reducing unnecessary contention for DL data at AP side
  Reducing DL wait time at STA end, especially in loaded network
  Ignoring undesired packets directed to other radios
  Allow to group power saving STAs together using advanced TX techniques such OFDMA