## Slide 1
UL OFDMA Random Access Control
Date: 2015-11-08
Authors:

## Slide 2: Introduction
TG approved OBO mechanisms and an OBO element in Trigger Frame during the last meeting[1]
  An HE AP is allowed to broadcast a TBD parameter in the trigger frame to the STAs so that STAs can initiate the random access process after the trigger frames
OBO mechanism was considered under the identical priority case [2]
802.11e EDCA needs to be discussed in OBO situation

## Slide 3: Contention Control
OBO efficiency depends on traffic load
OFDMA random access control needs to be considered in TF-R
Variable CWO or Variable Transmission probability could be a possible solution [3]
SFD states only one TBD parameter is included in trigger frame for contention control [1]
[3] has shown PTx and CWO could be a one of the example of ‘a TBD parameter’ in trigger frame
  AP broadcasts the randomization parameter(s) to the STAs, which can be
    Contention window size  CWO
    Transmission probability  PTX
    Etc.

## Slide 4: OFDMA Contention Window (CWO)
CWO is a window size of OBO
Large CWO may cause long UL random access delay but small CWO could cause severe collision which causes much longer delay
CWO value needs to be optimized depending on contention (congestion) level
[2] already showed how different CWO min values control various contention levels

## Slide 5: Transmission Probability (PTx)
After OBO procedure, OFDMA p-persistence could be applied on UL OFDMA random access STAs
If OFDMA p-persistence is adopted, OBO=0 STAs could transmit its data Frame with probability of PTx
[3] has shown PTx and CWO could be a one of the example of ‘a TBD parameter’ in trigger frame
  AP broadcasts the randomization parameter(s) to the STAs, which can be
    Contention window size
    Transmission probability
    Etc.
PTx provides immediate contention control for the TF-R TXOP

## Slide 6: OBO parameter control
CWOmin, CWOmax
  Controlling CWOmin value provides channel access delay control effect on data frame which is generated after trigger frame transmission
p-persistent
  Controlling p-persistent value provides contention control effect on immediate TXOP
CWO
CWO
6
RUs
BO
BO
CWO
6
RUs
p
-
percent access
BO

## Slide 7: OBO Parameters for Access Categories
802.11e provides EDCA parameters for each Access Categories(ACs)
Current OBO mechanism only considers the identical priority case
When STAs with different ACs contend using OBO, OBO mechanism needs to provide parameters for ACs
CWOmin, CWOmax and TX Probability could be possible parameters for OFDMA EDCA
CWO control and Tx probability control have their own pros. and cons.

## Slide 8: OBO Parameters for Access Categories
The table needs to be defined to support ACs on UL OFDMA
Minimum size of RU, OFDMA TXOP, etc… could be possible parameters for the Access Categories
AC | CWOmin | CWOmax | PTx (TBD)
Background (AC_BK) | TBD | TBD | TBD
Best Effort (AC_BE) | TBD | TBD | TBD
Video (AC_VI) | TBD | TBD | TBD
Voice (AC_VO) | TBD | TBD | TBD
Legacy DCF | TBD | TBD | TBD

## Slide 9: OBO Parameters for Access Categories
Current SFD does not allow broadcasting multiple parameters in the trigger frame
If ACs are considered for OBO procedure, multiple OBO parameters need to be broadcast
Indexing mechanism (e.g., contention index) can be used to efficiently indicate contention level
  Depending on the contention level, different CWO or PTX values can be applied

## Slide 10: Example of contention index
AC | Parameter | index = 1 | index= 2 | index= 3 | …
BK | CWO | 4 | 8 | 16 | 
 | PTx | <1 | <1 | <1 | 
BE | CWO | 4 | 8 | 16 | 
 | PTx | <1 | <1 | <1 | 
VI | CWO | 2 | 4 | 8 | 
 | PTx | <1 | <1 | <1 | 
VO | CWO | 1 | 2 | 4 | 
 | PTx | <1 | <1 | <1 | 
*For each contention index, PTx (VO)≥ PTx (VI)≥ PTx (BE)≥ PTx (BK)
*Exact CWO values and PTx values are FFS

## Slide 11: Contention index
Contention index could be interpreted as a intensity of contention
AP is assumed to have a capability to measure the intensity of contention roughly
If AP recognizes contention level of UL random access is high, it advertise high contention index value to BSS via trigger frame
Utilizing contention index could solve the problems of different parameters among different ACs
  Advertising single contention value cannot assure 802.11e priority on UL OFDMA

## Slide 12: Conclusion
Access Categories need to be considered in the OBO mechanism
  Parameters for OBO ACs
  CWOmin, CWOmax, PTx …
Trigger frame could advertise the index of contention level instead of specific contention parameter
  Advertising specific contention parameters (CWO or PTx ) is not feasible for multiple ACs

## Slide 13: StrawPoll 1
Do you agree to add to the TG Specification Frame work document?
  4.5. A STA transmitting data using UL OFDMA random access shall follow OBO QoS parameters (TBD) for its access category.
    Y
    N
    A

## Slide 14: StrawPoll 2
Do you agree to add to the TG Specification Frame work document?
  4.5. The spec shall define a contention index field in the random access trigger frame to indicate contention level. Depending on the contention index value, TBD parameters (e.g., CWOmin, PTx , etc) are used for random access procedure.
    Y
    N
    A

## Slide 15: References
[1] 15/0132r9 “Spec Framework”
[2] 15/1105r0 “UL OFDMA-based Random Access Procedure”
[3] 15/1137r1 “Triggered OFDMA Random Access Observations”