## Slide 1: Consideration for protecting cascading MU DL/UL transmission with MU RTS/CTS
Date:2015-11-09
Authors:

## Slide 2: Introduction
MU UL procedure can set up TXOP to protect MU UL transmission either by trigger frame or by RTS/CTS exchange.
MU RTS/CTS procedure is defined for protecting DL MU transmission in SFD [1].
This presentation proposes to use MU RTS/CTS to protect cascading DL/UL transmission.

## Slide 3: Protecting cascading MU DL/UL transmission with MU RTS/CTS
Using one MU RTS/CTS exchange to protect cascading MU DL/UL transmission
  MU RTS/CTS exchange
    AP initiates MU RTS/CTS exchange for protecting the following MU transmission, while, the 3rd-party STAs which receive RTS/CTS set their NAV to the duration of the cascading MU DL/UL transmission.
  MU DL transmission
    STAs with pending UL DATA, after receiving MU DL transmission, could set a bit in its UL MU response frame, e.g. BA, to inform AP that it has pending UL DATA
  If STAs have pending UL DATA, MU UL transmission will be scheduled and initiated with the trigger frame transmission.
  If no STA has pending UL DATA, a NAV cancellation mechanism could be used, e.g. AP could send CF-End for NAV cancellation

## Slide 4: Protecting cascading MU DL/UL transmission with MU RTS/CTS
E.g.
Using one MU RTS/CTS exchange to protect cascading MU DL/UL transmission
MU DL transmission
MU UL transmission

## Slide 5: Conclusions
Protecting cascading MU DL/UL transmission with MU RTS/CTS is discussed
  Protecting both MU DL and UL transmission with one MU RTS/CTS exchange.
  STAs with pending UL DATA, after receiving the MU DL transmission, could set a bit in their response frame, e.g. More Data bit of BA frame, to indicate AP that they have pending UL DATA.

## Slide 6: Straw poll
Do you agree to add to the TG Specification Frame work document?
  The spec shall include a mechanism that allows MU RTS/CTS to protect both MU Downlink and MU Uplink transmission(s) within the same TXOPs.
Yes:
No:
Abstain

## Slide 7: References
[1] “SPEC framework”, IEEE 802.11-15/0132r9
.