## Slide 1: TGax PHY Ad Hoc Nov 2015 Meeting Agenda
Date: 2015-11-10
Authors:

## Slide 2: IEEE 802.11 TGax High Efficiency WLAN PHY Ad Hoc
Co-Chairs:
Yakun Sun (Marvell)
Jianhan Liu (Mediatek)
Bo Sun (ZTE)

## Slide 3: Agenda Items
Call meeting to order
Patent policy, etc. (Call for Potentially Essential Patents)
Set and approve agenda
Review ad hoc rules
Technical Presentations approved by 802.11ax for presentation this week, and related straw polls
Any other technical presentations

## Slide 4: Meeting Protocol, Attendance, Voting & Document Status
Slide 4
Please announce your affiliation when you first address the group during a meeting slot
Cell Phones to be silent or Off
Register your attendance via https://imat.ieee.org while on meeting SSID (e.g. Verilan-secure)
Make sure your badges are correct
If you plan to make a submission be sure it does not contain company logos or advertising
Questions on Voting status, Ballot pool, Access to Reflector, Documentation, Member’s Area
  Contact Jon Rosdahl – jrosdahl@ieee.org

## Slide 5: Patent Policy and Other Guidelines
Following 5 slides

## Slide 6: Instructions for the WG Chair
The IEEE-SA strongly recommends that at each WG meeting the chair or a designee:
  Show slides #1 through #4 of this presentation
  Advise the WG attendees that:
    The IEEE’s patent policy is consistent with the ANSI patent policy and is described in Clause 6 of the IEEE-SA Standards Board Bylaws;
    Early identification of patent claims which may be essential for the use of standards under development is strongly encouraged;
    There may be Essential Patent Claims of which the IEEE is not aware. Additionally, neither the IEEE, the WG, nor the WG chair can ensure the accuracy or completeness of any assurance or whether any such assurance is, in fact, of a Patent Claim that is essential for the use of the standard under development.
  Instruct the WG Secretary to record in the minutes of the relevant WG meeting:
    That the foregoing information was provided and that slides 1 through 4 (and this slide 0, if applicable) were shown;
    That the chair or designee provided an opportunity for participants to identify patent claim(s)/patent application claim(s) and/or the holder of patent claim(s)/patent application claim(s) of which the participant is personally aware and that may be essential for the use of that standard
    Any responses that were given, specifically the patent claim(s)/patent application claim(s) and/or the holder of the patent claim(s)/patent application claim(s) that were identified (if any) and by whom.
  The WG Chair shall ensure that a request is made to any identified holders of potential essential patent claim(s) to complete and submit a Letter of Assurance.
  It is recommended that the WG chair review the guidance in IEEE-SA Standards Board Operations Manual 6.3.5 and in FAQs 12 and 12a on inclusion of potential Essential Patent Claims by incorporation or by reference.
  Note: WG includes Working Groups, Task Groups, and other standards-developing committees with a PAR approved by the IEEE-SA Standards Board.

## Slide 7: Participants, Patents, and Duty to Inform
All participants in this meeting have certain obligations under the IEEE-SA Patent Policy. Participants:
  “Shall inform the IEEE (or cause the IEEE to be informed)” of the identity of each “holder of any potential Essential Patent Claims of which they are personally aware” if the claims are owned or controlled by the participant or the entity the participant is from, employed by, or otherwise represents
    “Personal awareness” means that the participant “is personally aware that the holder may have a potential Essential Patent Claim,” even if the participant is not personally aware of the specific patents or patent claims
  “Should inform the IEEE (or cause the IEEE to be informed)” of the identity of “any other holders of such potential Essential Patent Claims” (that is, third parties that are not affiliated with the participant, with the participant’s employer, or with anyone else that the participant is from or otherwise represents)
  The above does not apply if the patent claim is already the subject of an Accepted Letter of Assurance that applies to the proposed standard(s) under consideration by this group
Quoted text excerpted from IEEE-SA Standards Board Bylaws subclause 6.2
Early identification of holders of potential Essential Patent Claims is strongly encouraged
No duty to perform a patent search
Slide #1

## Slide 8: Patent Related Links
  All participants should be familiar with their obligations under the IEEE-SA Policies & Procedures for standards development.
  Patent Policy is stated in these sources:
  IEEE-SA Standards Boards Bylaws
  http://standards.ieee.org/guides/bylaws/sect6-7.html#6
  IEEE-SA Standards Board Operations Manual
  http://standards.ieee.org/guides/opman/sect6.html#6.3
  Material about the patent policy is available at
  http://standards.ieee.org/board/pat/pat-material.html
Slide #2
If you have questions, contact the IEEE-SA Standards Board Patent Committee Administrator at patcom@ieee.org or visit http://standards.ieee.org/board/pat/index.html
This slide set is available at http://standards.ieee.org/board/pat/pat-slideset.ppt

## Slide 9: Call for Potentially Essential Patents
If anyone in this meeting is personally aware of the holder of any patent claims that are potentially essential to implementation of the proposed standard(s) under consideration by this group and that are not already the subject of an Accepted Letter of Assurance:
  Either speak up now or
  Provide the chair of this group with the identity of the holder(s) of any and all such claims as soon as possible or
  Cause an LOA to be submitted
Slide #3

## Slide 10: Other Guidelines for IEEE WG Meetings
All IEEE-SA standards meetings shall be conducted in compliance with all applicable laws, including antitrust and competition laws.
  Don’t discuss the interpretation, validity, or essentiality of patents/patent claims.
  Don’t discuss specific license rates, terms, or conditions.
    Relative costs, including licensing costs of essential patent claims, of different technical approaches may be discussed in standards development meetings.
      Technical considerations remain primary focus
  Don’t discuss or engage in the fixing of product prices, allocation of customers, or division of sales markets.
  Don’t discuss the status or substance of ongoing or threatened litigation.
  Don’t be silent if inappropriate topics are discussed … do formally object.
---------------------------------------------------------------
See IEEE-SA Standards Board Operations Manual, clause 5.3.10 and “Promoting Competition and Innovation: What You Need to Know about the IEEE Standards Association's Antitrust and Competition Policy” for more details.
Slide #4

## Slide 11: Ad Hoc Groups Operation
Straw Polls are only allowed during Ad Hoc group meeting // no motions, anyone can vote
A straw poll affecting the Spec Framework has to start with,
  Do you agree to add to the TG Specification Frame work document?
A straw poll needs to achieves at least 75% to be converted to a motion at the TG level.
Each Presentation will be limited to 20 minutes.

## Slide 12: Meeting Schedule
 | Monday | Tuesday |  | Wednesday |  | Thursday
AM1 | TGax |  |  | TGax |  | TGax
AM2 |  | PHY | MAC |  |  | 
PM1 | TGax | MU | SR | PHY | SR | TGax
PM2 |  |  |  | PHY | MU | 
EVE |  | PHY | MAC |  |  | 

## Slide 13: Submissions
Preamble (SIGA)
11-15/1309 Extended Range Support for 11ax
11-15/1353 Preamble Formats
11-15/1357 Extra tones in the preamble
11-15/1372 L-LENGTH Equation Updates
Data
11-15/1289 Non-Uniform Constellations for 1024-QAM
11-15/1305 STBC and Padding Discussions
11-15/1310 11ax LDPC Tone Mapper for 160MHz
11-15/1311 11ax Spectral Mask
11-15/1327 Diversity Mode in OFDMA
11-15/1329 Link Adaptation for HE WLAN
11-15/1331 PHY Padding Capability Signaling
STF/LTF
11-15/1323 HE-STF Sequence
11-15/1303 LTF Sequence Designs
11-15/1334 HE-LTF Sequence Design
11-15/1322 Channel Estimation Enhancement and Transmission Efficiency Improvement Using Beam-Change Indication and 1x HE-LTF
SIGB
11-15/1304 Supported Resource Allocations in SIG-B
11-15/1315 HE-SIG-B Mapping and Compression
11-15/1324 MCS for HE-SIG-B
11-15/1335 HE-SIG-B Contents
11-15/1059 SIG-B Encoding Structure Part II
11-15/1350 Spatial Configuration And Signaling for MU-MIMO
11-15/1354 SIGA fields and Bitwidths
Sounding and feedback
11-15/1320 Maximum Tone Grouping Size for 802.11ax Feedback
11-15/1321 Reducing Explicit MIMO Compressed Beamforming Feedback Overhead for 802.11a
11-15/1332 Implicit Sounding for HE WLAN
11-15/1347 Strategies to reduce MIMO feedback overhead
11-15/1349 Sounding for Uplink Transmission

## Slide 14: Tuesday AM2
11-15/1309 Extended Range Support for 11ax
11-15/1353 Preamble Formats
11-15/1357 Extra tones in the preamble
11-15/1372 L-LENGTH Equation Updates
11-15/1289 Non-Uniform Constellations for 1024-QAM
11-15/1310 11ax LDPC Tone Mapper for 160MHz

## Slide 15: 1309r1 SP#1
Do you support adding the following to the spec framework
“L-STF power is boosted by 3 dB in the extended range preamble”
Y: 50
N: 4
A: 18
SP passes

## Slide 16: 1309r1 SP#2
Do you support adding the following to the spec framework
“L-LTF power is boosted by 3 dB in the extended range preamble”
Y: 51
N: 0
A: 22
SP passes

## Slide 17: 1353r0 SP #1
Do you support that there are only three pre-HE-STF preamble formats defined as:
  SU format (mandatory) / Trigger based UL
  MU format (mandatory)
  Extended range SU format
Yes: 51
No: 2
Abs: 21
SP passes

## Slide 18: 1353r0 SP #2
Do you support the signaling of the three preamble formats as shown on slide 15?
Yes: 55
No: 0
Abs: 21
SP passes

## Slide 19: 1353r0 SP #3
Do you support that the following are the only mandatory combinations of LTF size and CP size
2x LTF+ 0.8uS
2x LTF+ 1.6uS
4x LTF+ 3.2uS
with HE-LTF and payload using the same CP size.
and that LTF size and CP size are jointly signaled using 3 bits.
Yes: 57
No: 0
Abs: 15
SP passes

## Slide 20: 1353r0 SP #4
Do you support that SIGB only has one CP size equal to 0.8uS
Yes: 61
No: 0
Abs: 14
SP passes

## Slide 21: 1357r1 Straw poll
Do you support to:
  Allocate 4 extra subcarriers, two at each edge of each 20MHz sub-channel, for L-SIG, RL-SIG, HE-SIG-A and HE-SIG-B fields in 11ax PPDUs.
    The 4 subcarriers added to the L-SIG and RL-SIG fields are transmitted with known TBD BPSK constellations (+-1).
    The number of data subcarriers in HE-SIG-A and HE-SIG-B fields are increased by 4 in each 20MHz sub-channel.
    L-SIG, RL-SIG, HE-SIG-A and HE-SIG-B fields are always transmitted with the same total power as L-LTF field (in cases when L-LTF is not being boosted).
  Y: 46
  N: 0
  A: 13
  SP Passes

## Slide 22: 1372r0 Straw Poll
Do you agree to make the following changes in red, on the equations in Section 3.3.5 of TGax SFD?
Y: 71
N: 0
A: 2
SP passes

## Slide 23: 1289r1 Straw Poll #1
Do you agree that is desirable to achieve the maximum possible gain for 1024-QAM (e.g. make also use of non-uniform constellations)?
Y/N/A
Y: 10
N: 5
Abs: many

## Slide 24: 1289r1 Straw Poll #2
Do you agree that non-uniform constellations shall be used for 1024-QAM?
Y/N/A
Y: 10
N: 9
Abs: Many

## Slide 25: 1310r0 Straw-poll
Do you support to add the following text to 11ax SFD?
  2x996RU employs a segment parser (as in 11ac) between two 996 tones (frequency segments) and the LDPC tone mapper in each 996 tone segment uses DTM=20
Y: 57
N: 0
A: 3

## Slide 26: Tuesday Evening
11-15/1305 STBC and Padding Discussions
11-15/1311 11ax Spectral Mask
11-15/1327 Diversity Mode in OFDMA
11-15/1329 Link Adaptation for HE WLAN
11-15/1331 PHY Padding Capability Signaling

## Slide 27: 1305r0 SP
Do you agree to add the following text in 11ax SFD?
  STBC is an optional feature in 11ax and it is ONLY defined for single spatial stream (Nss=1 and Nsts=2)
  In a MU PPDU all RUs are either STBC or not STBC.
Y: 46
N: 0
A: 12

## Slide 28: 1311r0 Straw-poll
Do you support to add the following to 11ax SFD?
The spectral masks for 11ax non-OFDMA 20/40/80/160/80+80 MHz PPDU are defined as in slides 13-15?
  The bandwidth of the applied spectrum mask for a (non-OFDMA) PPDU shall be determined by the bandwidth occupied by the pre HE-STF portion of the preamble in this PPDU, regardless of the BSS bandwidth
  The spectral mask requirements do not apply to LO leakage
  Y: 49
  N: 0
  A: 8

## Slide 29: 1327r0 Straw Poll 1
Do you agree to add the following to the SFD?
Transmission diversity mode (i.e. non-continuous transmission) shall be supported in 11ax.
  Transmission diversity mode divides a single encoded packet in half and maps to 13 + 13 (26 RU) or 26 + 26 (52 RU) tones, that are spaced apart in frequency.
  TBD whether only 26 RU, only 52 RU, or both 26 and 52 RU support transmit diversity mode.
Y: 12
N: 23
A: 21

## Slide 30: 1329r1 Straw Poll #1
Do you agree to include the following text to TGax SFD:
HE link adaptation shall define reference payload size for the reported MCS in MFB.
  Reference payload size may be dependent on the frames involved in link adaptation or fixed in specification. Details TBD.
Y: 12
N: 1
A: many

## Slide 31: 1329r1 Straw Poll #2
Do you agree to include the following text to TGax SFD:
HE link adaptation field, which is part of HE variant of HT control field, consists of MFB and TBD subfields. The MFB subfield includes NSS and MCS subfield.
Y: 17
N: 0
A: 37

## Slide 32: 1331r0 Strawpoll #1
To you agree to added the following text in SFD:
HE padding and packet extension capability field shall be defined separately for STBC and non-STBC transmissions.
HE padding and packet extension capability field content for STBC transmission is limited to Nss = 1.
Y: 12
N: 28
A: 16

## Slide 33: 1331r0 Strawpoll #2
Do you agree to the following concept:
Maximum TPE of 0us, 8us, or 16us is determined by number of codewords in the last two OFDM symbols (denoted as NCW,left) containing information payload.
Maximum TPE capability can be signaled using two threshold values threshold8 and threshold16, which determine the NCW,left threshold for using max TPE of 8us or 16us, respectively. The threshold value will be common for all BW and NSS.
Y:12
N:26
A:13

## Slide 34: Wednesday PM1
11-15/1323 HE-STF Sequence
11-15/1303 LTF Sequence Designs
11-15/1334 HE-LTF Sequence Design
11-15/1322 Channel Estimation Enhancement and Transmission Efficiency Improvement Using Beam-Change Indication and 1x HE-LTF
11-15/1315 HE-SIG-B Mapping and Compression
11-15/1324 MCS for HE-SIG-B

## Slide 35: 1323r1 Straw poll
Do you agree to add the following HE-STF sequences for 0.8us and 1.6us periodicity to the 11ax SFD:
  M = {-1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1}
  1x HE-STF sequences
    20MHz
      HES-112,112(-112:16:112) = M *(1+j)*sqrt(1/2)
      HES-112,112(0) = 0
    40MHz
      HES-240,240(-240:16:240) = {M, 0, -M} *(1+j)*sqrt(1/2)
    80MHz
      HES-496,496(-496:16:496) = {M, 1, -M, 0, -M, 1, -M} *(1+j)*sqrt(1/2)
  2x HE-STF sequences
    20MHz
      HES-120,120(-120:8:120) = {M, 0 , -M} *(1+j)*sqrt(1/2)
    40MHz
      HES-248,248(-248:8:248) = {M, -1, -M, 0, M, -1, M} *(1+j)*sqrt(1/2)
      HES-248,248(±248) = 0
    80MHz
      HES-504,504 (-504:8:504) = {M, -1, M, -1, -M, -1, M, 0, -M, 1, M, 1, -M, 1, -M} *(1+j)*sqrt(1/2)
      HES-504,504(±504) = 0
Y: 48, N: 0, A: 12

## Slide 36: 1303r0 Straw Poll #1
Do you agree to add the following texts into the SFD?
  A HE LTF for 242SU shall reuse VHT-122,122 with the same phase rotation [1, -1, -1, -1].
    HELTF242SU = VHTLTF-122,122 with the phase rotation of VHT80
Withdrawn

## Slide 37: 1303r0 Straw Poll #2
Do you agree to add the following texts into the SFD?
    HE LTFs for 26RU, 52RU, and 106RU shall use the following sequences:
      HELTF26RU ={1,-1,1,1,-1,-1,-1,-1,1,1,1,-1,1,1,1,-1,1,1,1,-1,1,1,-1,-1,-1,-1}
      HELTF52RU = {HELTF26RU(1:13), -HELTF26RU(14:26), -HELTF26RU}
      HELTF106RU = {HELTF26RU, 1, -HELTF26RU, -HELTF26RU, 1, -HELTF26RU}
Withdrawn

## Slide 38: 1303r0 Straw Poll #3
Do you agree to add the following texts into the SFD?
  A HE LTF for 242RU shall use VHT-122,122 removing zeros with the phase rotation [1, -1, -1, -1].
      HELTF242RU = {VHTLTF-122,122left(1:60), -VHTLTF-122,122left(61:121), -VHTLTF-122,122right(1:121)},
          where VHTLTF-122,122left and VHTLTF-122,122right are 121-length sequences in the left and right sides of 3 DCs in VHTLTF-122,122, respectively
Withdrawn

## Slide 39: 1303r0 Straw Poll #4
Do you agree to add the following texts into the SFD?
  HE LTF sequences for 484RU, 484SU, and 996SU shall be made from concatenations of the HELTF sequence for 242RU in frequency domain, as shown in the followings:
      HELTF484RU = {HELTF242RU, HELTF242RU}
      HELTF484SU = {HELTF242RU, 0, 0, 0, 0, 0, HELTF242RU}
      HELTF996SU = {1, HELTF242RU, -HELTF242RU, -HELTF26RU(1:13), 0,0,0,0,0, -HELTF26RU(14:26), -HELTF242RU, -HELTF242RU, 1}
Withdrawn

## Slide 40: 1334r1 SP#1
Do you support to add to SFD
  4x/2x HE-LTF sequences for 80MHz in slide 13-15
  4x/2x HE-LTF sequences for 40MHz in slide 20-21
  4x/2x HE-LTF sequences for 20MHz in slide 26
  Y: 63
  N: 2
  A: 16
Le Liu, Huawei, et. al.

## Slide 41: 1334r1 SP#2
Do you support to add to SFD
  In all transmission modes, HE-STF and HE-LTF only populate RUs that are populated in the data field.
  Y: 74
  N: 6
  A: 15
Le Liu, Huawei, et. al.

## Slide 42: 1334r1 SP#3
Do you support to add to SFD
  Gamma (tone rotation as defined in 22.3.7.5) is not applied on HE-STF and beyond.
    TBD in case of a duplicated HE PPDU (if ever defined)
  Y: 60
  N: 0
  A: 13
Le Liu, Huawei, et. al.

## Slide 43: 1322r0 Straw Poll #1
Do you agree to add 1-bit beam-change indication into HE-SIGA?
    Value “1” indicates that spatial mapping is changed
    Value “0” indicates that spatial mapping is unchanged
Y: 63
N: 0
A: 14

## Slide 44: Straw poll #2
Do you agree that when beam-change indication is “0”, the pre-HE-STF portion preamble shall be spatially mapped in the same way as HE-LTF1 on each tone?
Y: 62
N: 0
A: 8

## Slide 45: Straw Poll #3
Do you agree to add 1x HE-LTF as an optional mode in 11ax for SU PPDU (TBD for MU-MIMO)?
  1xLTF + 0.8us GI is one optional combination as indicated by the “GI and LTF size” sub-field in HE-SIG-A.
Y: 60
N: 1
A: 14

## Slide 46: 1315r1 Straw Poll #1
Do you agree to add the following text to the 11ax SFD:
The resource allocation signaling in the common control field and user specific subfields for an STA carried in the HE-SIG-B are transmitted in the same 20MHz sub-channel as the data for 20MHz and 40MHz PPDU.
For an 80MHz PPDU, the default mapping per 20MHz as shown in the figure below.

## Slide 47
For a 160MHz PPDU , the default mapping per 20MHz is as shown in the figure below
No objection

## Slide 48: 1315r1 Straw Poll #2
Do you agree to add the following text to the 11ax SFD:
A compression bit is carried in the HE-SIG-A MU format to differentiate full BW MU-MIMO from OFDMA MU PPDU.
In case of full BW MU-MIMO, the following conditions hold:
  Only applicable for RU sizes 242,484,996,2*996
  The RU information in HE-SIGB common is not signaled
  For bandwidths > 20MHz, the user specific sub-fields are split equitably between the two HE-SIG-B Channels
No objection

## Slide 49: Wednesday PM2
11-15/1324 MCS for HE-SIG-B (Q&A, SP)
11-15/1335 HE-SIG-B Contents
11-15/1304 Supported Resource Allocations in SIG-B
11-15/1059 SIG-B Encoding Structure Part II
11-15/1350 Spatial Configuration And Signaling for MU-MIMO
11-15/1354 SIGA fields and Bitwidths

## Slide 50: 1324r0 Straw poll #1
Do you agree to add to TGax Specification Framework Document
  Signaling in the first encoded part (HE-SIG-A) has the following MCS values for HE-SIG-B:
    MCS0, MCS1, MCS2, MCS3, MCS4, MCS5
    Other MCS is TBD
  Signaling for HE-SIG-B MCSs has 3 bits
    If two MCS set for BW40MHz are to be signaled, additional TBD bits used
Y: 34
N: 0
A: 9

## Slide 51: 1335r2 SP#1
Do you agree to modify the text in IEEE 802.11ax SFD(r9) as follows
  Change “The exact mapping of the 8 bit to the arrangement and the number of MU-MIMO allocations is TBD.” to “The mapping of the 8 bits to the arrangement and the number of MU-MIMO allocations is defined in the following lookup table.”
Note: ‘yyy’ = 000~111 indicates number of MU-MIMO STAs.
Definition for entries with ‘x’ bits are TBD.
8 bits indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Num of entries
000 0 0000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 0001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 0010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 0011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 0100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 0101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 0110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 0111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
000 0 1000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 1001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 1010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 1011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 1100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 1101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 1110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 1111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
000 1 xxxx | Definition TBD |  |  |  |  |  |  |  |  | 16
00100 yyy | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 8
00101 yyy | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 8
00110 yyy | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 8
00111 yyy | 52 |  | 52 |  | 26 | 106 |  |  |  | 8
01000 yyy | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 8
01001 yyy | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 8
01010 yyy | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 8
01011 yyy | 106 |  |  |  | 26 | 52 |  | 52 |  | 8
011 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
10 yyy yyy | 106 |  |  |  | 26 | 106 |  |  |  | 64
11 0 00yyy | 242 |  |  |  |  |  |  |  |  | 8
11 0 01yyy | 484 |  |  |  |  |  |  |  |  | 8
11 0 10yyy | 996 |  |  |  |  |  |  |  |  | 8
11 0 11yyy | 2*996 |  |  |  |  |  |  |  |  | 8
11 1 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
Y: 50
N: 4
A: 18

## Slide 52: 1335r2 SP#2
Do you agree to add the STAID size in the user specific subfields of HE-SIGB is 11bits?
Y: 57
N: 0
A: 14

## Slide 53: 1335r2 SP#3
Do you agree to add a DCM subfield (1-bit) to the user-specific subfields of HE-SIG-B in IEEE 802.11ax SFD(r9) (as shown in red)
  For single-user allocations in a RU: NSTS (Number of Spatial Streams), TxBF (transmit beamforming ), MCS (Modulation and Coding Scheme), DCM (Dual Sub-Carrier Modulation) and Coding (Use of LDPC)
  For each user in a multi-user allocation in a RU: Spatial Configuration Fields, MCS, DCM and Coding
Y: 54
N: 0
A: 19

## Slide 54: 1304r1 Straw Poll #1
Do you agree to add the following text into the SFD?
  The 8 bits in the common field of HE SIG-B includes a state of ‘No STA Assigned’ for which no STA-specific field is transmitted
  Y: 12
  N: 26
  A: 16

## Slide 55: 1304r1 Straw Poll #2
Do you agree to add the following text into the SFD?
  The number of spatially multiplexed STAs for 106 RU limited to 4
    For RUs larger than 106, it can be 8 STAs as maximum
  Y: 5
  N: 34
  A: 16

## Slide 56: 1304r1 Straw Poll #3
Do you agree to support the following text?
  The 8 bits in the common field of HE SIG-B includes explicit states for the existence of the center 26RU of 80MHz
  Y: 9
  N: 16
  A: 25

## Slide 57: 1350r1 SP #1
Do you support to add the following text in Section x.x.x in current SFD:
  The number of spatially multiplexed user in a DL or UL MU-MIMO transmission is up to 8 (in a given RU)?
Y: 46
N: 5
A: 8

## Slide 58: 1350r1 SP #2
Do you support to add the following text in Section x.x.x current SFD:
  The Nsts value for each user in a MU-MIMO RU is less than or equal to 4?
Y: 41
N: 1
A: 7

## Slide 59: 1350r1 SP #3
Do you support to add the following text in Section x.x.x in current SFD:
  A MU-MIMO user block includes a “spatial config” field of 4bit indicating the number of spatial streams for each multiplexed STA. The field is constructed by using the entries corresponding to the value of Nuser of this RU in the following table?
Nuser | B0…B3 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | #Entries
2 | 0000~0011 | 1~4 | 1 |  |  |  |  |  |  | 10
 | 0100~0110 | 2~4 | 2 |  |  |  |  |  |  | 
 | 0111~1000 | 3~4 | 3 |  |  |  |  |  |  | 
 | 1001 | 4 | 4 |  |  |  |  |  |  | 
3 | 0000~0011 | 1~4 | 1 | 1 |  |  |  |  |  | 13
 | 0100~0110 | 2~4 | 2 | 1 |  |  |  |  |  | 
 | 0111~1000 | 3~4 | 3 | 1 |  |  |  |  |  | 
 | 1001~1011 | 2~4 | 2 | 2 |  |  |  |  |  | 
 | 1100 | 3 | 3 | 2 |  |  |  |  |  | 
4 | 0000~0011 | 1~4 | 1 | 1 | 1 |  |  |  |  | 11
 | 0100~0110 | 2~4 | 2 | 1 | 1 |  |  |  |  | 
 | 0111 | 3 | 3 | 1 | 1 |  |  |  |  | 
 | 1000~1001 | 2~3 | 2 | 2 | 1 |  |  |  |  | 
 | 1010 | 2 | 2 | 2 | 2 |  |  |  |  | 
5 | 0000~0011 | 1~4 | 1 | 1 | 1 | 1 |  |  |  | 6
 | 0100~0101 | 2~3 | 2 | 1 | 1 | 1 |  |  |  | 
6 | 0000~0010 | 1~3 | 1 | 1 | 1 | 1 | 1 |  |  | 4
 | 0011 | 2 | 2 | 1 | 1 | 1 | 1 |  |  | 
7 | 0000~0001 | 1~2 | 1 | 1 | 1 | 1 | 1 | 1 |  | 2
8 | 0000 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Y:48
N:1
A:10

## Slide 60: 1059r2 SP #1
Do you agree to modify the text in Section 3.2.4 of the SFD as follows
Two users are grouped together and jointly encoded in each BCC block in the user specific section of HE-SIG-B
The CRC in the common block is TBD
The common block has a CRC separate from the CRC of the user specific blocks
The last user information is immediately followed by tail bits (regardless of whether the number of users is odd or even) and padding bits are only added after those tail bits
Yes: 56
No: 0
Abs: 7
SIG-B
Common
User-specific
2 users + CRC + Tail
…
2 users + CRC + Tail
1 or 2 users + CRC + Tail
Common bits + CRC +Tail
1 BCC Block
1 BCC Block
Last BCC Block
1 BCC Block
Padding

## Slide 61: 1354r1 Strawpoll 1
Do you agree to add to the TG Specification Frame work document: the HE-SIG-A field definitions for SU preamble format in [2] (PHY Motions 43, 46, 48, 54) shall be replaced with the table in slide 11?
Yes: 54
No: 0
Abs: 7

## Slide 62: 1354r1 Strawpoll 2
Do you agree to add to the TG Specification Frame work document: the HE-SIG-A field definition for the MU preamble format [2] (PHY Motions 44, 46, 54) shall be replaced with the table in slide 12?
Yes: 50
No: 0
Abs: 7

## Slide 63: 1354r1 Strawpoll 3
Do you agree to add to the TG Specification Frame work document: the HE-SIG-A field definition for trigger based UL preamble format in [2] (PHY Motion 45) shall be replaced with the table in slide 13?
Yes: 51
No: 0
Abs: 10