## Slide 1: Hybrid Multiple Access in 802.11ax
Date: 2015-11-04
Authors:
Name | Affiliations | Address | Phone | Email
Yanyan Guo | Beijing Bai Hui Wei Kang Technology Co. Ltd. | Beijing, China |  | luegyy@163.com
Guixia Kang | Beijing University of Posts and Telecommunications | Beijing, China |  | gxkang@bupt.edu.cn
Ningbo Zhang | Beijing University of Posts and Telecommunications | Beijing, China |  | nbzhang@bupt.edu.cn
Doc.: IEEE xxxx-xx

## Slide 2: Background
Internet of Things (IoT) is an important scenario in the future
  Hundreds of billions of M2M UEs will access the network.
  Massive connections require 802.11ax to improve the capacity of access
Massive connections result in serious resource collision issue
  Orthogonal multiple access (OMA) random access (RA) is traditional RA in 802.11 and LTE systems
  NOMA with successive interference cancellation (SIC) is a positional technique to improve the spectral efficiency as well as the number of accesses
Doc.: IEEE xxxx-xx

## Slide 3: Current CSMA scheme in 802.11ac
CSMA (OMA scheme)
  Only one STA is allowed to transmit message in a channel
  When detecting the resource is occupied, it regards the detection as a collision and reattempts random access after a back-off.
Doc.: IEEE xxxx-xx

## Slide 4: Performance of NOMA
(MMSE-SIC) receiver is performed at AP
  The performance of NOMA degrades compared to OMA
  There exists SNR threshold between the OMA RA and the NOMA RA for a target BLER. Taking as the target BLER, the SNR threshold is about 6.3dB
Transport block size (TBS) :100 bits
Modulation order: QPSK
The number of STAs in Group A: Two
The number of STAs in Group B: Three
Channel model: Extended pedestrian A (EPA)
Difference of received power : 5dB
Doc.: IEEE xxxx-xx

## Slide 5: Hybrid RA in 802.11ax
Access mode selection
  Received SNR at AP
  where is the variance of noise and is the received power at AP.
Fig.2 Hybrid RA scheme
Doc.: IEEE xxxx-xx

## Slide 6: NOMA RA
Step 1: Peer discovery: This step is to discover neighbor paired STAs.
Step 2: NOMA group establishment: Select a group center and allocate the power back-off index.
Step 3: Channel detection: The group center sends preamble to detect the channel on behalf of NOMA group.
Step 4: Detection response: AP sends back the detection response to NOMA group STAs.
Step 5: Power back-off: NOMA group STA power back-off to guarantee diverse received power at AP.
Step6: SIC reception and ACK: AP performs SIC receiver to cancel multi-STA interferences and sends back ACK/NACK.
Doc.: IEEE xxxx-xx

## Slide 7: Simulation results
Observations
  Hybrid RA scheme increases the total number of accesses by 55.7% compared to OMA RA scheme.
Fig.3 The number of accesses for OMA RA and hybrid RA
Parameters | Value
Radius of AP | 500m
Carrier frequency | 2GHz
Bandwidth | 20MHz
 | 23dBm
 | 1
Fading channel model | Extended Pedestrian A
TBS | 100bits
Modulation order | QPSK
Target BLER | 
Receiver at eNB | MMSE-SIC
Simulation assumptions
Doc.: IEEE xxxx-xx

## Slide 8: Summary
Hybrid RA significantly improve the number of accesses
  STA adaptively selects the OMA RA procedure or the NOMA RA according to a predefined SNR threshold.
  AP performs SIC receiver to cancel multi-STA interferences.
  Clearly, adaptive OMA RA and NOMA scheme achieves larger number of accesses than OMA RA scheme.
Next step
  Work out an practical SNR threshold set for OMA RA and NOMA selection.
  Calibrate the WLAN system level simulation with hybrid RA scheme for a number of simulation scenarios.
Doc.: IEEE xxxx-xx

## Slide 9: References
[1] IEEE 802.11ac-2013, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications--Amendment 4: Enhancements for Very High Throughput for Operation in Bands below 6 GHz,” 2013.
[2] IEEE 802.11ad-2012, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band,” 2012.
Doc.: IEEE xxxx-xx

## Slide 10
Thanks!
Doc.: IEEE xxxx-xx