## Slide 1: Thoughts on 802.11 in a 3GPP 5G Network
Date: 2015-11-10
Authors:

## Slide 2: Abstract
The work to define what a 5G network is has begun.
Many groups, companies, and individuals are providing use cases and their views on what 5G networks should do. One group working to define a 5G network is 3GPP and they are working in conjunction with many government, corporate, and academic groups to do so. Based on currently available information this contribution attempts to provide some insight as to how 802.11 can fit in the 3GPP 5G network as a RAT.

## Slide 3: Contents
What is a 5G network
5G RAT requirements
Background on 3GPP integration of 802.11
Where do we go from here?

## Slide 4: A 5G Network
A 5G Network is a next generation network
  This means many things to many people
3GPP has defined the 4G Cellular Phone Network
  LTE and LTE-A
  This network consists of both a RAN (Radio Access Network) and a CN (Core Network)
3GPP has begun to develop its vision for a 5G Network
  I am pulling information from the NGMN 5G white paper [1] and from various 3GPP sources to define a view of a 5G Network
The intent is not do define what a 5G Network will be but to discuss how 802.11 might fit with my guess at what the 3GPP 5G network may be.

## Slide 5: 5G Use Case Families [1]

## Slide 6: The 5G Network Slice/Infrastructure [1]
Common Infrastructure
UP- User Plane
CP -Control Plane

## Slide 7: A 5G network needs a RAT to support:
Connectivity: wirelessly connect users to the network
Connectivity transparency:
  the best user experience, without user intervention
  Seamless connectivity, without service interruption – including user authentication
  Network control for operator preferences and user subscription
  Transparent connection management (HO, Stream Control, …)
Location services:
  In support of contextual attributes for instant/personal services
Security:
  Subscriber Authentication
  User Privacy
  Network Security

## Slide 8: Is 802.11 a RAT?
RAT = Radio Access Technology
There will be multiple 5G RATs
  Legacy: LTE, UMTS, GSM, 802.11?
  3GPP New RATs (<6GHz, >6GHz)
  Non-3GPP RATs: 802.11ax, 802.11ay, 802.11ah …
In a 5G network it is expected that a terminal/device may be connected to several RATs at a given instant
  RAT aggregation
  Carrier/Band aggregation
  Higher Layer aggregation

## Slide 9: The 5G Use Case Triangle
Throughput
Many Devices/Cost/Power
Latency/Reliability
Critical Communications: V2V, V2X, Tactile
Massive Broadband
Massive M2M
.11ax
.11p
.11ah
.11ac
.11n
.11ad
.11ay
Where does 802.11 fit in the use case triangle?

## Slide 10: How should 802.11 work with a 5G network?
To fit in a 3GPP 5G network a RAT should:
Be controllable
Enable users access to the network
Enable the network to optimize data and services to the user, typically requiring:
  Access control (who can use network resources, and how much)
  Handover (how mobile users maintain their connection)
  Service control (which services are available to the user)
  Data stream control (how data flows on multiple RATs to the user)
  Security, user identification, and privacy

## Slide 11: Some Background How does 3GPP “work” with 802.11 now
Some current Wi-Fi / 3GPP “Interworking”:
3GPP Core access via:
  WAF (Wireless Access Gateway)
  Packet Data Gateway
  (ePDG) enhanced packet data Gateway
“Control” via:
  3GPP Access Network Discovery and Selection Function (ANDSF)
  3GPP RAN Controlled LTE-WLAN Interworking (RCLWI)*
  *On going 3GPP RAN2 WI

## Slide 12: 3GPP 4G Architecture [2]
Legend:
Bold lines: interfaces supporting user traffic;
Dashed lines: interfaces supporting signalling.

## Slide 13: Configuration of a 3GPP/WLAN interworking function [3]

## Slide 14: ANDSF: Mobile Services Discovery Protocol [4]
Provides 3GPP Mobiles (UEs) information about available networks and policies for selecting and using such networks
Primary function is selecting non-3GPP access networks, in particular 802.11-based (WLAN) networks
  Also includes CDMA2000 info, WiMaX info, etc.
Location (and UE) specific
Relatively static: (currently) not intended to be responsive to real-time network conditions
Allows UE to Locate ANDSF Server and “Pull” ANDSF Information

## Slide 15: Access Network Discovery and Selection Function (ANDSF) [4]
Services
Service Provider NW
P-GW
WLAN /
Unlicensed Band
ANDSF Server
UE/STA
Terminal Selects & Connects to WLAN
Allocate Specific App Flows to Specific Links
Terminal Fetches Policy

## Slide 16: RAN Controlled LTE-WLAN Interworking RCLWI: Overall E-UTRAN Architecture [5]
WLAN Termination (WT) terminates the Xw interface

## Slide 17: Current 3GPP/802.11 Status
Virtually all “smart” phones have 802.11 capability
Many cellular operators use 802.11 for network “Offload” to boost/enable high speed data
802.11 is not well integrated with 3GPP core networks
  Limited Control of Data Flow (for multiple RATs)
  Limited 802.11 configuration control (only some elements)
  No real time handover, limited to relative performance rules
  No true QoS capability, only some relative best effort rules
  No real time access control, limited non-real time access control
  Limited service control
  Limited support of security, user identification, and privacy

## Slide 18: Where Do We Go From Here?
Does 802.11 attempt to enable/define/specify the capabilities to make 802.11 a fully functioning RAT that can be integrated in a 5G network?
Does 802.11 continue to rely on 3GPP to define 802.11’s place in the 5G network?
Does 802.11 need to define an 802.11 RAN?
Should 802.11 work with 802.1, 802.3, 802.15, … to define a 5G network? An IMT 2020 technology?
What areas should 802.11 work to enable capability?:
  Access Control
  Handover
  QoS support
  Enable 802.11 RATs Aggregation with other 5G RATs
  Security
  Privacy

## Slide 19
Access Router
Access Network
Terminal
Should 802.11 work to support 802.1 OmniRAN network view? [6]
Terminal Interface
R1
Coordination and Information Service
R2
R10
R8
AN Ctrl
TE Ctrl
Subscription
Service
Access Router Interface
R3
R4
AR Ctrl
R9
NA
Backhaul
R6
R5
R7
R11
STA
AP
NA = Node of Attachment {AP, BS}
Radio interface components

## Slide 20: References
NGMN 5G White Paper, NGMN Alliance, 11-15/0322r01
3GPP TS 23.002 v13.3.0, 3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Network architecture (Release 13) TS23002-d30
3GPP TS 23.234 v12.0.0, 3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3GPP system to Wireless Local Area Network (WLAN) interworking; System description (Release 12) TS23234-c00
WLAN and Cellular Interworking and Discovery Use Case, Joseph Levy and Juan Carlos Zuniga 11-12/0346r0
Running 36.300 CR for LTE-WLAN Radio Level Integration and Interworking Enhancement R2-154997
Max Riegel, Radio Interface Component from an OmniRAN perspective https://mentor.ieee.org/omniran/dcn/15/omniran-15-0044-00-CF00-radio-interface-component.pptx