## Slide 1: SB1000 CID 6304 PHY-CCARESET.request
Date: 2015-11-10
Authors:

## Slide 2: Abstract
Addressing Sponsor Ballot 1000 CID 6304.

## Slide 3: CID 6304 and Context
6304 | 7.3.5.10.4 | 551 | 36 | "reset the PHY CS/CCA timers" -- what PHY CS/CCA timers | Refer explicitly to the timers being reset
Cited text from PHY-CCARESET.request():
7.3.5.10.4 Effect of receipt
The effect of receipt of this primitive by the PHY entity is to reset the PHY CS/CCA timers to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle. If IPI-STATE parameter is IPI-ON, the PHY entity collects IPI values when it is not transmitting or receiving and provides those values to the MAC sublayer using the IPI-REPORT parameter.

## Slide 4: Example PHY Receiver
18.3.12 Receive PHY
The received PSDU bits are assembled into octets, decoded, and presented to the MAC using a series of PHY-DATA.indication(DATA) primitive exchanges. The rate change indicated in the SIGNAL field shall be initiated from the SERVICE field data of the PHY header, as described in 18.3.2 (PPDU format). The PHY shall proceed with PSDU reception. After the reception of the final bit of the last PSDU octet indicated by the PHY preamble LENGTH field, the receiver shall be returned to the RX IDLE state, as shown in Figure 18-19 (Receive PHY). A PHY-RXEND.indication(NoError) primitive shall be issued.
In the event that a change in the RSSI causes the status of the CCA to return to the IDLE state before the complete reception of the PSDU, as indicated by the PHY LENGTH field, the error condition shall be reported to the MAC using a PHY-RXEND.indication(CarrierLost) primitive. The CCA of the OFDM PHY shall indicate a busy medium for the intended duration of the transmitted packet.
To determine the correct number of octets in the reception and the duration of the packet, a counter or timer is implied, but no explicit implementation is prescribed or required. This is the timer that is referenced by the primitive.

## Slide 5: Use of PHY-CCARESET
9.3.2.1 CS mechanism
At aRxTxTurnaroundTime + AirDelay + aRxPHYDelay + 10% of aSlotTime after each MAC slot boundary as defined in 9.3.7 (DCF timing relations) and 9.22.2.4 (Obtaining an EDCA TXOP), the MAC shall issue a PHY-CCARESET.request primitive to the PHY

## Slide 6: Suggested Actions - Reject
Reject
  Existence of at least one counter/timer based on the PHY LENGTH field is implied in the description of the PHY receiver behavior.
  I.e. the PHY LENGTH field timer should be reset if PHY-CCARESET.request() is issued.
  Note that resetting this timer this would effectively abort any RX that has reached the end of PHY SIGNAL field decode at the time of the issuance of the SAP.

## Slide 7: Suggested Actions – Revise (1)
Revise choice 1
  Change: The effect of receipt of this primitive by the PHY entity is to reset the PHY CS/CCA timers to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle.
  To: The effect of receipt of this primitive by the PHY entity is to reset the PHY RECEIVER to the RX IDLE state, to issue PHY-CCA.indication(IDLE) and PHY-RXEND.indication(CarrierLost) and to initiate a new CCA evaluation cycle.
Does this go too far, by affecting not just the CCA, but also resetting the receiver? Not an easy question.

## Slide 8: PHY-RXEND.indication() RXERROR parameter values
- NoError. This value is used to indicate that no error occurred during the receive process in the PHY.
— FormatViolation. This value is used to indicate that the format of the received PPDU was in error.
— CarrierLost. This value is used to indicate that during the reception of the incoming PSDU, the carrier was lost and no further processing of the PSDU can be accomplished.
— UnsupportedRate. This value is used to indicate that during the reception of the incoming PPDU, a nonsupported date rate was detected.
— Filtered. This value is used to indicate that during the reception of the PPDU, the PPDU was filtered out due to a condition set in the PHYCONFIG_VECTOR.

## Slide 9: Suggested Actions – Revise (2)
Revise choice 2
  Change: The effect of receipt of this primitive by the PHY entity is to reset the PHY CS/CCA timers to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle.
  To: The effect of receipt of this primitive by the PHY entity is to reset the PHY RECEIVER to the RX IDLE state, to issue PHY-CCA.indication(IDLE) and PHY-RXEND.indication(RxAborted) and to initiate a new CCA evaluation cycle.
  And add a new RXERROR parameter value to 7.3.5.14.2 Semantics of the service primitive:
    - RxAborted. This value is used to indicate that during the reception of the incoming PPDU, a PHY-CCARESET.request() primitive was received.

## Slide 10: Suggested Actions – Revise (3)
Revise choice 3
  Change: The effect of receipt of this primitive by the PHY entity is to reset the PHY CS/CCA timers to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle.
  To: The effect of receipt of this primitive by the PHY entity is to reset the PHY CS/CCA counter to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle.
  Explicitly mention a timer in 18.3.12 Receive PHY:
    And all similar language in all PHY subclauses,
    See next slide

## Slide 11: 18.3.12 Receive PHY
The received PSDU bits are assembled into octets, decoded, and presented to the MAC using a series of PHY-DATA.indication(DATA) primitive exchanges. The rate change indicated in the SIGNAL field shall be initiated from the SERVICE field data of the PHY header, as described in 18.3.2 (PPDU format). The PHY shall proceed with PSDU reception. After the reception of the final bit of the last PSDU octet indicated by a counter based on the PHY preamble LENGTH field, the receiver shall be returned to the RX IDLE state, as shown in Figure 18-19 (Receive PHY). A PHYRXEND.indication(NoError) primitive shall be issued.
In the event that a change in the RSSI causes the status of the CCA to return to the IDLE state before the complete reception of the PSDU, as indicated by a counter based on the PHY LENGTH field, the error condition shall be reported to the MAC using a PHY- RXEND.indication(CarrierLost) primitive and the PHY receiver shall return to the RX IDLE state. The CCA of the OFDM PHY shall indicate a busy medium for the intended duration of the transmitted packet.

## Slide 12: Comment on revise choice 3
As mentioned before, resetting the counter is equivalent to terminating the Receive process, and the existing language implies this as well:
to the state appropriate for the end of a received frame
So perhaps choice 2 is better.
Or……maybe choice 4:

## Slide 13: Suggested Actions – Revise (4)
Revise choice 4
  Change: The effect of receipt of this primitive by the PHY entity is to reset the PHY CS/CCA timers to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle.
  To: The effect of receipt of this primitive by the PHY entity is to reset the PHY CCA mechanism to IDLE, to issue PHY-CCA.indication(IDLE) and to initiate a new CCA evaluation cycle.

## Slide 14: There is a PHY CCA mechanism:
18.3.6 CCA
The PHY shall provide the capability to perform CCA and report the result to the MAC. The CCA mechanism shall detect a “medium busy” condition with requirements specified in 18.3.10.6 (CCA requirements) and 18.3.12 (Receive PHY). The PHY issues the PHY-CCA.indication primitive to provide this medium status report to the MAC

## Slide 15: References
Draft P8021.11REVmc_D4.0.pdf
Draft P802.11REVmc_D4.3.pdf