## Slide 1: Drivers of the dynamic CCA adaptation
Authors:
Date: 2015-11-11

## Slide 2: Outline
Context
Communication model
Optimal setting of CCA Threshold
DSC vs. fixed CCA threshold scheme
Conclusions
References

## Slide 3: 1. Context
  Many contributions to the TGax study CCA adaptation (more than 70 references and counting [1])
    (…and many of them start with this same sentence)
  Most of the studies are based on static CCA thresholds settings; few dynamic/adaptive mechanisms were proposed (based on intuitive heuristics).
    In all cases, throughput improvements are observed
  Following a simple approach, in this work we try to provide a theoretical background to better understand CCA adaptation and its drivers.

## Slide 4
is an IEEE 802.11 STA
  Pt tx power
  Sr receiver sensitivity
    Rr reception range
    d is the distance tx  rx
    α is the path loss exponent
represents a tx  rx link
For simplicity, assume that all nodes have equal properties (i.e. same Pt, Sr, etc.)
Rr
A
X
B
E
C
G
H
F
D
2. Communication model

## Slide 5: 2. Communication model
is an IEEE 802.11 STA
  Pt tx power
  CCATh carrier sense Threshold
    Rc carrier sense range
    d is the distance tx  rx
    α is the path loss exponent
represents a tx  rx link
A
X
B
For simplicity, assume that all nodes have equal properties (i.e. same Pt, Sr, etc.)
Rc
E
C
G
H
F
D

## Slide 6
Capture effect
  Upon a collision, the receiver locks to a strongest PPDU provided that it is, at least, CTh times stronger than the current frame.
    CTh : capture threshold
  This ability defines the interference range (Ri)
    Any ‘s transmission within Ri is received with power not CTh times lower than the wanted transmission  prevents the wanted transmission to benefit from the capture effect  upon collision, prevents the correct reception of the wanted transmission.
  Interesting behavior that allows increasing spatial reuse [4]
2. Communication model
X

## Slide 7: 2. Communication model
is an IEEE 802.11 STA
  Pxy power received at Y from X
  dxy distance between Y and X
  CTh capture threshold
    if is at the edge of B’s Ri
    α is the path loss exponent
A
X
B
For simplicity, assume that all nodes have equal properties (i.e. same Pt, Sr, etc.)
E
C
G
H
F
D
C
Ri
(*)

## Slide 8: 2. Communication model
Setting an optimal CCATh
  Leverage the capture effect
  Ideally ’s Rc limits coincide with B’s Ri limits (increases spatial reuse while avoids destructive interference)
  In the worst case (A, B and C are on the same line):
  from (*):
A
B
For simplicity, assume that all nodes have equal properties (i.e. same Pt, Sr, etc.)
Ri
E
C
G
H
F
D
Rc
A
B
+
R*c

## Slide 9: 3. Optimal setting of CCATh
From our simple communication model
  (realistic) Numerical example:
    STA receives -40dBm from its AP
    CTh = 15dB CCATh ≈ -60dBm
    α = 3.5
    That is, in terms of DSC algorithm [2]: CCATh can be computed from the measured power of received beacons minus a Margin
      By means of simulations, in [3] the optimal Margin was found to be 20dB
Margin = 20dB

## Slide 10: 3. Optimal setting of CCATh
From a more generic perspective
  CCATh = f(CTh , path losses, Pt )
    CTh = f(MCS, preamble/payload stage,...see [5])
  CCATh should be different at each STA and it should vary dynamically (with tx power, mobility, MCS, etc.)

## Slide 11: 4. DSC vs. fixed CCA threshold scheme
  To support our previous claim we run simulations in residential building scenario: dynamic/adaptable approach (DSC) vs. best fixed threshold (FCST)
    NS-3 simulations
      IEEE 802.11n without aggregation (other simulation details can be found in [3]).
      FCST = -65dBm
Chart: % Increase
| DSC | FCST
Throughput | 6.7694 | 5.8536
Fairness | 2.3183 | 13.8074
Chart: % Increase
| DSC | FCST
FER | 37.0296 | 73.0902
Hidden nodes | 24.9489 | 44.7286
DSC slightly outperforms FCST in terms of throughput
DSC provided better FER when compared with FCST.

## Slide 12: 5. Conclusions
  In this presentation, we provide a simple communication model to justify the use of dynamic CCATh adaptation
    Improve spatial reuse while keeping interference at acceptable levels
  Sensible adaptation of CCATh should depend on:
    TX Power
    MCS of transmission
    Type of scenario (different propagation loss characteristics)
  Simulation results support our claim that the drawbacks of increasing spatial reuse are reduced when CCATh is adapted per STA.

## Slide 13: 7. References
[1] 11-15/1138r1, “To DSC or not to DSC”
[2] 11-13/1290r1, “Dynamic Sensitivity Control for HEW”
[3] 11-15/0027r1, “Simulation-based evaluation of DSC in residential scenario”
[4] 11-15/1302r2, “System Level Simulator Evaluation with/without Capture Effect”
[5] J. Lee, W. Kim, S.-J. Lee, D. Jo, J. Ryu, T. Kwon, and Y. Choi, “An experimental study on the capture effect in 802.11a
networks,” in ACM WiNTECH, 2007