## Slide 1: What is the status of the ETSI BRAN work on a revised version of EN 301 893?
10 Nov 2015
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com

## Slide 2: EN 301 893 revision is progressing in ETSI BRAN but more participation by Wi-Fi folk is encouraged
802.11 operation in Europe is based on EN 301 893 as authorised by European Directive 1999/5/EC
A revision of EN 301 893 is required by early 2016 to support a new European Directive 2014/53/EC
The work in ETSI BRAN revising EN 301 893 has been focused on a new adaptivity clause
RSC and TCAM have determined that fairness is a key requirement for adaptivity in the 5GHz band
ETSI BRAN has made significant progress on a new adaptivity clause but there are still major open issues
Scheduling issues make the development of new adaptivity clauses in EN 301 893 challenging!
New EN 301 893 is required
Most work is focused on fairness in adaptivity
Progress is being made but there are open issues
Companies that want to support Wi-Fi coexistence in Europe are encouraged to participate in ETSI BRAN or at least assist the effort

## Slide 3: 802.11 operation in Europe is based on EN 301 893 as authorised by European Directive 1999/5/EC
  IEEE 802.11 equipment is currently subject to requirements authorised by the European Directive 1999/5/EC
  EN 301 893 documents explicit requirements for operation in the 5GHz band in Europe, as authorised by 1999/5/EC, including:
    Frequencies
    Bandwidths
    Power
    Spurious emissions
    DFS
    Adaptivity
    …
  EN 301 893 also includes some simple tests against some of these requirements

## Slide 4: A revision of EN 301 893 is required by early 2016 to support a new European Directive 2014/53/EC
  A new EC Directive (2014/53/EC) repeals the previous EC Directive (1999/5/EC) on radio equipment
  The main objective of the new Directive is to provide:
    a high level of protection of health and safety, adequate level of electromagnetic compatibility and an effective and efficient use of radio spectrum so as to avoid harmful interference while guaranteeing the proper functioning of the internal market
  Essential requirements include requirements for effective & efficient use:
    Radio equipment shall be so constructed that it both effectively uses and supports the efficient use of radio spectrum in order to avoid harmful interference
  The new Directive comes into effect in June 2017 …
  … but EN 301 893 will need to be revised by early 2016 to allow approval and transition processes to be executed in time

## Slide 5: The work in ETSI BRAN revising EN 301 893 has been focused on a new adaptivity clause
  One key element of EN 301 893 is the adaptivity requirement
    Adaptivity is formally defined as an automatic channel access mechanism by which a device avoids transmissions in a channel in the presence of transmissions from other RLAN devices in that channel.
    There is an implicit goal of fair sharing of the channel, which is compatible with the goal of 2014/53/EC for effective channel use
  It is accepted that the current adaptivity clause in EN 301 893 needs a significant rewrite
    There is a desire to make EN 301 893 more “technology neutral”, which requires the removal of the direct reference to IEEE 802.11 in the current version
    The current version of EN 301 893 includes two “load based” and one “frame based” adaptivity mechanism that are known to not work
  ETSI BRAN has been focusing on developing a new adaptivity clause in EN 301 893 since December 2014

## Slide 6: RSC and TCAM have determined that fairness is a key requirement for adaptivity in the 5GHz band
  The requirement for fairness is implicit rather than explicit in the European Directive 2014/53/EC
  Fortunately, a meeting of two European Commission committees on 8 Oct 2015 provides clarity
    Radio Spectrum Committee (RSC)
    Telecommunications Conformity Assessment & Market Surveillance Committee (TCAM)
  In a discussion on Compliance of 5 GHz RLANs and LTE unlicensed use in the 5 GHz band (compatibility with other radio applications, coexistence between Wi-Fi and LTE unlicensed) they determined that:
    … coexistence means the fair use of the spectrum, which should ensure equal access for all technologies and applications …

## Slide 7: ETSI BRAN has made significant progress on a new adaptivity clause but there are still major open issues
  At the last ETSI BRAN F2F meeting in Oct 2015 it was agreed to base future discussions on EN(15)150r2 (available via liaison agreement)
  It includes some important agreements, with the most fundamental being it incorporation of LBT with exponential back using a scheme very similar to EDCA
  It also documents a variety of open issues
    Most of the issues are minor or editorial and will be resolved over time after ongoing discussions
    Three open issues can be described as “major”
  The major open issues are:
    What is the definition of the energy detect (ED) threshold?
    What is an appropriate value of max TxOP?
    What are the multi-channel requirements?

## Slide 8: What is the definition of the energy detect (ED) threshold? There are two options on the table!
“Evidence based” proposal enables fair coexistence
  Proposal
    ED of -62dBm and PD of -82dBm (like Wi-Fi); OR
    ED of ~-77dBm
  Comments
    The first option is based on status quo for billions Wi-Fi devices
    The second option is based on 3GPP simulations that show LAA needs ED of ~-77dBm to coexist fairly with Wi-Fi
    Note: It is asserted many Wi-Fi devices do not satisfy these rules
“Alternate” proposal requires us to trust 3GPP to share fairly
  Proposal
    ED of -62dBm
  Comments
    Based on the idea that 3GPP can be trusted to define LAA in such a way that it maintains fairness …
    … and that all implementers in this band will follow 3GPP rules!

## Slide 9: What is an appropriate value of max TxOP? There are at least two proposals on the table
Wi-Fi based max TxOP enables proven fairness
  Proposal
    6ms
  Comments
    Value is compatible with max frame length in 802.11
    Value based on extensive 3GPP simulations that show fairness between LAA & Wi-Fi, particularly for real time QoS traffic
    Note: it is asserted many Wi-Fi devices do not satisfy this rule
LTE based max TxOP promotes efficiency over fairness
  Proposals
    10ms; OR
    6ms DL + 6ms UL; OR
    8ms (compromise?)
  Comments
    Use of larger value promotes efficiency over fairness
    Longer value allows for UL and DL in LAA, as well as LTE protocol derived delay between DL ending and UL starting

## Slide 10: What are the multi-channel requirements? There are at least two proposals on the table
Wi-Fi based multi-channel promotes LAA/Wi-Fi fairness
  Proposal
    Use a primary/secondary multi-channel similar to 802.11
  Comments
    Using same mechanism as Wi-Fi guarantees fair sharing
Looser multi-channel prioritises efficiency over fairness
  Proposal
    Allow all of the multiple channels to be a primary channel and once access gained, allow the remaining channels to be a secondary channel
  Comments
    This mechanism allows LAA to make more efficient use of multiple channels …
    … but at cost of unfair access to the channel compared with Wi-Fi

## Slide 11: Scheduling issues make the development of new adaptivity clauses in EN 301 893 challenging!
  EN 301 893 needs to be finished very soon, but probably by March 2016 at the latest to allow time for approval and transition
  At the same time:
    3GPP is developing LAA with a nominal completion date of March 2016, but probably later
    … and IEEE 802.11 WG is developing 802.11ax, with a nominal completion date of ~1919
    … and billions of IEEE 802.11a/n/ac need to remain compatible with the EN 301 893 revision
  The challenge is that a revision of EN 301 893 needs to enforce fair sharing of the 5GHz band …
    between technologies that already exist
    and multiple technologies in various stages of development
  … without unduly limiting innovation

## Slide 12: There are two proposals in ETSI BRAN to address the scheduling challenge
“Two step” is based on what we know at various times
  Proposal
    Define EN 301 893 based on what we know about LAA/802.11a/n/ac coexistence today
    Once complete start a new project to revise it again once we know more about LAA and LAA/802.11ax coexistence
  Comments
    This approach is a nice balance between allowing innovation, while ensuring coexistence and not risking the immense value of Wi-Fi today
“Open” is based on trusting all to do the “right thing”
  Proposal
    Define EN 301 893 once with very broad constraints to ensure innovation is not constrained
  Comments
    This approach relies on 3GPP (and promoters of other technologies) to design their protocols to share fairly
    It also puts the ability of Wi-Fi to fulfil the promise of “anyone, anytime, anyplace can put together a network that meets their needs”

## Slide 13: Companies that want to support Wi-Fi coexistence in Europe are encouraged to participate
  The goal of todays presentation is twofold
    Inform IEEE 802.11 WG about the work being done in Europe to protect the huge socioeconomic value derived from Wi-Fi (noting this work will have an indirect impact on sharing in the US and around the world)
    Encourage IEEE 802.11 WG members to participate in the ETSI BRAN process - the companies that have supported Wi-Fi in this forum are few in number but have had a massive impact – thank you!
  If your company is an ETSI member then you can participate in a
    Teleconference on 3 December
    F2F meeting in Germany on 14-18 December
  If you are not an ETSI member you can still help by contributing to the work of those companies supporting Wi-Fi in ETSI BRAN
  Contact Andrew Myles (amyles@cisco.com) for details