## Slide 1: Updated Simulation Results for Box5
Date: 2015-11-05
Authors:
Name | Affiliation | Address | Email
Zhiqiang Han | ZTE |  | han.zhiqiang1@zte.com.cn
Ke Yao | ZTE |  | yao.ke5@zte.com.cn
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn
Yonggang Fang | ZTE |  | yfang@ztetx.com

## Slide 2: Abstract
  The submission provides updated simulation results for Box-5 calibration.
  Applying the assumptions about preamble detection and other issues like receiving procedure in .
  Some further details in our simulation are listed in the following slides.

## Slide 3: Box5 Calibration Scenario
11ac SS6 – OBSS Enterprise [1]
AP C | (-40,-20)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
AP A | (0,0)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
AP B | (40,20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)

## Slide 4: 11ac SS6 Traffic Flow Model
DL/UL traffic assigned for each STA
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow

## Slide 5: Box-5 PHY Details
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 dB standard deviation) per link
Data Preamble Type | [5GHz, 11ac], always decoded correctly after successful reception, duration is considered.
STA TX Power | 15 dBm per antenna
AP TX Power | 20 dBm per antenna
AP number of TX/RX antennas | 1/1
STA number of TX /RX antennas | 1/1
Capture Window | [0 ns 800ns]
preemption window | [0 ns]
AP antenna gain | 0 dBi
STA antenna gain | -2 dBi
Noise Figure | 7dB
CCA threshold ( CCA-SD) | -76dBm (measured across the entire bandwidth after large-scale fading)
ED threshold (CCA-ED) | -56dBm
Link Adaption | Fixed MCS =7 (292.5Mbps)
Channel estimation | ideal
PHY abstraction | RBIR, BCC [1, 5]
Channel correlation | Independent or time-correlated channel per packet

## Slide 6: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3]
Queue length | 2000 packets length multiplied by the STA number inside AP; 2000 packets length inside STA
Traffic type | UDP CBR with rate 10^8bps. The same traffic is attached to each STA or AP.
MPDU size | 1530 Bytes (1472 MSDU + 36 UDP、IP、LLC header + 30 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU with immediate BA], Max aggregation: 32 MPDUs with 4-byte MPDU delimiter (with 2 bytes padding)
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Traffic direction | UL Only, DL only, Mixed DL & UL
Throughput metric | CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time)

## Slide 7: Single BSS Test Result
 |  | STA 3 (Mbps) | STA 9 (Mbps) | STA15 (Mbps) | STA21 (Mbps) | STA27 (Mbps) | SUM (Mbps)
DL |  | 38.95 | 40.62 | 40.19 | 40.61 | 38.95 | 199.32
UL | 1 STA | 100.51 | 100.52 | 100.50 | 100.52 | 100.51 | 
 | 2 STA | 92.53 | 93.76 |  |  |  | 186.29
 |  | 92.938 |  | 93.46 |  |  | 186.40
 |  | 92.96 |  |  |  | 93.69 | 186.65
 | 3 STA | 60.89 | 61.87 | 58.57 |  |  | 181.33
 |  | 58.86 | 59.15 |  |  | 62.71 | 180.71

## Slide 8: Two BSSs Test Result -- DL only （A-B）
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 27
20 drops | 7.9971 | 4.4467 | 7.3815 | 6.7864 | 6.9254 | 6.0213 | 6.2082 | 3.6242 | 5.7534 | 5.9399 | 6.1127 | 6.9618 | 6.8208 | 5.8018 | 4.7794 | 5.3684 | 7.9433 | 4.4088 | 26.4129 | 27.1977 | 27.1322 | 26.3117
2-BSS DL-only results show similar trend and value with [2].
AP A and AP B can listen to each other，the Transition of A and B interact each other.

## Slide 9: Two BSSs Test Results-DL only （A-C and B-C）
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 25 | 26 | 28 | 29 | 6 | 12 | 18 | 30
20 drops | 6.8127 | 6.6855 | 7.1123 | 5.4958 | 4.748 | 7.2096 | 6.5746 | 6.7421 | 6.1345 | 5.7197 | 6.3405 | 8.4122 | 5.7824 | 6.8121 | 7.5776 | 4.8386 | 4.9188 | 5.4144 | 24.37 | 24.091 | 23.2579 | 25.9291
Chart: 
| 3 | 9 | 15 | 27 | 6 | 12 | 18 | 30
20 drops | 50.9037 | 50.1785 | 50.4018 | 51.0601 | 49.6627 | 51.1322 | 51.1389 | 50.7521

## Slide 10: Three BSSs Test Result -- DL only
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
20 drops | 2.51 | 4.8025 | 4.4874 | 4.226 | 2.8689 | 5.5492 | 5.1992 | 4.0677 | 2.3141 | 1.1666 | 1.7332 | 2.4533 | 4.4482 | 2.8983 | 4.5439 | 2.0574 | 2.6613 | 3.6198 | 36.5532 | 36.4829 | 37.2141 | 0 | 38.5051 | 34.7719 | 37.0626 | 35.2393 | 0 | 35.0434
Throughput (Mbps):
  BSS A: 61.61
  BSS B:148.755
  BSS C: 142.117

## Slide 11: Analysis
Because of the similar position of A-C and A-B, the throughput are similar.
The APs of BSS A and BSS C（or BSS B）can hear each other, they share the channel.
BSS B and BSS C can not hear each other, BSS B and BSS C can independently occupy the channel all the time.
For three BSS DL case, BSS B and BSS C have more chance to occupy the channel than two BSS cases (A-B or A-C), thanks to they can transmit separately.

## Slide 12: Two BSSs Test Results -- UL only （A-B and B-C）
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 21 | 27
20 drops | 2.6932 | 11.6885 | 17.6528 | 14.9178 | 3.1145 | 1.349 | 16.4111 | 12.4156 | 17.1114 | 2.8318 | 4.6858 | 22.8344 | 5.2937 | 65.7956 | 62.9467
Chart: 
| 3 | 21 | 27 | 6 | 24 | 30
20 drops | 60.5848 | 61.6314 | 62.742 | 62.3538 | 64.1519 | 60.4444

## Slide 13: Three BSSs Test Result -- UL only （A-B-C）
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 21 | 27 | 6 | 24 | 30
20 drops | 0.32246 | 1.8617 | 25.3058 | 8.997 | 1.3981 | 0.94748 | 21.9859 | 5.1708 | 10.1589 | 0.41919 | 0.91078 | 29.6454 | 4.2031 | 65.8436 | 65.8909 | 47.655 | 73.9573 | 21.212
Throughput (Mbps):
  BSS A：107.124
  BSS B：135.938
  BSS C：142.824

## Slide 14: Three BSSs Test Result -- DL&UL
Throughput (Mbps):
  BSS A：77.95(DL：33.16, UL:44.79)
  BSS B：130.37 (DL:90.56, UL:39.80)
  BSS C：125.07 (DL:70.01, UL:55.06)
Chart: 
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
DL | 1.821 | 1.6143 | 1.9541 | 2.213 | 1.5453 | 1.1902 | 1.9849 | 2.1846 | 2.0694 | 1.8886 | 1.7239 | 2.1649 | 2.0134 | 2.1232 | 0 | 0 | 1.7009 | 1.1894 | 1.8076 | 2.0644 | 21.4908 | 22.8169 | 22.7267 | 0 | 23.5296 | 19.7361 | 16.2864 | 17.1259 | 0 | 16.864
UL | 0.13082 | 0.3738 | 14.5422 | 1.0398 | 0.35575 | 0.0443 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.4343 | 0.77721 | 0.91335 | 0.1457 | 0.2813 | 22.7499 | 1.735 | 0 | 0 | 19.4918 | 18.5773 | 19.1075 | 0 | 0 | 29.6263 | 6.3235

## Slide 15: References
[1] 11-15-0053-00-00ax-box5-results-of-11ac-ss6.
[2] 11-15-1149-00-00ax-updated-simulation-results-for-box5-calibration