## Slide 1: NGP Use Cases For High Resolution
Date: 2016-01-12
Authors:

## Slide 2: Abstract
This document contains several use cases for high resolution location estimation
Location requirements are included with each use case to drive focus for the SIG

## Slide 3: 1. Nano Location in store
User: Person with a smartphone which has the store app installed
Environment: A store has APs for 802.11ad/ay coverage. The store has an AP on every isle
Use case:
  The user is going around in the store with their phone
  Phone location indicates whether the user is moving, or whether he stopped in front of some product
  The AP determines that the user is facing a specific product, and can offer promotional ad for competition (e.g. Pepsi instead of Coca-Cola machine)
  Locate specific item (e.g. specific size/model in clothes department)
  Power consumption profile: foreground for positioning determination, background for positioning services discovery.
  Operating mode: AP2STA
  Usage duration: 1 hour (10 minutes of foreground activity).
Expected:
  Horizontal + vertical accuracy: <1 cm@90%
  Pointing angles (AZ, EL & Roll) accuracy: <10deg
  Latency: <10ms, for motion estimation, <100ms for static estimation
  Refresh Rate: 10-100Hz (same as GPS)

## Slide 4: 2. Augmented reality
User: High-end wearable devices
Environment: User wearing glasses with augmented reality features
Use case:
  The user is wandering around, wearing glass with augmented reality features
  Exact location of the glasses is used for exact augmentation at each eye, per location. Each door which is looked at, is supplemented with an image showing behind the door scene
  Power consumption profile: foreground for positioning determination
  Operating mode: AP2STA
Expected:
  Horizontal + vertical accuracy: <1 cm@90%
  Pointing angles (AZ, EL & Roll) accuracy: <2deg
  Latency: <10ms: augmentation data is required to be tagged with the exact location
  Refresh Rate: 0.5Hz-100Hz

## Slide 5: 3. Determine dynamic (conference) room setup
User: Presenters in a conference room
Environment: Conference room
Use case:
  Determine and track the physical setup of the Laptops and Displays in the room, and make it available to the users in the room.
  Use the setup to move windows or other display elements between different laptops display and the room displays
Expected:
  Horizontal + vertical accuracy: <20 cm@90%
  Pointing angles (AZ, EL & Roll) accuracy: < 20deg
  Latency: <0.5s:
  Refresh Rate: <2Hz
  Number of users – up to 30 users, ≥3 APs

## Slide 6: 4. Proximity Detection
User: Any 60GHz device
Environment: Any environment
Use case:
  The user connects the device to the other device.
  Distance between devices is measured.
  If the distance is less than a predefined distance (10cm -100cm) special medium access rules may be applied
    For example – relaxed CCA requirements
  Operating mode: STA2STA or AP2STA
Expected:
  Ranging accuracy: <5 cm@90%
  Pointing angles (AZ, EL & Roll) accuracy: <15deg (optional)
  Latency: <200ms:
  Refresh Rate: <2Hz

## Slide 7: 5. Determining Relative Location to Dock(s)
User: Person with a Laptop/Tablet looking for docking
Environment: Enterprise cubicle environment
Use case:
  The user is walking in an enterprise environment
  User is presented with a list of docks, with the direction to each dock, and the distance.
  Only docks within effective docking range are presented
  If the user takes the laptop and walks away, the docking disconnects
Expected:
  Horizontal + vertical accuracy: <30 cm@90%
  Pointing angles (AZ, EL & Roll) accuracy: <20deg
  Latency: <100ms
  Refresh Rate: 1-10Hz
  Mobility – up to 1meter/sec
  Number of simultaneous users – up to 12 users to 7 docking stations.

## Slide 8: 6. Wearable devices
User: User during sport activity
Environment: Wearable sensors on the person, connected to the mobile phone
Use case:
  Monitor movement-trajectory with location-tagging to avoid injury and improve performance
  Monitor additional physical data such as heart-rate and electrical activity
  Power consumption profile: foreground for positioning determination
  Operating mode: AP2STA
  Usage duration: 1-24 hour, low duty cycle activity
  Up to 8 attached devices
Expected:
  Horizontal + vertical accuracy: <1 cm@90%
  Pointing angles (AZ, EL & Roll) accuracy: <5deg
  Latency: <10ms: sensory data is required to be tagged with the exact location
  Refresh Rate: 0.5Hz-100Hz
Note:
  Configuration of usage duration, refresh rate and battery are application specific and linked

## Slide 9: 7. Control consoles
User: User controls TV, or a gaming console by using his phone, using location instead of gestures
Environment: Living room
Use case:
  Using the mobile phone to control the TV menus, w/o using its screen
  Using the mobile phone as control for gaming
  Exact location of the phone is used for game control
  Operating mode: AP2STA
    Optional operating mode: STA2STA
Expected:
  Horizontal + vertical accuracy: <1 cm@90%
  Pointing angles (AZ, EL & Roll) accuracy: <2deg
  Latency: <100ms:
  Refresh Rate: 10Hz-100Hz