## Slide 1: Long Range versus Low Power and Coexistence
Date: 2016-01-18
Authors:
Slide 1

## Slide 2: Abstract
This presentation analyses the use cases presented in LRLP TIG
  It observes that majority of the use cases require low power but not long range
It discusses the legacy coexistence while keeping the Tx-power of the LRLP devices in mind
  It observes that for LRLP devices with low transmit power, the legacy coexistence can be achieved to some level by using the legacy preamble in DL and UL trigger.
  However for the direct-link extended range scenarios as well as for Peer-to-Peer (P2P) scenarios, there is no benefit in using the legacy preamble.
  Eventually, this presentation calls for finding coexistence solutions beyond AP’s legacy preamble protection
  It also proposes to address the long-range in LRLP as a by-product of the range optimization within the asymmetric link of the BSS stemming from the low-power nature of the typical STA side
Slide 2

## Slide 3: Use Cases across Range and Power Consumption
Distance (meters)
A summary from contributions [1-6] confirms
  majority of use cases require Low Power, but NOT Long Range
Slide 3
Longer
Shorter
Lower
Higher
Range
Power Consumption
Smart Buildings
Home (entertainment)
Assisted Living
Industrial Automation
Building Energy Management
Agriculture
Industrial Worker
Security/Public Safety
Transportation
Healthcare
Home (control/security)
> 5 years
Battery Life
> 2 years
Plug in
Home (entertainment)
Industrial Automation
> 500
< 10
Long Range Low Power
Low Power
Regular 802.11

## Slide 4: Coexistence by Using the Legacy Preamble
Slide 4
Longer
Shorter
Range
> 500
Distance (meters)
> 500
< 10
It was proposed in [7] to
    Use legacy preambles to protect DL LRLP transmissions
    Use legacy preambles and triggering UL from LRLP STAs to protect UL LRLP transmissions
  However, the contribution 11-16/0026 [9] discusses in details that the above proposal cannot solve all the coexistence issues
The link budget analysis in [8] showed a 100 byte packet with transmit power of 20dBm has a range of 135 meters assuming
Indoor Channel Model D
NF and other losses: 7 dB
A range longer than the legacy preamble coverage cannot be protected (without any relay) by using the legacy preamble or a trigger frame
an approximate limit for legacy coexistence without any relay

## Slide 5: Coexistence Problem for P2P Scenarios
Previous slide discussed the possibility of AP’s high-power protection to STA’s low-power transmissions
But LRLP devices may be used on P2P links as well, where no such legacy preamble is available perhaps
  Multi-hop networks should also be considered under this umbrella
This implies that coexistence with legacy devices has to rely on other techniques besides the legacy preamble protection
  These techniques may include simple approaches (for example considering lower amount of activity or duty cycling), but most likely more sophisticated methods are required.

## Slide 6: Asymmetric Link: Devices with Low Tx-Power
Slide 6
It is envisaged that the low power narrowband LRLP devices will transmit at much lower power than AP, as small as 0dBm
AP affords to transmit at greater Tx-power than Tx-power of IoT devices. In addition, it has more number of antennas with higher gains, which in outdoor scenarios are installed at roof tops that can provide line of sight
  Asymmetry in transmit power
    DL has 10 dB or more higher transmit power than UL
Inclusion of the legacy preamble in DL and restricting UL Tx to trigger based transmissions can provide some level of coexistence/protection, but only
  within the coverage of the AP legacy preamble with the assumption that the Low Power narrowband (e.g., 2MHz) Low Power devices can close the link

## Slide 7: LRLP-based Extended Range WiFi
If range is optimized for LRLP-based transmissions of low-power devices (~0dBm), it is immediately applicable to high-power devices achieving extended range with LRLP-based PHY
  The extended range is a by-product of the range optimization of the low-power devices
  If the market is there, the usage will follow
  Coexistence?
    Extended-range use cases are rare
    The solution for P2P (when found) may be suitable here as well
Moreover, LRLP standard could present itself now as being capable both of low-power (battery ready) and long-range (by-product of the range optimization of the low-power devices)

## Slide 8: Conclusion
Slide 8
Observed that majority of LRLP use cases are Low Power and not Long Range
  The first priority of the technical development of LRLP should be on low-power
Coexistence problems exist for P2P communications as well as Long Range
  New techniques should be sought in addition to usage of legacy preamble protection from the AP
The extended range may be supported by a by-product of the range optimization of low-power devices
  Long Range devices are inevitable, but LRLP development does not have to put its resources into them
  They would become available as a by-product of the range optimization of the asymmetric link (AP-STA)
  P2P coexistence solutions may suit Long-Range coexistence problems as well

## Slide 9: Straw Poll #1
Do you support that the first priority of the technical development of LRLP should be on enabling a low-power capability?
Yes (low power is the priority) (18)
No (long range has equal or higher priority than low power) (25)
Abstain (no opinion or too soon to decide) (52)

## Slide 10: References
[1] IEEE 802.11-15/0775r1, WNG SC - Integrated Long Range Low Power Operation for IoT
[2] IEEE 802.11-15/1112r1, LRLP TIG - Use Case of LRLP Operation for IoT
[3] IEEE 802.11-15/1306r0, LRLP TIG - Use Case for LRLP and Full Function in STA
[4] IEEE 802.11-15/1365r0, LRLP TIG - Use Cases of LRLP Operation for IoT
[5] IEEE 802.11-15/1380r0, LRLP TIG - Digital Health Use Case
[6] IEEE 802.11-15/1383r0, LRLP TIG - Use Cases for Indoor & Outdoor
[7] IEEE 802.11-15/1108r0, LRLP TIG - Technical Feasibility for LRLP
[8] IEEE 802.11-15/1308r0, LRLP TIG - Link Budget Analysis
[9] IEEE 802.11-16/0026, LRLP TIG - Coexistence Problem
Slide 10