## Slide 1: Coexistence Problem
Date: 2016-01-18
Authors:

## Slide 2: Abstract
In this presentation, we show that there is a coexistence problem between legacy 802.11 stations and LRLP stations when the LRLP stations are only capable of transmitting and receiving narrow bandwidth signals (e.g. 2 MHz).

## Slide 3: Current LRLP Requirements for Backward Compatibility and Range
In [1], LRLP requirements are described as follows:
“LRLP requirements
  Integration and backward compatibility with legacy 802.11 [2]
    LRLP AP has both HE/legacy and LRLP capability to ensure WLAN coexistence
      The 2.4 GHz band is the primary objective, although other bands are not ruled out. LRLP is band agnostic.
    Mechanisms for Sub20MHz operation
    LRLP STA not required to support legacy 20MHz Tx or Rx [2]
      I.e. No detection or transmission of legacy preambles required for LRLP STA [3]
    LRLP AP will be required to support legacy 20MHz Tx & Rx
      Perform CCA and legacy network access
      Protect DL LRLP transmissions using legacy preambles
  Protect UL LRLP transmissions using legacy preambles and triggering UL from LRLP STAs [3]
  Long Range (approx. 10dB improvement above existing 20 MHz operation)
    Improved coverage edge performance
    …”

## Slide 4: Example 1a
LRLP STA
(2MHz)
LRLP AP
(20MHz
and 2MHz)
Legacy AP
(20MHz)
Legacy STA
(20MHz)
LRLP link
Legacy
link
RTS
CTS
Data
Legacy STA
Legacy AP
Data
LRLP AP
LRLP STA
Trigger frame
Collision
Ack
20MHz Tx range
2MHz Tx range
LRLP STA cannot decode 20MHz CTS and thus cannot set NAV
2 MHz
20 MHz
Victim STA

## Slide 5: Example 1b
LRLP STA
(2MHz)
LRLP AP
(20MHz
and 2MHz)
Legacy AP
(20MHz)
Legacy STA
(20MHz)
LRLP link
Legacy
link
RTS
CTS
Data
Legacy STA
Legacy AP
LRLP AP
LRLP STA
Trigger frame
DL data
20MHz Tx range
2MHz Tx range
LRLP STA cannot decode 20MHz CTS and thus cannot set NAV
2 MHz
20 MHz
Victim STA
Collision

## Slide 6: Example 2a
LRLP STA
(2MHz)
LRLP AP
(20MHz
and 2MHz)
Legacy AP
(20MHz)
Legacy STA
(20MHz)
LRLP link
Legacy
link
CTS
Legacy STA
Legacy AP
Data
LRLP AP
LRLP STA
Trigger frame
Cannot decode duration of 2 MHz PPDU; relies on energy detection (-62dBm)
Ack
20MHz Tx range
2MHz Tx range
2 MHz
RTS
Collision
Victim STA

## Slide 7: Example 2b
LRLP STA
(2MHz)
LRLP AP
(20MHz
and 2MHz)
Legacy AP
(20MHz)
Legacy STA
(20MHz)
LRLP link
Legacy
link
Legacy STA
Legacy AP
UL data
LRLP AP
LRLP STA
Trigger frame
Cannot decode duration of 2 MHz PPDU; relies on energy detection (-62dBm)
DL data
20MHz Tx range
2MHz Tx range
Collision
Data
Victim STA
2 MHz
20 MHz

## Slide 8: Observations: Example 1a/1b and 2a/2b
Example 1a/1b: LRLP STA cannot decode 20MHz PPDU
  Example 1a:
    The legacy STA cannot receive packet transmitted by the LRLP AP (out-of-range)
    The 2 MHz only LRLP STA cannot decode the CTS frame transmitted from the legacy STA and thus cannot defer correctly causing collision between the data frames transmitted by the LRLP STA and the legacy AP at the legacy STA
  Example 1b:
    The data packets transmitted by the LRLP AP and the legacy AP collide at the LRLP STA
Example 2a/2b: Legacy STA cannot decode 2 MHz PPDU
  Example 2a:
    The legacy STA cannot receive packet transmitted by the LRLP AP (out-of-range)
    The legacy STA cannot decode the 2 MHz PPDU transmitted by the LRLP STA and thus the legacy STA cannot defer correctly
    The legacy AP’s transmission collides with the 2 MHz PPDU transmission by the LRLP STA at the legacy STA
  Example 2b:
    The data packets transmitted by the LRLP AP and the legacy STA collide at the LRLP STA

## Slide 9: Example 3
LRLP AP
(20MHz
and 2MHz)
Legacy
link
20MHz Tx range
LRLP
STA
(2MHz)
Legacy
STA
(20MHz)
Legacy
AP
(20MHz)
LRLP
link
RTS
CTS
Data
Legacy STA
Legacy AP
LRLP AP
LRLP STA
20 MHz
Receives CTS and defers transmission
Ack
Trigger frame
Data
Ack
Defer (NAV set)
Defer
  The legacy STA and the LRLP STA are within the transmission range of the LRLP AP
  The legacy STA can defer correctly based on the information from the LRLP AP

## Slide 10: Conclusions
The extended range operation based on sub-20MHz signaling makes the coexistence problem between a LRLP STA and a legacy STA worse
  Legacy STA cannot decode a sub-20MHz signal
  LRLP STA cannot decode a 20 MHz signal
A LRLP STA and a legacy STA (i.e. interfering STA) needs to be within the 20 MHz transmission range of an LRLP AP to coexist with each other
802.11ah supports the long range operation without the coexistence problem
  No coexistence problem with legacy 2.4/5GHz band STAs
  Sub 1 GHz operation: better signal propagation characteristic
  Supports up to 1km range: mandatory 1MHz signal support with 2x repetition

## Slide 11: References
[1] IEEE 802.11-15/1446r3, “Long Range Low Power (LRLP) Operation in 802.11: Use Cases and Functional Requirements: Guidelines for PAR Development”