## Slide 1: TXOP Truncation Enhancement
Date: 2016-01-18
Authors:

## Slide 2
Abstract
In this contribution, we explore using duration settings in CF-End frames to enhance TXOP Truncation Procedures.

## Slide 3: Introduction
The 802.11ax SFD states [1]:
  “An HE STA should have a mechanism to remember and distinguish NAVs set by intra-BSS frame and OBSS frame. A CF-end frame that comes from intra-BSS should not reset NAV that was set by a frame from OBSS. To determine which BSS is the origin of a frame, the HE STA may use BSS color.”
No detailed procedure on what a STA should do to Inter-BSS NAV if an inter-BSS CF-End frame is received
There are many Overlapping BSSs, particularly in dense deployment scenarios
  Real-life measurement shows that there may be >100 APs per channel in stadium settings [2]
CF-End frame sent by OBSS X (TXOP Truncation) should not reset Inter-BSS NAV set by frames sent by OBSS Y

## Slide 4: Inter-BSS NAV Reset
To further complicate the issue, the SFD states [1]:
  “A STA maintains two NAVs
    One is the NAV for Intra-BSS frame, and second one is the NAV for Inter-BSS frame or frame that cannot be determined to be Intra-BSS or Inter-BSS”
NAV set by non-HT/HT/VHT CTS frames sent to a non-AP STA may be determined to be Inter-BSS NAV as well
It is important to reset the correct NAV, i.e., the Inter-BSS or Intra-BSS NAV

## Slide 5: Inter-BSS NAV Reset
Two approaches may be used to remember and to correctly reset the Inter-BSS NAV:
  Approach 1:
  Remember the BSSID/Color of each frame setting the Inter-BSS NAV;
  Reset the Inter-BSS NAV when a CF-End frame is received carrying the same BSSID/Color as the frame that set the Inter-BSS NAV
  Approach 2 (A similar approach is allowed in 802.11ah):
  Use Duration field settings in CF-End frames
  Inter-BSS NAVs may be reset if the Duration carried in a CF-End frame matches that of the Inter-BSS NAV counter, with adjustment for clock drift, etc.

## Slide 6: Comparison of the Two Approaches
  Approach 1:
  Can correctly reset Inter-BSS NAVs when the BSSID/Color of the frames setting the Inter-BSS NAVs can be determined
  May not be able to correctly reset Inter-BSS NAVs set by non-HT/HT/VHT CTS sent to non-AP STAs
  Approach 2:
  Can correctly reset Inter-BSS NAVs when the Duration carried in a CF-End frame matches the NAV timer
  May facilitate the resetting of Intra-BSS NAVs as well
  May need to adjust for clock drift, propagation delays, etc.
  Does not need to remember BSSID/Color of each frames setting the Inter-BSS NAV

## Slide 7: Inter-BSS NAV Reset
  Current 802.11 RevMC 5.0 states:
  “When transmitted by a non-DMG STA, the Duration field is set to 0.”
  Approach 2 can provide enhancement to 802.11ax TXOP Truncation procedures by utilizing the Duration field in CF-End frames that is currently not used

## Slide 8: Conclusion
Correctly resetting the Inter-BSS NAVs may be difficult
Using of the (currently reserved) Duration field settings in CF-End frames may facilitate resetting of Inter-BSS NAVs and therefore enhance the TXOP Truncation Procedures

## Slide 9
References
11-15/0132r13, Specification Framework for Tgax
11-15/1336r1, BSS Color Field Size Measurements

## Slide 10: Straw Poll
Do you agree to add the following to the SFD:
6.1 The spec should consider to use Duration settings in CF-End frames to facilitate resetting of NAVs