## Slide 1: UL MU Carrier Sensing (CS) Rules
Date: 2016-01-16
Authors:
Name | Affiliation | Address | Phone | Email
Yakun Sun | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2
Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Jinmin Kim |  |  |  | Jinmin1230.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn

## Slide 3
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Alice Chen |  |  |  | 
Lin Yang |  |  |  | 
Authors (continued)

## Slide 4
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com

## Slide 5
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Authors (continued)

## Slide 6
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 7
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Authors (continued)

## Slide 8: Background (1)
Typical 11ax UL MU frame exchange sequences: Basic and Cascading
TXOP
UL MU PPDU
Trigger
AP Gains the channel access
DL
UL
DL
ACK
/BA
Basic: Trigger ++ UL MU data ++ DL ACK/BA
UL MU PPDU
Trigger + DL MU Data
TXOP
AP Gains the channel access
DL
UL
DL
ACK
/BA
Cascading: (Trigger + DL MU data) ++ UL MU data ++ DL ACK/BA

## Slide 9: Background (2)
Based on the 11ax contribution [1], the text below has been accepted into the current revision of 11ax SFD [2]:
  A STA shall consider CCA status to respond to a Trigger frame under a non-null TBD set of conditions.
The above 11ax SFD text indicates two possible scenarios:
  Scenario-1: Under a non-null TBD set of conditions, a STA can transmit UL MU PPDU in response to a trigger frame, without considering CS, i.e., without carrier sensing;
  Scenario-2: Otherwise, a STA shall consider CS, i.e., with carrier sensing, before transmitting UL MU PPDU in response to a trigger frame
Then some open questions for the scenario that carrier sensing is required before UL MU transmission in responses to a trigger frame, e.g.,
  When to sense the channel?
  Which channel to sense?
  This contribution addresses the above questions.

## Slide 10: When To Sense the Channel?
When to sense the channel if CS is required before UL MU transmission in responses to a trigger frame?
  Two places as shown in the diagram below:
    before trigger frame:
      Similar to the 11ac procedure required for RTS operation with dynamic BW;
      but not applicable to cascading OFDMA transmission.
    after trigger frame:
      applicable to cascading OFDMA transmission.
      But IFS requirement needs to be addressed.
Recommend to conduct Carrier Sense (CS) after trigger frame, as a unified solution.
UL MU PPDU
Trigger
TXOP
AP Gains the channel access
DL
UL
DL
ACK
/BA
UL MU PPDU
Trigger + DL MU Data
TXOP
AP Gains the channel access
DL
UL
DL
ACK
/BA
CS Detection
CS Detection

## Slide 11: Which channel to sense? (1)
First, what’s the baseline carrier sense (CS) when channel bandwidth is greater than 20MHz?
  Virtual CS (NAV): based on Primary Channel;
  Physical CS (CCA detection):
    The PHY entity reports to the MAC entity whether the wireless medium is busy through the following channel list:
      primary 20MHz, secondary 20MHz, secondary 40MHz, secondary 80MHz.
    The MAC entity doesn’t know the busy/idle state of each 20MHz channel.

## Slide 12: Which channel to sense? (2)
What about 11ax channel sensing, particularly with OFDMA?
  For simplicity, the minimum channel size for carrier sense is 20MHz; e.g., STA1 needs to sense Ch1, even its UL OFDAM allocation is only part of Ch1;
  A STA really cares the channel status of its allocated subchannel, i.e., a 20MHz channel or multiple of adjacent 20MHz channels where its UL OFDAM allocation is located;
  STA0 and STA1 care the status of Ch1;
    a single 20MHz channel, i.e., the Secondary20
  STA2 cares the status of Ch2+Ch3;
    a combination of two adjacent 20MHz channel, i.e., primary20 + party of Secondary40
    sensing either per 20MHz or one 40MHz
  STA3 cares the status of Ch4
    a single 20MHz channel, part of the Secondary40
AP
STA1
STA2
STA0
STA3
Primary 20MHz
STA2 A-MPDU to AP
TXOP
Backoff or
PIFS
DL
UL
STA3 A-MPDU to AP
STA0 A-MPDU to AP
STA1 A-MPDU to AP
DL
Trigger
Trigger
Trigger
Trigger
M-BA
M-BA
M-BA
M-BA
Ch1
Ch2
Ch3
Ch4
Secondary 20MHz
Secondary 40MHz

## Slide 13: Which channel to sense? (3)
The baseline channel sensing does not service 11ax UL MU transmission well, e.g.,
  STA3 needs to sense Primary20, Secondary20, and Secondary40, (Ch3+Ch4), but it actually only cares Ch4;
  STA2 does not care Ch1, but the baseline channel sensing requires it to sense Ch1, due to the order of channel list;
  Every STA needs to sense the primary channel (Ch2), while only STA2 actually cares Ch2.
AP
STA1
STA2
STA0
STA3
Primary 20MHz
STA2 A-MPDU to AP
TXOP
Backoff or
PIFS
DL
UL
STA3 A-MPDU to AP
STA0 A-MPDU to AP
STA1 A-MPDU to AP
DL
Trigger
Trigger
Trigger
Trigger
M-BA
M-BA
M-BA
M-BA
Ch1
Ch2
Ch3
Ch4
Secondary 20MHz
Secondary 40MHz

## Slide 14: Which channel to sense? (4)
Discussions about 11ax STA Channel Sensing for UL MU transmissions:
  Does every STA still need to sense primary channel? NO
    Only the STA(s) have its/their UL allocation in the Primary channel needs to sense it
  Can an 11ax STA only sense the subchannel that contains its UL allocation before the UL MU transmission in response to a Trigger Frame?  Yes
    Notes: The sensed subchannel is either a single 20MHz channel or multiple of 20MHz channels
Recommendation:
  An 11ax STA only conducts physical channel sensing on the subchannel that contains its UL allocation before the UL MU transmission in response to a Trigger Frame.

## Slide 15: Straw Poll #1
Do you support that , when a STA is required to sense the medium before its UL MU transmission in response to a trigger frame, it senses the medium using ED after receiving the PPDU that contains the trigger frame (i.e. during the SIFS time)?
  Yes
  No
  Abstain

## Slide 16: Straw Poll #2
Do you support that , when a STA needs to perform the physical carrier sensing (ED) before its UL MU transmission in response to a trigger frame, it shall perform the physical carrier sensing (ED) at least in the subchannel that contains the STA’s UL allocation, where the sensed subchannel consists of either a single 20MHz channel or multiple of 20MHz channels?
  Yes
  No
  Abstain

## Slide 17: References
11-15-1058-00-00ax-cca-consideration-for-ul-mu-transmission
11-15-0132-13-00ax-spec-framework
IEEE P802.11-REVmc/D4.2, Sept 2015

## Slide 18: Motion #1
Move to add the following text into Section 4.3 of the SFD:
When a STA is required to sense the medium before its UL MU transmission in response to a trigger frame, it senses the medium using ED after receiving the PPDU that contains the trigger frame (i.e. during the SIFS time).
  Yes
  No
  Abstain

## Slide 19: Motion #2
Move to add the following text into Section 4.3 of the SFD:
When a STA needs to perform the physical carrier sensing (ED) before its UL MU transmission in response to a trigger frame, it shall perform the physical carrier sensing (ED) at least in the subchannel that contains the STA’s UL allocation, where the sensed subchannel consists of either a single 20MHz channel or multiple of 20MHz channels.
  Yes
  No
  Abstain