## Slide 1: Sequence for 1x LTF
Date: 2016-01-18
Authors:

## Slide 2: Summary of 2x/4x LTF Sequence PAPR
 | Max PAPR | 
 | 2x LTF | 4x LTF
160 MHz* [2x996 RU] | 8.21 dB | 8.76 dB
80 MHz [996 RU] | 6.08 dB | 6.29 dB
40 MHz [484 RU] | 5.84 dB | 5.47 dB
20 MHz [242 RU] | 5.24 dB | 5.36 dB
*Sequence for 160MHz was generated by concatenating two 80MHz sequences.

## Slide 3: 1x LTF Sequence
Current SFD [1]
A 1x LTF as an optional mode in 11ax for SU PPDUs (TBD for MU-MIMO). The 1x LTF + 0.8 µs GI is one optional combination as indicated by the “GI and LTF size” sub-field in HE-SIG-A.
[PHY Motion 85, November 2015, see [8]]
Design Goals
20MHz: 242 tones + 3 DCs, length 62 (including DC)
40MHz: 484 tones + 5 DCs, length 123 (including DC)
80MHz: 996 tones + 5 DCs, length 251 (including DC)
Simple computer search looking for sequences with good PAPR properties.

## Slide 4: Proposed 1x LTF Sequence 80 MHz
HE-LTF996(-500:4:500) =
{-1, -1, +1, +1, +1, -1, -1, -1, +1, -1, +1, -1, -1, +1, +1, +1, +1, +1, -1, -1, -1, +1, -1, -1, +1, +1, +1, +1, -1, -1, +1, -1, -1, +1, -1, +1, -1, -1, -1, -1, +1, -1, +1, +1, -1, +1, -1, +1, +1, -1, +1, -1, +1, -1, -1, -1, +1, -1, -1, -1, -1, -1, +1, +1, -1, +1, -1, +1, +1, +1, +1, +1, -1, +1, +1, -1, -1, +1, +1, -1, +1, -1, -1, -1, -1, -1, +1, +1, +1, -1, -1, -1, +1, +1, +1, -1, +1, +1, +1, +1, +1, -1, +1, -1, +1, -1, -1, +1, +1, -1, -1, +1, +1, +1, +1, +1, +1, -1, -1, -1, +1, -1, -1, -1, +1, +0, -1, -1, +1, +1, -1, +1, +1, +1, -1, -1, -1, -1, -1, -1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, -1, -1, -1, -1, -1, +1, -1, -1, -1, +1, +1, +1, -1, -1, -1, +1, +1, +1, +1, +1, -1, +1, -1, -1, +1, +1, -1, -1, +1, -1, -1, -1, -1, -1, +1, -1, +1, -1, -1, +1, -1, -1, -1, -1, +1, -1, -1, -1, +1, -1, +1, -1, +1, +1, -1, +1, -1, +1, +1, -1, +1, -1, -1, -1, -1, +1, -1, +1, -1, -1, +1, -1, -1, +1, +1, +1, +1, -1, -1, +1, -1, -1, -1, +1, +1, +1, +1, +1, -1, -1, +1, -1, +1, -1, -1, -1, +1, +1, +1, -1, -1}

## Slide 5: Proposed 1x LTF Sequence 40 MHz
HE-LTF484(-244:4:244) =
{-1, +1, -1, -1, -1, +1, -1, +1, -1, +1, -1, +1, +1, -1, -1, -1, +1, -1, -1, +1, -1, +1, +1, -1, -1, +1, +1, -1, +1, -1, +1, -1, -1, -1, -1, -1, -1, -1, +1, -1, -1, +1, +1, +1, -1, -1, +1, +1, -1, +1, +1, +1, +1, -1, +1, +1, +1, -1, -1, -1, -1, +0, -1, -1, -1, +1, -1, -1, -1, -1, +1, -1, -1, -1, +1, +1, -1, +1, -1, -1, +1, -1, +1, -1, -1, +1, +1, -1, +1, +1, -1, -1, -1, -1, -1, +1, -1, +1, -1, +1, -1, +1, +1, +1, +1, +1, +1, -1, -1, -1, -1, +1, +1, +1, +1, -1, -1, +1, +1, -1, -1, +1, +1}

## Slide 6: Proposed 1x LTF Sequence 20 MHz
HE-LTF242(-122:4:122) =
{+1, -1, +1, +1, +1, -1, -1, +1, -1, +1, -1, -1, -1, -1, -1, +1, +1, +1, +1, -1, -1, +1, -1, -1, +1, -1, -1, -1, -1, -1, +0, -1, -1, -1, +1, -1, +1, -1, -1, -1, +1, +1, +1, -1, +1, +1, -1, +1, +1, -1, -1, -1, +1, -1, -1, -1, +1, +1, +1, -1, -1}

## Slide 7: PAPR Results
 | Max PAPR |  | 
 | 1x LTF (Computer Search) | 2x LTF | 4x LTF
160 MHz* [2x996 RU] | 7.53 dB | 8.21 dB | 8.76 dB
80 MHz [996 RU] | 4.82 dB | 6.08 dB | 6.29 dB
40 MHz [484 RU] | 4.96 dB | 5.84 dB | 5.47 dB
20 MHz [242 RU] | 4.30 dB | 5.24 dB | 5.36 dB
*Sequence for 160MHz was generated by concatenating two 80MHz sequences.

## Slide 8: References
[1] 11-15-0132-13-00ax-spec-framework