## Slide 1: RU Allocation in SIG-B
Date: 2016-01-17
Authors:

## Slide 2: Recap: RU Allocation Indication Table [1]
8 bits indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Num of entries
000 0 0000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 0001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 0010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 0011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 0100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 0101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 0110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 0111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
000 0 1000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 1001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 1010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 1011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 1100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 1101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 1110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 1111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
8 bits indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Num of entries
000 1 xxxx | Definition TBD |  |  |  |  |  |  |  |  | 16
00100 yyy | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 8
00101 yyy | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 8
00110 yyy | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 8
00111 yyy | 52 |  | 52 |  | 26 | 106 |  |  |  | 8
01000 yyy | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 8
01001 yyy | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 8
01010 yyy | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 8
01011 yyy | 106 |  |  |  | 26 | 52 |  | 52 |  | 8
011 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
10 yyy yyy | 106 |  |  |  | 26 | 106 |  |  |  | 64
11 0 00yyy | 242 |  |  |  |  |  |  |  |  | 8
11 0 01yyy | 484 |  |  |  |  |  |  |  |  | 8
11 0 10yyy | 996 |  |  |  |  |  |  |  |  | 8
11 0 11yyy | 2*996 |  |  |  |  |  |  |  |  | 8
11 1 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32

## Slide 3: Dynamic Split of MU-MIMO STA specific information
Agreement
“For MU-MIMO allocation of RU size > 20 MHz, the user-specific subfields is dynamically split between two HE-SIG-B content channels (1/2) and the split is decided by the AP (on a per case basis).”
[PHY Motion 41]
The support of dynamic split of STA specific information between HE-SIG-B channel 1 and 2 enables load balancing of STA specific information.

## Slide 4: Discussion on Dynamic Split
Dynamic split for 2*996 RU
  Not needed.
  Full bandwidth MU-MIMO, which can be supported by ‘SIG-B Compression Mode’
    Equal split of STA specific information is optimal load balancing, which is supported by ‘SIG-B Compression Mode’
Dynamic split for 484/996 RU
  8 user MU: {1/7, 2/6, 3/5} {4/4} {5/3, 6/2, 7/1}
  7 user MU: {1/6, 2/5, 3/4} {4/3, 5/2, 6/1}
  6 user MU: {1/5, 2/4} {3/3} {4/2, 5/1}
  5 user MU: {1/4, 2/3} {3/2, 4/1}
  4 user MU: {1/3} {2/2} {3/1}
  3 user MU: {1/2} {2/1}
  2 user MU: {1/1}
12 + 4 + 12
= 28 States

## Slide 5: An Example of Large Asymmetry Split
SIG-B
Duplication of SIG-B in Channel 1
Duplication of SIG-B in Channel 2
80 MHz
242 RU
484RU - MU
484RU - MU
484RU - MU
484RU - MU
484RU - MU
484RU - MU
484RU - MU
484RU - MU
Freq.
52RU
52RU
26RU
26RU
26RU
26RU
26RU
STA-Specific Info.
Common - A | Common - B
Common - C | Common – D
26 RU | 242 RU
26 RU | 484 RU (MU - 2)
26 RU | 484 RU (MU - 3)
26 RU | 484 RU (MU - 4)
26 RU | 484 RU (MU - 5)
52 RU | 484 RU (MU - 6)
52 RU | 484 RU (MU - 7)
484 RU (MU - 1) | 484 RU (MU - 8)
Band
C/D
Band
A
Band B
Band C/D
Common Info.
Band A
Band B
Band C
Band D
RU Allocation

## Slide 6: Signaling Aspect of Dynamic Split
Fully flexible dynamic split of user specific information requires 56 states (28 each for 484 and 996 RU).
Given that there are total of 80 TBD states available, we should be able to work out some mapping.

## Slide 7: Zero User Specific Information Indication
8 bit RU allocation subfield will run into cases where no explicit assignment is needed.
  An example is shown below.
No assignment (i.e. zero user) will require 1 state from the RU allocation subfield.
484RU (STA3)
484RU (STA2)
Common (A)
A
B
Common
(B)
C
D
Common (C)
Common
(D)
80MHz
STA-specific
(STA1)
STA-specific
(STA2)
STA-specific
(STA3)
STA-specific
(STA4)
Duplication of SIG-B in Channel 1
Duplication of SIG-B in Channel 2
Padding
Padding
484RU (STA1)
…
…
Spatially multiplexed (MU-MIMO)
484RU (STA4)
No assignment
…
…
SIG-B
Data

## Slide 8: Strawpoll #1
Do you agree with not to support dynamic split (not precluding equal split) of MU-MIMO STA specific information for 2x996 RU (i.e. 160MHz MU-MIMO).
Y/N/A

## Slide 9: Strawpoll #2
Do you agree with support equal split and no split (all STA information in one SIG-B channel) of MU-MIMO STA specific information for 2x996 RU (i.e. 160MHz MU-MIMO).
Y/N/A

## Slide 10: Strawpoll #3
Do you agree to include the following text to SFD?
At least 1 state is reserved in the 8 bit RU allocation subfield of the HE-SIG-B common field for ‘no STA-specific information field assigned by the RU allocation subfield’.
  Details TBD
Y/N/A

## Slide 11: Reference
[1] IEEE802.11-15/0132r13, “Specification Framework for TGax”