## Slide 1: BSS Color Settings for a Multiple BSSID Set
Date: 2016-01-18
Authors:

## Slide 2: Introduction
According to SFD [1],
  HE PPDU includes BSS color subfield in HE-SIG-A.
    Spatial reuse and Power save operations are based on the BSS color of the received PPDU.
  HE STAs shall support the multiple BSSID set.
    A single physical AP can establish multiple virtual BSSs managed by a multiple BSSID set.
TGax needs to define a BSS color assignment method for BSSs in the same multiple BSSID set.
  Case 1: Assigning different BSS colors to BSSs (in the same multiple BSSID set)
  Case 2: Assigning the same BSS color to BSSs (in the same multiple BSSID set)
In this contribution, we propose
  To use a same BSS color value for BSSs of a multiple BSSID set
  To consider a frame of BSS in the same multiple BSSID set as an intra-BSS frame

## Slide 3: Multiple BSSID Set [2]
With Multiple BSSID, profiles of multiple BSSs are transmitted with a single Beacon or Probe Response frame.
  Non-AP STA can obtain information for multiple BSSs by interpreting Multiple BSSID element which is included in a Beacon or Probe Response frame.
  This reduces excessive airtime consumption for management frames.
Single physical AP can operate as multiple virtual APs.
VAP 1
VAP 2
VAP 3
Co-located
STA
STA
STA
STA

## Slide 4: Spatial Reuse Operation
STA uses BSS color (or MAC address) to determine the detected frame is an inter- or an intra-BSS frame.
  Then if the frame is an inter-BSS frame (under TBD conditions), STA uses OBSS PD level for CCA.
  In case that OBSS PD level is used incorrectly, collision may happen.
Case 1:
STAs in a multiple BSSID set will interfere each other by trying spatial reuse transmissions, which are not desirable.
Case 2:
STAs in a multiple BSSID set will correctly preserve PPDUs in the same multiple BSSID set.
PPDU of BSSID(1)
AP or non-AP STA
of BSSID(1)
Case 1: Different BSS color
(Unknown to members
in a multiple BSSID set)
STA of
BSSID(2)
STA of
BSSID(2)
Case 2: Same BSS color
Busy
Idle
STA may transmit PPDU
Packet detection
RSSI < OBSS PD
Suspend countdown.
RSSI > minimum receive sensitivity level
End of determination whether PPDU is an intra- or inter-BSS frame.
Busy
Idle

## Slide 5: Power Save Operation
STA checks BSS color of the detected frame to enter the Doze state.
  Then if STA determines that it is not able to transmit/receive another frame during the detected frame, STA may enter the Doze state.
Case 1:
STAs in a multiple BSSID set cannot enter Doze state even though they receive PPDUs from other BSSs in the same set.
Case 2:
STAs in a multiple BSSID set may enter Doze state even when they receive PPDUs from other BSSs in the same set.
DL PPDU
of BSSID(1)
AP
Case 1: Different BSS color
(Unknown to members in a multiple BSSID set)
DL PPDU
of BSSID(1)
STA of
BSSID(2)
Case 2: Same BSS color
Awake
Doze
(SU or UL MU)
PPDU of BSSID(1)
STA of
BSSID(1)
STA of
BSSID(2)
Awake
Doze

## Slide 6: BSS Color in Multiple BSSID Set
If different BSS colors are assigned:
  (Pros) STAs can distinguish PPDUs from different BSSs in the same BSSID set
    Early decision to stop further decoding
  (Cons) Problems arise during spatial reuse and power save operations
    Therefore, all members of a multiple BSSID set should know all BSS colors of the BSSs.
  (Cons) Due to the lack of BSS color values, the probability of BSS color collision increases in dense environment
If the same BSS color is assigned:
  (Pros) No problems arise during spatial reuse and power save operations
  (Cons) STAs cannot distinguish PPDUs from different BSSs by using BSS color in the same BSSID set
We propose to assign the same BSS color for BSSs in the multiple BSSID set.
  To use the same operation for channel access and power save defined in 11ax
  To avoid BSS color collision between different BSSID sets in dense environments
  To extend the same operation in 11ah to 11ax, “AP shall set BSS color for a multiple BSSID set to a same value” [2].

## Slide 7: Intra-BSS Frame in Multiple BSSID Set
When PPDU is sent in legacy packet format using multiple BSSID set,
  If 11ax STA detects the frame of the same multiple BSSID set without BSS color,
    1. Receiver determines whether the frame is an inter-/intra-BSS frame by using “MAC address”.
    2. Since MAC addresses of VAPs are different, receiver can consider the frame as an “inter-BSS” frame.
    3. Using OBSS PD level may cause interference to the frame from the same multiple BSSID set.
Need to consider the frame of the same multiple BSSID set as an “intra-BSS” frame
AP 0 (MAC addr.: REF_BSSID)
AP 1 (MAC addr.: BSSID(1))
Co-located
Legacy STA
(associated with AP 0)
HE STA
(associated with AP 1)
Legacy
PPDU

## Slide 8: Conclusions
TGax shall set BSS color for a multiple BSSID set to a same value
  To use the same operation for channel access and power save defined in 11ax
  To avoid BSS color collision between different BSSID sets in dense environments
TGax shall consider a frame of BSS in the same multiple BSSID set as an intra-BSS frame
  To avoid the packet collision/interference to the frame for the same AP operating with a multiple BSSID set

## Slide 9: References
[1] 11-15/0132r13 Specification Framework for TGax
[2] Draft P802.11REVmc D5.0
[3] Draft P802.11ah D5.1

## Slide 10: Straw Poll 1
  Do you agree to add the following text into 11ax SFD ?
  6.y.z All BSSs in a multiple BSSID set shall have the same BSS color.
  Y
  N
  A

## Slide 11: Straw Poll 2
  Do you agree to add the following text into 11ax SFD ?
  5.y.z AP and STAs in one BSS identified by a Multiple BSSID element shall consider a frame from another BSS identified by the same Multiple BSSID element as an intra-BSS frame.
  Y
  N
  A