## Slide 1: Flexible Wider Bandwidth Transmission
Date: 2016-01-18
Authors:

## Slide 2: Introduction
IEEE 802.11ac [1] allows wider bandwidth PPDU transmissions up to 160MHz with contiguous channel extension rule
  However, the probability of wider bandwidth PPDU transmission is low in dense environments from OBSS interferences in secondary channels
There has been several contributions [2~4] proposing more flexible wider bandwidth operations in 11ax
Also, 3GPP’s LAA(Licensed Assisted Access) recently specified channel access procedures for multiple channels in 5GHz band [5]
In this submission, we discuss several wider bandwidth PPDU transmission methods and discuss related issues

## Slide 3: HE PPDU bandwidth
3.2.4 HE-SIG-A
Field | Length (bits) | Description
... |  | 
Bandwidth | ≥ 2 | May accommodate more than in SU case to take advantage of OFDMA
... |  | 
Table 2 - HE-SIG-A field for an HE MU PPDU
Field | Length (bits) | Description
... |  | 
Bandwidth | TBD | 
... |  | 
Table 3 - HE-SIG-A field for the HE Trigger-based PPDU
4.4 MU RTS/CTS procedure
MU-RTS will carry signaling for each STA to indicate the 20 MHz channel(s) for transmitting CTS responses when CTS is sent in (duplicate) non-HT PPDU
The indicated 20 MHz channel(s) can be either Primary20, Primary40, Primary80 or 160/80+80 MHz. Other indications are TBD.
Current HE PPDU bandwidth definitions in 11ax SFD [6]
  For HE SU PPDU: 20/40/80/160(80+80) MHz
  For HE MU PPDU and HE Trigger-based PPDUs: Bandwidth options are TBD
  MU-RTS can indicate channels options for CTS other than P20, P40, P80, P160/80+80
Field | Length (bits) | Description
... |  | 
Bandwidth | 2 | 
... |  | 
Table 1 - HE-SIG-A field for an HE SU PPDU

## Slide 4: 11ac’s Wider Bandwidth Transmission
A STA wishes to send wider bandwidth PPDU performs multi-channel CCA
Then, if any Secondary channel (e.g. S20 MHz) is busy
  If the STA supports Static bandwidth operation
    Restart backoff procedure to perform multi-channel CCA again
    Therefore, the channel access is delayed
  If the STA supports Dynamic bandwidth operation
    Reconstruct PPDU instantly, transmit in smaller BW
    Therefore, the other idle secondary channel (e.g. S40 MHz) is not utilized
    Also the dynamic PPDU reconstruction is not widely implemented due to complexities
In this submission, we propose several (A) wider bandwidth transmission methods, and (B) a dynamic HE PPDU reconstruction method
P20MHz
S20MHz
yIFS
yIFS
AIFS
Busy
Dynamic PPDU reconstruction
3
2
1
20MHz PPDU
yIFS
AIFS
AIFS
3
2
1
Busy
PIFS
5
4
3
2
1
6
Delayed channel access
9
8
7
10
P20MHz
S20MHz
80MHz PPDU
(b) Dynamic bandwidth operation
(a) Static bandwidth operation
PIFS
PIFS
PIFS
PIFS
PIFS
PIFS
unutilized secondary channel
S40MHz
S40MHz

## Slide 5: (A) Wider Bandwidth Transmission Methods
Contiguous vs. Non-contiguous
  Contiguous: a PPDU is only constructed with contiguous span of channels
  Non-contiguous: a PPDU can be constructed with non-contiguous span of channels
Fixed (11ac) Extension vs. Flexible (20MHz) Extension
  Fixed (11ac) Extension: a PPDU is extended with S20/S40/S80MHz units only
  Flexible (20MHz) Extension: a PPDU can be extended with 20MHz unit
We compare the above three methods in terms of 1) Channel utilization, 2) 2nd CH CCA requirements, 3) HE-SIG-A overheads, and 4) HE-SIG-B overheads
PPDU
Busy
Method A
PPDU
Busy
Current 11ac
PPDU
PPDU
Busy
Method C
Busy
Primary
20MHz
Secondary
20MHz
Secondary
40MHz
PPDU
PPDU
Busy
Method B
Non-contiguous,
Fixed Extension
Contiguous,
Fixed Extension
Non-Contiguous,
Flexible Extension
Contiguous,
Flexible Extension

## Slide 6: 1. Channel utilization
Based on analysis of [2][4], we calculated average PPDU bandwidths according to various 20MHz CH busy probability (p)
Compared to the current 11ac operation, the proposed methods provided 10~28% and 22~95% higher channel utilizations in the max 80MHz and 160MHz PPDU sizes respectively
10.3%
17.9%
28.2%
21.9%
37.0%
94.9%

## Slide 7: 2. Secondary channel CCA requirements
11ax needs to define CCA procedures in secondary channels [7].
However, secondary channel CCA requirements of the methods are as follows
 | 11ac | Method A | Method B | Method C
Detect | Detect signals in Secondary 20, Secondary 40 and Secondary 80MHz channels |  | Detect signals in each non-primary 20MHz channels | 
Report | Report the first busy secondary channel | Report each channel’s busy/idle status | Report the first busy 20MHz channel | Report each 20MHz channel’s busy/idle status
Method A does not require new CCA mechanisms
Method B & C requires finer 20MHz-based CCA decisions in non-primary channels

## Slide 8: 3. HE-SIG-A overheads
A transmitting STA should indicate PPDU bandwidth early in SIG-A for receiving STA(s)
Considering insufficient bit spaces of HE-SIG-A in HE MU PPDU format, the PPDU BW subfield should be limited to max 3~4 bits
 | 11ac | Method A | Method B | Method C
# of PPDU BW options | 4 (20/40/80/160(80+80)) | 8 [see Appendix] | 18 [see Appendix] | 128 (busy/idle of 7 non-primary 20MHz CHs)
SIG-A BW (bits) | 2 bits | 3 bits | 5 bits | 7 bits

## Slide 9: 4. HE-SIG-B overheads
P20
(A)
S40
(C)
S40
(D)
S20
(B)
HE-SIG-B’s MU signaling information should be contained in both Primary & Secondary 20MHz channels
  If the secondary 20MHz is not utilized, the MU signaling should be transferred to the primary 20MHz channel
Method A & C imposes higher signaling overheads on primary channel having more PPDU BW options without Secondary 20MHz channel
L-Pre
SIG-A
SIG-B
(A,C,D)
Busy
P20+S40 case
Dup.
L-Pre
Dup.
SIG-A
Dup.
L-Pre
Dup.
SIG-A
Dup.
SIG-B
(A,C,D)
Dup.
SIG-B
(A,C,D)
MU
Data
HE-
STF
/LTF

## Slide 10: Comparisons
 |  | Cont., Fixed Ext. (11ac) | Method A. Non-Cont., Fixed Ext. | Method B. Cont., Flexible Ext. | Method C. Non-Cont., Flexible Ext.
Channel Utilization Gains | 80MHz | - | 10.3% | 17.9% | 28.2%
 | 160MHz | - | 21.9% | 37.0% | 94.9%
Secondary CH CCA |  | CCA per S20/S40/S80 CHs |  | CCA per non-primary 20MHz CHs | 
HE-SIG-A overheads | # of PPDU BWs | 4 | 4+4=8 | 4+14=18 | 4+124=128
 | BW subfield | 2 bits | 3 bits | 5 bits | 7 bits
HE-SIG-B overheads | Pri CH overheads (# of 20M to handle) | 2 | 3.125 | 2.44 | 3.25
Comparisons |  | - | Possible methods for 11ax |  | Too much overheads
Method A:
  Provides modest channel utilization gains without additional CCA requirements
  The increase in HE-SIG-B overheads would require higher MCS in HE-SIG-B
Method B:
  Provides higher channel utilization gains, but requires 20MHz based CCA requirements
Method C:
  Maximum channel utilization gains in all cases
  Requires 20MHz based CCA requirements, has the highest HE-SIG-A/B signaling overheads

## Slide 11: (B) Dynamic HE PPDU Reconstruction
S40MHz
In 11ac, dynamic PPDU reconstruction at transmit time is hard to be implemented
  A-MPDU should be reformed to meet TXOP/PPDU length limit with the narrow BW PPDU
Dynamic HE PPDU reconstruction procedure
  Prepare a HE PPDU with the intended wider bandwidth configuration
  Perform multi-channel CCA and identify busy channels
  Transmit HE PPDU in idle-sensed channels only
Dup.
L-Part
Dup.
HE-
SIG-A
HE-SIG-B
(A, C, D)
HE-
STF/LTF
Dup.
L-Part
Dup.
HE-
SIG-A
HE-SIG-B
(A, C, D)
L-Part
HE-
SIG-A
HE-SIG-B
(A, C, D)
Dup.
L-LTF
Dup.
HE-
SIG-A
HE-SIG-B
(C)
(D)
P20MHz
(A)
S20MHz
(B)
RU (C1)
RU (D1)
RU (A1)
...
...
...
RU (Cn)
RU(Dn)
RU (X)
RU (B1)
...
RU (Bn)
RU (An)
not transmitted
CCA
(idle)
CCA
(idle)
CCA
(busy)

## Slide 12: Summary
In 11ac, the chance to transmit wider bandwidth PPDU is low from OBSS interferences in secondary channels
We proposed wider bandwidth PPDU transmission methods and compared their advantages
  We propose that Method A & B should be considered as candidates for wider bandwidth transmission methods for 11ax
We also proposed the dynamic HE PPDU reconstruction to quickly adapt PPDU bandwidth according to CCA results

## Slide 13: Straw poll
Do you agree to add the following text into 11ax SFD?
  3.x.x The spec shall define HE PPDU bandwidth options other than 20/40/80/160(80+80)MHz for HE MU PPDU and HE Trigger-based PPDU formats.
  Y/N/A

## Slide 14: References
  [1] IEEE Std. 802.11ac-2013
  [2] 11-13/1058r0, Efficient Wider Bandwidth Operation
  [3] 11-13/0839r1, Discussion on OFDMA in IEEE 802.11ax
  [4] 11-15/0353r1, OFDMA Non-contiguous Channel Utilization
  [5] “15.1.5 Channel access procedure for transmission(s) on multiple channels” in 3GPP TS 36.213 V13.0.0 (2015-12) http://www.3gpp.org/ftp/specs/archive/36_series/36.213/
  [6] 11-15/0132r13, Spec Framework Doc
  [7] 11-15/1337r1, Secondary Channel CCA of HE STA

## Slide 15: Ref: PPDU BW cases
Method B:
Contiguous,
Flexible Ext.
P20
MHz
S20
MHz
S40
MHz
S80
MHz
P40
S80A
S80B
S80C
S40B
P160
P80
S80A
S80B
S80C
P80
S80A
S80B
P80
S80A
P80
P20
S40
P20
S40B
P40
S80
S40B
P40
S40B
P40
S40B
S80A
P40
S80A
S80B
S40B
P20
P40
S80A
S80B
S80C
P40
P40
S80A
P40
S80A
S80B
P40
S80
P20
MHz
S20
MHz
S40
MHz
S80
MHz
P160
P80
P20
S40
P20
P40
P40
S80
P20
S40
S80
P20
S80
Method A:
Non-Contig.,
Fixed Ext.